## Slide 1: Fundamentals of Control Theory
Acknowledgment: Joseph Hellerstein, Sujay Parekh, Chenyang Lu
Hongwei Zhang
hongwei@iastate.edu, 515 294 2143
http://www.ece.iastate.edu/~hongwei

## Slide 2: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 3: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 4: Example 1: Liquid Level System
Input valve control
float
Output
valve
Goal: Design the input valve control to maintain a constant height regardless of the setting of the output valve
(height)
(input flow)
(output flow)
(volume)
(resistance)
Notes: This can be applied to computer systems as a fluid model of queues: inflow is in work/sec; volume represents work in system; R relates to service rate.

## Slide 5: Example 2: Admission Control
Users
Administrator
Controller
RPCs
Sensor
Server
Reference
value
Queue
Length
Tuning
control
Server
Log
Goal: Design the controller to maintain a constant queue length regardless of the workload
Notes: Jlh: May want a slide that explains how this controller works?

## Slide 6: Open-loop control
Compute control input without continuous variable measurement
  Simple
  Need to know EVERYTHING ACCURATELY to work right
    Cruise-control car: friction(t), ramp_angle(t)
    E-commerce server: Workload (request arrival rate? resource consumption?); system (service time? failures?)
Open-loop control fails when
  We don’t know everything
  We make errors in estimation/modeling
  Things change
Notes: Open-loop: Non adaptive system
Close-loop: Adaptive system
Feedback control is Everywhere. Aircrafts, cruise control, chemical processes, even economics …

## Slide 7: Feedback (closed-loop) Control
Actuator
Monitor
reference
control
input
controlled
variable
manipulated
variable
Controlled System
+
-
error
control
function
Controller
sample

## Slide 8
Measure variables and use it to compute control input
  More complicated (so we need control theory)
  Continuously measure & correct
    Cruise-control car: measure speed & change engine force
    E-commerce server: measure response time & admission control
    Embedded network: measure collision & change scheduling
Feedback control theory makes it possible to control well even if
  We don’t know everything
  We make errors in estimation/modeling
  Things change
Notes: Open-loop: Non adaptive system
Close-loop: Adaptive system
Feedback control is Everywhere. Aircrafts, cruise control, chemical processes, even economics …

## Slide 9: Why feedback control in computing? Open, unpredictable environments
Deeply embedded networks: interaction with physical environments
  Number of working nodes
  Number of interesting events
  Number of hops
  Connectivity
  Available bandwidth
  Congested area
Internet: E-business, on-line stock broker
Unpredictable off-the-shelf hardware
Notes: Performance control becomes harder and harder!

## Slide 10: Why feedback control in computing? We want QoS guarantees
Deeply embedded networks
  Report/share vehicle locations every 100ms
  Update intruder position every 30sec
  Report fire <= 1min
E-business server
  Purchase completion time <= 5 sec
  Throughput >= 1000 transaction/sec
The challenge:
provide QoS guarantees in open, unpredictable environments
Notes: Performance control becomes harder and harder!

## Slide 11: Advantages of feedback control theory
Systematic approach to analysis and design
  Transient response
  Consider sampling times, control frequency
  Taxonomy of basic controls;
  Select controller based on desired characteristics
Predict system response to some input
  Speed of response (e.g., adjust to workload changes)
  Oscillations (variability)
Approaches to assessing stability and limit cycles

## Slide 12
In comparison
  Adaptive resource management heuristics
    Laborious design/tuning/testing iterations
    Not enough confidence in face of untested workload
  Queuing theory
    Doesn’t handle feedbacks
    Not good at characterizing transient behavior in overload

## Slide 13: Example: Control & Response in an Email Server
Control
(MaxUsers)
Response
(queue length)
Good
Slow
Bad
Useless
Notes: Explain the organization of the figure and how this relates to the Lotus Notes example. Justify having target queue lengths. Explain the reference values.

## Slide 14: Examples of applying control theory in computing systems
Network flow controllers (TCP/IP – RED)
  C. Hollot et al. (U.Mass)
Lotus Notes admission control
  S. Parekh et al. (IBM)
QoS in Caching, Apache QoS differentiation
  C. Lu et al. (U.Va)
Predictable interference control in wireless
  H. Zhang et al. (ISU)

## Slide 15: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 16: Feedback Control System
Plant
Controller
S
Disturbance
Transducer/Sensor
+
–
Reference Value
Notes: Examples of transducers in computer systems are mainly surrogate variables. For example, we may not be able to measure end-user response times. However, we can measure internal system queueing. So we use the latter as a surrogate for the former and sometimes use simple equations (e.g., Little’s result) to convert between the two.
Jlh: Be careful here since Little’s result only applies to steady state, not transients.
Another aspect of the transducer are the delays it introduces. Typically, measurements are sampled. The sample rate cannot be too fast if the performance of the plant (e.g., database server) is slower.

## Slide 17: Controller Design Methodology
Block diagram construction
Model Ok?
Stop
Start
Transfer function formulation and validation
Controller Design
Objective achieved?
Controller Evaluation
Y
Y
N
N
System Modeling

## Slide 18: Control System Goals
Regulation
  thermostat, target service levels
Tracking
  robot movement, adjust TCP window to network bandwidth
Optimization
  best mix of chemicals, minimize response times

## Slide 19: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 20: System Models
Linear vs. non-linear
  Principle of superposition: for linear systems, the net response at a given place and time caused by two or more stimuli is the sum of the responses which would have been caused by each stimulus individually.
Deterministic vs. Stochastic
Time-invariant vs. Time-varying
  Are coefficients functions of time?
Continuous-time vs. Discrete-time
  t Î R vs. k Î Z
Notes: Stochastic control is a subfield of control theory which deals with the existence of uncertainty in the data. The designer assumes, in a Bayesian probability-driven fashion, that a random noise with known probability distribution affects the state evolution and the observation of the controllers. Stochastic control aims to design the optimal controller that performs the desired control task with minimum average cost despite the presence of these noises.[1]
An extremely well studied formulation in stochastic control is that of linear-quadratic-Gaussian problem. Here the model is linear, and the objective function is the expected value of a quadratic form, and the additive disturbances are distributed in a Gaussian manner. A basic result for discrete time centralized systems is the certainty equivalence property:[2] that the optimal control solution in this case is the same as would be obtained in the absence of the additive disturbances. This property is applicable to all systems that are merely linear and quadratic (LQ), and the Gaussian assumption allows for the optimal control laws, that are based on the certainty-equivalence property, to be linear functions of the observations of the controllers.
This property fails to hold for decentralized control, as was demonstrated by Witsenhausen in the celebrated Witsenhausen's counterexample.
Any deviation from the above assumptions—a nonlinear state equation, a non-quadratic objective function, or noise in the multiplicative parameters of the model—would cause the certainty equivalence property not to hold. In the discrete-time case with uncertainty about the parameter values in the transition matrix and/or the control response matrix of the state equation, but still with a linear state equation and quadratic objective function, a matrix Riccati equation can still be obtained for iterating to each period's solution.[3][2]ch.13 The discrete-time case of a non-quadratic loss function but only additive disturbances can also be handled, albeit with more complications.[4]
Linear systems satisfy the properties of superposition and scaling
Typical differential equations of linear time-invariant systems are well adapted to analysis using the Laplace transform in the continuous case, and the Z-transform in the discrete case (especially in computer implementations).
Another perspective is that solutions to linear systems comprise a system of functions which act like vectors in the geometric sense.
A common use of linear models is to describe a nonlinear system by linearization. This is usually done for mathematical convenience.

## Slide 21: Approaches to System Modeling
First Principles
  Based on known laws
    Physics, Queueing theory
  Difficult to do for complex systems
Experimental (System ID)
  Statistical/data-driven models
  Requires data
  Is there a good “training set”?

## Slide 22: The Complex Plane (review)
Imaginary axis (j)
Real axis
(complex) conjugate
argument of u
modulus or absolute value of u
Notes: In mathematics, the complex plane or z-plane is a geometric representation of the complex numbers established by the real axis and the orthogonal imaginary axis. It can be thought of as a modified Cartesian plane, with the real part of a complex number represented by a displacement along the x-axis, and the imaginary part by a displacement along the y-axis.[1]
The complex plane is sometimes called the Argand plane because it is used in Argand diagrams. These are named after Jean-Robert Argand (1768-1822), although they were first described by Norwegian-Danish land surveyor and mathematician Caspar Wessel (1745-1818).[2] Argand diagrams are frequently used to plot the positions of the poles and zeroes of a function in the complex plane.
The concept of the complex plane allows a geometric interpretation of complex numbers. Under addition, they add like vectors. The multiplication of two complex numbers can be expressed most easily in polar coordinates – the magnitude or modulus of the product is the product of the two absolute values, or moduli, and the angle or argument of the product is the sum of the two angles, or arguments. In particular, multiplication by a complex number of modulus 1 acts as a rotation.
A complex number, in mathematics, is a number comprising a real number and an imaginary number; it can be written in the form a + bi, where a and b are real numbers, and i is the standard imaginary unit, having the property that i2 = −1.[1] The complex numbers contain the ordinary real numbers, but extend them by adding in extra numbers and correspondingly expanding the understanding of addition and multiplication. This is in order to form a closed field, where any polynomial equation has a root, including examples such as x2 = −1.
Complex numbers were first conceived and defined by the Italian mathematician Gerolamo Cardano, who called them "fictitious", during his attempts to find solutions to cubic equations.[2] The solution of a general cubic equation may require intermediate calculations containing the square roots of negative numbers, even when the final solutions are real numbers, a situation known as casus irreducibilis. This ultimately led to the fundamental theorem of algebra, which shows that with complex numbers, a solution exists to every polynomial equation of degree one or higher.
The rules for addition, subtraction, multiplication, and division of complex numbers were developed by the Italian mathematician Rafael Bombelli.[3] A more abstract formalism for the complex numbers was further developed by the Irish mathematician William Rowan Hamilton, who extended this abstraction to the theory of quaternions.
Complex numbers are used in a number of fields, including: engineering, electromagnetism, quantum physics, applied mathematics, and chaos theory. When the underlying field of numbers for a mathematical construct is the field of complex numbers, the name usually reflects that fact. Examples are complex analysis, complex matrix, complex polynomial, and complex Lie algebra.

## Slide 23: Basic Tool For Continuous Time: Laplace Transform
Convert time-domain functions and operations into frequency-domain
  f(t) ® F(s)
  Linear differential equations (LDE) ® algebraic expression in Complex plane
Graphical solution for key LDE characteristics
Discrete systems use the analogous z-transform
Notes: Jlh: First red bullet needs to be fixed?

## Slide 24: Laplace Transforms of Common Functions
Name
f(t)
F(s)
Impulse
Step
Ramp
Exponential
Sine
1
Notes: Jlh: function for impulse needs to be fixed

## Slide 25: Properties of Laplace Transform

## Slide 26: Insights from Laplace Transforms
What does the Laplace Transform say about f(t)?
  Value of f(0)
    Initial value theorem
  Value of f(t) at steady state (if it converges)
    Final-value theorem
  Does f(t) converge to a finite value
    Poles of F(s): whether negative (why?)
  Does f(t) oscillate?
    Poles of F(s): whether the imaginary part is 0

## Slide 27: Digital/Discrete Control
More useful for computer systems
Time is discrete
  denoted k instead of t, in general
Main tool is z-transform
  f(k) ® F(z) , where z is complex
  Analogous to Laplace transform for s-domain
Notes: Root-locus analysis has similar flavor (discussed later)
Root-locus analysis has similar flavor (discussed later)
  Insights are slightly different

## Slide 28: z-Transforms of Common Functions
Name
f(t)
F(z)
Impulse
Step
Ramp
Exponential
Sine
1
F(s)
1

## Slide 29: Properties of z-Transforms

## Slide 30: Z-Transform: Final Value Theorem
Z-Transform provides a convenient way to determine the steady state value of a signal, if one exists (i.e., poles within unit circle)
  If poles within unit circle but is negative, signal will oscillate as it converges to a limit
Example:
Notes: Why should the poles lie in the unit circle if we’re talking about a “final value”?

## Slide 31: Transfer Function
Definition
  H(s) = Y(s) / X(s)
Relates the output of a linear system (or component) to its input
Describes how a linear system responds to an impulse (where X(s)=1)
All linear operations allowed
  Scaling, addition, multiplication
H(s)
X(s)
Y(s)

## Slide 32: Block Diagrams
Pictorially expresses flows and relationships between elements in system
Blocks may recursively be systems
Rules
  Cascaded elements: convolution
  Summation and difference elements
Notes: Can simplify

## Slide 33: Block Diagram of System
Plant
Controller
S
Disturbance
Transducer
+
–
S
Reference Value

## Slide 34: Combining Blocks
Combined Block
S
Transducer
+
–
Reference Value

## Slide 35: Block Diagram of Access Control
M(z)
G(z)
N(z)
S(z)
Controller
Notes
Server
Sensor
R(z)
+
E(z)
U(z)
-
Q(z)
S
Users
Controller
Sensor
Server
Server
Log
Notes: Jlh: Can we make the diagram bigger and the title smaller?

## Slide 36: Key Transfer Functions
Plant
Controller
S
Transducer
+
–
Reference
Closed-Loop/

## Slide 37: What can we do with Transfer Functions?
Predict output for a given input (e.g., impulse)
Predict Stability of system
  Unstable systems are highly undesirable
Calculate steady-state gain
  Compute operating ranges, state space reachability
Use it as a basis for lowering system order
  Lower-order systems are easier to work with
Compose TFs to build/study complex systems (block diagram)
Easily simulate the system behavior

## Slide 38: Rational Laplace Transforms
Notes: Jlh: Need to give insights into why poles and zeroes are important. Otherwise, the audience will be overwhelmed.

## Slide 39: Bounded Signals
Which of these outputs are undesirable?
Lets Formalize this…
Definition:
  {u(k)} is bounded if there exists a constant M such that |u(k)| ≤ M for all k.
Notes: Intuitively, stable system should have a “reasonable” output behavior.

## Slide 40: BIBO Stability
NOTE: Bad reaction to unbounded inputs is OK?!
Are these systems BIBO stable?
Definition:
A system is BIBO stable if for any bounded input {u(k)}, its output {y(k)} is bounded.
Unity | y(k+1) = 1
P Controller | y(k+1) = KP u(k)
Integrator | y(k+1) = y(k) + u(k)
I Controller | y(k+1) = y(k) + KI u(k)
M/M/1/K | y(k+1) = 0.49y(k) + 0.033u(k)
Mystery | y(k+1) = -1.3y(k) + 2.3u(k)
There must be a better way…
Notes: It is tedious to figure out whether or not something is BIBO stable from its time-domain eqn… leads to next slide.

## Slide 41: BIBO Stability Theorem
Theorem:
A system G(z) is BIBO stable iff all the poles of G(z) are inside the unit circle.
System | Time domain Eq | Transfer Function | Poles
Unity | y(k+1) = 1 | G(z) = 1 | N/A
P Controller | y(k+1) = KP u(k) | G(z) = KP | N/A
Integrator | y(k+1) = y(k) + u(k) | G(z) = 1/(z-1) | z=1
I Controller | y(k+1) = y(k) + KI u(k) | G(z) = KI/(z-1) | z=1
M/M/1/K | y(k+1) = 0.49y(k) + 0.033u(k) | G(z) = 0.033/(z-0.49) | z = 0.49
Mystery | y(k+1) = -1.3y(k) + 2.3u(k) | G(z) = 2.3/(z+1.3) | z = -1.3

## Slide 42: Steady-state Gain
G(z) can be used to characterize steady-state reaction of system
  Reaction to a constant input
Given
  BIBO stable system G(z)
  Apply step input U(z)
NOTE
  Output MUST converge
Definition: Steady-state Gain (aka DC Gain)

## Slide 43: Steady-state Gain Theorem
Theorem: Steady state gain of a system G(z) is given by G(1)
Proof
  System response to a unit step (ie uss=1) is given by
  Applying final-value theorem to get yss
For a general ARX transfer function, steady-state gain is

## Slide 44: System Order
System order = # poles
  Same as m in ARX formula
  Same as # initial conditions needed to seed the difference equation
Why does it matter?
  “Complexity” of system response proportional to system order
  Higher (¸ 2nd) order systems have complex poles
    Implies oscillatory factors in system response
  More difficult to design/analyze higher-order systems

## Slide 45: First Order System
Reference
S
1
Notes: K is usually small for proportional controllers.
Examples of transducers in computer systems are mainly surrogate variables. For example, we may not be able to measure end-user response times. However, we can measure internal system queueing. So we use the latter as a surrogate for the former and sometimes use simple equations (e.g., Little’s result) to convert between the two.
Use the approximation to simplify the following analysis
Another aspect of the transducer are the delays it introduces. Typically, measurements are sampled. The sample rate cannot be too fast if the performance of the plant (e.g., database server) is

## Slide 46
Impulse response |  | Exponential
Step response |  | Step, exponential
Ramp response |  | Ramp, step, exponential
No oscillations (as seen by poles)

## Slide 47: Second Order System
Notes: See pages 112-113 of “Feedback control of dynamic systems”.
Zeta
Get oscillatory response if have poles that have non-zero Im values.

## Slide 48
Notes: Get oscillatory response if have poles that have non-zero Im values.
In engineering, the damping ratio is a measure of describing how oscillations in a system die down after a disturbance. Many systems exhibit oscillatory behavior when they are disturbed from their position of static equilibrium. A mass suspended from a spring, for example, will, if pulled and released, bounce up and down. On each bounce, the system is trying to return to its equilibrium position, but overshoots it. Frictional losses damp the system and cause the oscillations to gradually decay in amplitude towards zero. The damping ratio is a measure of describing how rapidly the oscillations decay from one bounce to the next.

## Slide 49
Notes: The radian is a unit of plane angle, equal to 180/π (or 360/2π) degrees, or about 57.2958 degrees, or about 57°17′45″. It is the standard unit of angular measurement in all areas of mathematics beyond the elementary level.

## Slide 50: Simulating Transfer Functions
For complex transfer functions, cannot analyze
  Solution: Simulate
  Observation:
  Inputs
    Initial conditions (depends on system order)
    u(k)

## Slide 51: Transfer Functions: Summary
Transfer Functions are expressed as polynomials in z
We can predict BIBO stability from the poles of a TF
We can calculate steady-state gain from a TF
We can build simplified TF from a high-order TF that has similar steady-state gain and settling time (see Chapter 6 of [1])
It is usually easy to convert a difference eq to a TF
  Can usually plug into the general ARX form
One can simulate a TF by converting back to difference equation

## Slide 52: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 53: Objectives of Control for Computing Systems: SASO
Stability
Accuracy
Settling time
Overshoot
Notes: The stability of a general dynamical system with no input can be described with Lyapunov stability criteria.
A linear system is called bounded-input bounded-output (BIBO) stable if its output will stay bounded for any bounded input.
Stability for nonlinear systems that take an input is input-to-state stability (ISS), which combines Lyapunov stability and a notion similar to BIBO stability.
For simplicity, the following descriptions focus on continuous-time and discrete-time linear systems.
Mathematically, this means that for a causal linear system to be stable all of the poles of its transfer function must have negative-real values, i.e. the real part of each pole must be less than zero. Practically speaking, stability requires that the transfer function complex poles reside
in the open left half of the complex plane for continuous time, when the Laplace transform is used to obtain the transfer function.
inside the unit circle for discrete time, when the Z-transform is used.

## Slide 54: Characteristics of Transient Response
Settling time
Overshoot
Controlled
variable
Time
%
Steady State
Transient State
Steady state error
Reference
Rise time

## Slide 55: Transient Response
Estimates the shape of the curve based on the foregoing points on the x and y axis
Typically applied to the following inputs
  Impulse
  Step
  Ramp
  Quadratic (Parabola)

## Slide 56: Effect of pole locations: continuous time
Faster Decay
Faster Blowup
Oscillations
(higher-freq)
Im(s)
Re(s)
(e-at)
(eat)

## Slide 57: Root-Locus Analysis
Based on characteristic equation of closed-loop transfer function
Plot location of roots of this equation
  Same as poles of closed-loop transfer function
  Parameter (gain) varied from 0 to 
Multiple parameters are ok
  Vary one-by-one
  Plot a root “contour” (usually for 2-3 parameters)
Quickly get approximate results
  Range of parameters that gives desired response
Notes: characteristic eqn: denominator of transfer function = 0
https://en.wikipedia.org/wiki/Root_locus

## Slide 58: Root Locus analysis of Discrete Systems
Stability boundary: |z|=1 (Unit circle)
Settling time: distance from Origin
Oscillation frequency: location relative to Im. axis
  Right half => slower
  Left half => faster
Notes: Jlh: Can this be combined with the picture on the next page?

## Slide 59: Effect of discrete poles
|z|=1
Longer settling time
Re(s)
Im(s)
Unstable
Stable
Higher-frequency
response

## Slide 60: Admission Control for Lotus Notes Server
M(z)
G(z)
N(z)
S(z)
Controller
Notes
Server
Sensor
R(z)
+
E(z)
U(z)
-
Q(z)
S
ARMA Models
Control Law
Transfer Functions
Open-Loop:

## Slide 61: Root Locus Analysis of Admission Control
Predictions:
Ki small => No controller-induced oscillations
Ki large => Some oscillations
Ki v. large => unstable system (when delay=2)
Usable range of Ki for delay=2 is small

## Slide 62: Experimental Results
Control
(MaxUsers)
Response
(queue length)
Good
Slow
Bad
Useless

## Slide 63: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 64: Basic Control Actions: u(t)
Notes: Jlh: Can we give more intuition on control actions. This seems real brief considering its importance.

## Slide 65: Effect of Control Actions
Proportional Action
  Adjustable gain (amplifier)
  May have non-zero steady-state error
Integral Action
  Eliminates bias (steady-state error)
  Can cause oscillations
Derivative Action (“rate control”)
  Effective in transient periods
  Provides faster response (higher sensitivity)
  Never used alone

## Slide 66: Basic Controllers
Proportional control is often used by itself
Integral and differential control are typically used in combination with at least proportional control
  eg, Proportional Integral (PI) controller:

## Slide 67: Summary of Basic Control
Proportional control
  Multiply e(t) by a constant
PI control
  Multiply e(t) and its integral by separate constants
  Avoids bias for step
PD control
  Multiply e(t) and its derivative by separate constants
  Adjust more rapidly to changes
PID control
  Multiply e(t), its derivative and its integral by separate constants
  Reduce bias and react quickly

## Slide 68: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 69: Advanced Control Topics
MIMO Control
  Multiple inputs and/or outputs
Robust Control
  Can the system tolerate noise?
Adaptive Control
  Controller changes over time (adapts)
Stochastic Control
  Controller minimizes variance
Optimal Control
  Controller minimizes a cost function (e.g., function of error)
Nonlinear systems
  Challenging to derive analytic results
Notes: Stochastic control is a subfield of control theory which addresses the design of a control methodology to address the probability of uncertainty in the data. In a stochastic control problem, the designer assumes that random noise and disturbances exist in the model and in the controller, and the control design must take into account these random deviations.[1]
Stochastic control aims to predict and to minimize the effects of these random deviations, by optimizing the design of the controller.[
Optimal Control
  Controller minimizes a cost function of error and control energy
Nonlinear systems
  Neuro-fuzzy control
  Challenging to derive analytic results
A fuzzy control system is a control system based on fuzzy logic - a mathematical system that analyzes analog input values in terms of logical variables that take on continuous values between 0 and 1, in contrast to classical or digital logic, which operates on discrete values of either 0 and 1 (true and false).

## Slide 70: Outline
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 71: Issues for Computer Science
Most systems are non-linear
  But linear approximations may do
    E.g., fluid approximations
First-principle modeling is difficult
  Use empirical techniques
Control objectives are different
  Optimization rather than regulation
Multiple Controls
  State-space techniques
  Advanced non-linear techniques (e.g., neural networks)
Notes: https://www.uni-obuda.hu/journal/Zilkova_Timko_Girovsky_8.pdf

## Slide 72: Summary
Examples and Motivation
Control Theory Vocabulary and Methodology
Modeling Dynamic Systems
Transient Behavior Analysis
Standard Control Actions
Advanced Topics
Issues for Computer Systems

## Slide 73: References
Control Theory Basics
  [1] Joseph L. Hellerstein, Yixin Diao, Sujay Parekh, Dawn M. Tilbury, Feedback Control of Computing Systems, Wiley-IEEE Press, 2004. (ISBN: 978-0-471-26637-2)
  [2] G. Franklin, J. Powell and A. Emami-Naeini. “Feedback Control of Dynamic Systems, 3rd ed”. Addison-Wesley, 1994.
  [3] K. Ogata. “Modern Control Engineering, 3rd ed”. Prentice-Hall, 1997.
  [4] K. Ogata. “Discrete-Time Control Systems, 2nd ed”. Prentice-Hall, 1995.
Applications in Computer Science
  C. Hollot et al. “Control-Theoretic Analysis of RED”. IEEE Infocom 2001
  C. Lu, et al. “A Feedback Control Approach for Guaranteeing Relative Delays in Web Servers”. IEEE Real-Time Technology and Applications Symposium, June 2001.
  S. Parekh et al. “Using Control Theory to Achieve Service-level Objectives in Performance Management”. Int’l Symposium on Integrated Network Management, May 2001
  Y. Lu et al. “Differentiated Caching Services: A Control-Theoretic Approach”. Int’l Conf on Distributed Computing Systems, Apr 2001
  S. Mascolo. “Classical Control Theory for Congestion Avoidance in High-speed Internet”. Proc. 38th Conference on Decision & Control, Dec 1999
  S. Keshav. “A Control-Theoretic Approach to Flow Control”. Proc. ACM SIGCOMM, Sep 1991
  D. Chiu and R. Jain. “Analysis of the Increase and Decrease Algorithms for Congestion Avoidance in Computer Networks”. Computer Networks and ISDN Systems, 17(1), Jun 1989

## Slide 74: Assignment
Module 2 Quiz-B
  Fundamentals of Real-Time Scheduling
  Fundamentals of Control Theory