## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2: Counters & Solved Problems
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © 2013

## Slide 3: Administrative Stuff
Homework 8 is due on Monday @ 4pm
Homework 9 will be due on Monday Oct 26 @ 4pm

## Slide 4
Counters

## Slide 5
[ Figure 5.15a,c from the textbook ]
T Flip-Flop (circuit and graphical symbol)

## Slide 6
T
D
Q
Q
Clock
Yet Another Way to Draw a T Flip-Flop

## Slide 7
The Complete Wiring Diagram for
a Positive-Edge-Triggered D Flip-Flop
D
Clock
Q
Q

## Slide 8
The Complete Wiring Diagram for
a Positive-Edge-Triggered D Flip-Flop
D
Clock
Q
Q
We need all of this just to store 1 bit!

## Slide 9
The Complete Wiring Diagram for
a Positive-Edge-Triggered T Flip-Flop
T
Clock
Q
Q

## Slide 10
The output of the T Flip-Flop divides the frequency of the clock by 2

## Slide 11
The output of the T Flip-Flop divides the frequency of the clock by 2
1

## Slide 12
A three-bit down-counter
[ Figure 5.20 from the textbook ]

## Slide 13
A three-bit down-counter
[ Figure 5.20 from the textbook ]
The first flip-flop changes
on the positive edge of the clock

## Slide 14
A three-bit down-counter
[ Figure 5.20 from the textbook ]
The first flip-flop changes
on the positive edge of the clock
The second flip-flop changes
on the positive edge of Q0

## Slide 15
A three-bit down-counter
[ Figure 5.20 from the textbook ]
The first flip-flop changes
on the positive edge of the clock
The second flip-flop changes
on the positive edge of Q0
The third flip-flop changes
on the positive edge of Q1

## Slide 16
A three-bit down-counter
[ Figure 5.20 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram

## Slide 17
A three-bit down-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
least
significant
most
significant

## Slide 18
A three-bit down-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram
Q0 toggles
on the positive
clock edge

## Slide 19
A three-bit down-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram
Q1 toggles
on the positive
edge of Q0

## Slide 20
A three-bit down-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram
Q2 toggles
on the positive
edge of Q1

## Slide 21
A three-bit down-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
7
6
5
4
3
2
1
0
(b) Timing diagram
The propagation delays get longer

## Slide 22
A three-bit up-counter
[ Figure 5.19 from the textbook ]

## Slide 23
A three-bit up-counter
[ Figure 5.19 from the textbook ]
The first flip-flop changes
on the positive edge of the clock

## Slide 24
A three-bit up-counter
[ Figure 5.19 from the textbook ]
The first flip-flop changes
on the positive edge of the clock
The second flip-flop changes
on the positive edge of Q0

## Slide 25
A three-bit up-counter
[ Figure 5.19 from the textbook ]
The first flip-flop changes
on the positive edge of the clock
The second flip-flop changes
on the positive edge of Q0
The third flip-flop changes
on the positive edge of Q1

## Slide 26
A three-bit up-counter
[ Figure 5.19 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
1
2
3
4
5
6
7
0
(b) Timing diagram

## Slide 27
A three-bit up-counter
[ Figure 5.19 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
1
2
3
4
5
6
7
0
(b) Timing diagram
least
significant
most
significant
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
1
1
0
0
0

## Slide 28
A three-bit up-counter
[ Figure 5.19 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
(b) Timing diagram
The count
is formed
by the Q’s

## Slide 29
A three-bit up-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
(b) Timing diagram
Q
0
Q
1
Q
2
The toggling
is done
by the Q’s

## Slide 30
A three-bit up-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
(b) Timing diagram
Q
0
Q
1
Q
2
Q0 toggles
on the positive
clock edge

## Slide 31
A three-bit up-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
(b) Timing diagram
Q
0
Q
1
Q
2
Q1 toggles
on the positive
Edge of Q0

## Slide 32
A three-bit up-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
(b) Timing diagram
Q
0
Q
1
Q
2
Q2 toggles
on the positive
edge of Q1

## Slide 33
A three-bit up-counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
(b) Timing diagram
Q
0
Q
1
Q
2
The propagation delays get longer

## Slide 34
A three-bit up-counter
[ Figure 5.19 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
1
2
3
4
5
6
7
0
(b) Timing diagram
The propagation delays get longer

## Slide 35
Synchronous Counters

## Slide 36
A four-bit synchronous up-counter
[ Figure 5.21 from the textbook ]

## Slide 37
A four-bit synchronous up-counter
[ Figure 5.21 from the textbook ]
The propagation delay through all AND gates combined must
not exceed the clock period minus the setup time for the flip-flops

## Slide 38
A four-bit synchronous up-counter
[ Figure 5.21 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
0
1
2
3
5
9
12
14
0
(b) Timing diagram
T
Q
Q
Q
3
Q
3
4
6
8
7
10
11
13
15
1

## Slide 39
Derivation of the synchronous up-counter
[ Table 5.1 from the textbook ]
0
0
1
1
0
1
0
1
0
1
2
3
0
0
1
0
1
0
4
5
6
1
1
7
0
0
0
0
1
1
1
1
Clock cycle
0
0
8
0
Q
2
Q
1
Q
0
Q
1
changes
Q
2
changes

## Slide 40
Derivation of the synchronous up-counter
[ Table 5.1 from the textbook ]
0
0
1
1
0
1
0
1
0
1
2
3
0
0
1
0
1
0
4
5
6
1
1
7
0
0
0
0
1
1
1
1
Clock cycle
0
0
8
0
Q
2
Q
1
Q
0
Q
1
changes
Q
2
changes
T0= 1
T1 = Q0
T2 = Q0 Q1

## Slide 41
A four-bit synchronous up-counter
[ Figure 5.21 from the textbook ]
T0= 1
T1 = Q0
T2 = Q0 Q1

## Slide 42
In general we have
T0= 1
T1 = Q0
T2 = Q0 Q1
T3 = Q0 Q1 Q2
…
Tn = Q0 Q1 Q2 …Qn-1

## Slide 43
Synchronous v.s. Asynchronous Clear

## Slide 44
2-Bit Synchronous Up-Counter
(without clear capability)
1
T
Q
Q
Clock
T
Q
Q
Q0
Q1

## Slide 45
2-Bit Synchronous Up-Counter
(with asynchronous clear)
1
T
Q
Q
Clock
T
Q
Q
Clear_n
Q0
Q1

## Slide 46
2-Bit Synchronous Up-Counter
(with asynchronous clear)
1
D
Q
Q
Clock
D
Q
Q
Clear_n
Q0
Q1
This is the same circuit but uses D Flip-Flops.

## Slide 47
2-Bit Synchronous Up-Counter
(with synchronous clear)
1
D
Q
Q
Clock
D
Q
Q
Clear_n
Q0
Q1
This counter can be cleared only on the positive clock edge.

## Slide 48
Adding Enable Capability

## Slide 49
A four-bit synchronous up-counter
[ Figure 5.21 from the textbook ]

## Slide 50
Inclusion of Enable and Clear Capability
[ Figure 5.22 from the textbook ]
T
Q
Q
Clock
T
Q
Q
Enable
Clear_n
T
Q
Q
T
Q
Q

## Slide 51
Inclusion of Enable and Clear Capability
[ Figure 5.22 from the textbook ]
T
Q
Q
Clock
T
Q
Q
Enable
Clear_n
T
Q
Q
T
Q
Q
This is the new thing relative to
the previous figure, plus the clear_n line

## Slide 52
[ Figure 5.56 from the textbook ]
Providing an enable input for a D flip-flop

## Slide 53
Synchronous Counter
(with D Flip-Flops)

## Slide 54
A 4-bit up-counter with D flip-flops
[ Figure 5.23 from the textbook ]

## Slide 55
A 4-bit up-counter with D flip-flops
[ Figure 5.23 from the textbook ]
T flip-flop
T flip-flop
T flip-flop
T flip-flop

## Slide 56
Equivalent to this circuit with T flip-flops
T
Q
Q
Clock
T
Q
Q
Enable
T
Q
Q
T
Q
Q

## Slide 57
Equivalent to this circuit with T flip-flops
T
Q
Q
Clock
T
Q
Q
Enable
T
Q
Q
T
Q
Q
Z
But has one extra output called Z, which can be used to
connect two 4-bit counters to make an 8-bit counter.
When Z=1 the counter will go 0000 on the next clock edge, i.e.,
the outputs of all flip-flops are currently 1 (maximum count value).

## Slide 58: Faster 4-bit Counter
Want to increase the speed of the 4-bit counter?
Use a similar method as the one used in 4-bit adder.
Replace the series of 2-input AND gates with AND gates with more input lines.

## Slide 59
Is it possible to reduce this delay?
T
Q
Q
Clock
T
Q
Q
Enable
T
Q
Q
T
Q
Q

## Slide 60
Equivalent 4-bit counter
[ Figure 5.67 from the textbook ]

## Slide 61
A faster 4-bit counter
[ Figure 5.75 from the textbook ]

## Slide 62
Counters with Parallel Load

## Slide 63
A counter with parallel-load capability
[ Figure 5.24 from the textbook ]

## Slide 64
How to load the initial count value
1
0
1
0
Set the initial count on
the parallel load lines
(in this case 5).

## Slide 65
How to zero a counter
1
1
0
1
0
1
0
1
0
Set "Load" to 1, to open the
"1" line of the multiplexers.

## Slide 66
How to zero a counter
1
1
0
1
0
1
0
1
0
1
0
1
0
When the next positive edge of
the clock arrives, the outputs
of the flip-flops are updated.

## Slide 67
Reset Synchronization

## Slide 68: Motivation
An n-bit counter counts from 0, 1, …, 2n-1
For example a 3-bit counter counts up as follow
  0, 1, 2, 3, 4, 5, 6, 7, 0, 1, 2, …
What if we want it to count like this
  0, 1, 2, 3, 4, 5, 0, 1, 2, 3, 4, 5, 0, 1, …
In other words, what is the cycle is not a power of 2?

## Slide 69
What does this circuit do?
[ Figure 5.25a from the textbook ]

## Slide 70
What does this circuit do?
0
0
0
0
Clock
time

## Slide 71
What does this circuit do?
1
0
0
0
Clock
time

## Slide 72
What does this circuit do?
0
1
0
0
Clock
time

## Slide 73
What does this circuit do?
1
1
0
0
Clock
time

## Slide 74
What does this circuit do?
0
0
1
0
Clock
time

## Slide 75
What does this circuit do?
1
0
1
1
Clock
time

## Slide 76
What does this circuit do?
0
0
0
0
Clock
time

## Slide 77
What does this circuit do?
1
0
0
0
Clock
time

## Slide 78
What does this circuit do?
0
1
0
0
Clock
time

## Slide 79
A modulo-6 counter with synchronous reset
[ Figure 5.25 from the textbook ]
Enable
Q
0
Q
1
Q
2
D
0
D
1
D
2
Load
Clock
1
0
0
0
Clock
0
1
2
3
4
5
0
1
Clock
Count
Q
0
Q
1
Q
2
(a) Circuit
(b) Timing diagram

## Slide 80
A modulo-6 counter with asynchronous reset
[ Figure 5.26 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
(b) Timing diagram
0
1
2
3
4
5
0
1
2

## Slide 81
A modulo-6 counter with asynchronous reset
[ Figure 5.26 from the textbook ]
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
Clock
Q
0
Q
1
Q
2
Count
(b) Timing diagram
0
1
2
3
4
5
0
1
2
The number 5 is displayed
for a very short amount of time

## Slide 82: Other Types of Counters (Section 5.11)

## Slide 83: A two-digit BCD counter
Use Two Parallel-load four-bit counters
  Figure 5.24
Each counts in binary
  0-9
Resets generated on 9
  Reset by loading 0’s
Second digit enabled by a 9 on first counter

## Slide 84
A two-digit BCD counter
[ Figure 5.27 from the textbook ]

## Slide 85
A two-digit BCD counter
[ Figure 5.27 from the textbook ]
What is this?

## Slide 86
It is a counter with parallel-load capability
[ Figure 5.24 from the textbook ]

## Slide 87
It is a counter with parallel-load capability
[ Figure 5.24 from the textbook ]
In this case,
the z output is ignored

## Slide 88
A two-digit BCD counter

## Slide 89
A two-digit BCD counter

## Slide 90
Zeroing the BCD counter
[ Figure 5.27 from the textbook ]
1
1
Setting "Clear" to 1,
zeroes both counters.
1
1
1

## Slide 91
Zeroing the BCD counter
[ Figure 5.27 from the textbook ]
0
0
0
0
1
1
Setting "Clear" to 1,
zeroes both counters.
1
1
1
0
0
0
0
0
0

## Slide 92
How to zero a counter
[ Figure 5.24 from the textbook ]
0
0
0
0
Set all parallel load
input lines to zero.

## Slide 93
How to zero a counter
[ Figure 5.24 from the textbook ]
1
0
0
0
0
0
0
0
0
Set "Load" to 1, to open the
"1" line of the multiplexers.

## Slide 94
How to zero a counter
[ Figure 5.24 from the textbook ]
1
0
0
0
0
0
0
0
0
0
0
0
0
When the positive edge of the
clock arrives, all outputs
are set to zero together.

## Slide 95
When Clear = 0
[ Figure 5.27 from the textbook ]
When "Clear" is equal to 0,
the two OR gates depend only
on the feedback connections.
0
0
0

## Slide 96
Enabling the second counter
[ Figure 5.27 from the textbook ]

## Slide 97
Enabling the second counter
0
0
0
0
0
0
The counter for the most
significant digit is disabled
most of the time.
0
0
0
0
0
0

## Slide 98
Enabling the second counter
1
0
0
0
0
0
The counter for the most
significant digit is disabled
most of the time.
1
0
0
0
0
0

## Slide 99
Enabling the second counter
0
1
0
0
0
0
The counter for the most
significant digit is disabled
most of the time.
2
0
0
0
0
0

## Slide 100
Enabling the second counter
1
1
0
0
0
0
The counter for the most
significant digit is disabled
most of the time.
3
0
0
0
0
0

## Slide 101
Enabling the second counter
0
0
1
0
0
0
The counter for the most
significant digit is disabled
most of the time.
4
0
0
0
0
0

## Slide 102
Enabling the second counter
1
0
1
0
0
0
The counter for the most
significant digit is disabled
most of the time.
5
0
0
0
0
0

## Slide 103
Enabling the second counter
0
1
1
0
0
0
The counter for the most
significant digit is disabled
most of the time.
6
0
0
0
0
0

## Slide 104
Enabling the second counter
1
1
1
0
0
0
The counter for the most
significant digit is disabled
most of the time.
7
0
0
0
0
0

## Slide 105
Enabling the second counter
0
0
0
1
0
0
The counter for the most
significant digit is disabled
most of the time.
8
0
0
0
0
0

## Slide 106
Enabling the second counter
1
0
0
1
1
1
It is enabled only when
the first counter is at 9.
9
0
0
0
0
0

## Slide 107
Enabling the second counter
1
0
0
1
1
1
At the same time the first
counter is reset.
9
0
0
0
0
1
0

## Slide 108
Enabling the second counter
0
0
0
0
0
0
At the same time the first
counter is reset.
0
1
0
0
0
0
1

## Slide 109
Enabling the second counter
1
0
0
0
0
0
1
1
0
0
0
0
1

## Slide 110
Enabling the second counter
0
1
0
0
0
0
2
1
0
0
0
0
1

## Slide 111
. . .

## Slide 112
Enabling the second counter
0
0
0
1
0
0
8
1
0
0
0
0
1

## Slide 113
Enabling the second counter
1
0
0
1
1
1
9
1
0
0
0
1
1

## Slide 114
Enabling the second counter
0
0
0
0
0
0
0
0
1
0
0
0
2

## Slide 115
Enabling the second counter
1
0
0
0
0
0
1
0
1
0
0
0
2

## Slide 116
. . .

## Slide 117
Enabling the second counter
0
0
0
1
0
0
8
1
0
0
1
0
9

## Slide 118
Enabling the second counter
1
0
0
1
1
1
9
1
0
0
1
1
9

## Slide 119
Enabling the second counter
1
0
0
1
1
1
9
1
0
0
1
1
9
1
1

## Slide 120
Enabling the second counter
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 121
Enabling the second counter
1
0
0
0
0
0
1
0
0
0
0
0
0
0
0

## Slide 122: Ring Counter

## Slide 123
How to build a 4-bit ring counter
To build a ring counter we start with a shift register.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
In
Out
Q
0
Q
1
Q
2
Q
3

## Slide 124
Next, add a loop from the last flip-flop to the first…
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
In
Out
Q
0
Q
1
Q
2
Q
3
How to build a 4-bit ring counter

## Slide 125
... and remove the In input line.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
How to build a 4-bit ring counter

## Slide 126
Also, add a start input that goes inverted to preset_n of
the first flip=flop and to clear_n of all remaining flip-flops.
How to build a 4-bit ring counter
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start

## Slide 127
Finally, extend the output lines that form the count number.
How to build a 4-bit ring counter
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3

## Slide 128
This is the final circuit diagram.
How to build a 4-bit ring counter
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3

## Slide 129: 4-bit ring counter
  There is only one 1 on the outputs of the four flip-flops
  The counting sequence is: 1000, 0100, 0010, 0001, 1000, …
  To reset the counter
    set start to 1 for a short period of time
    This sets the four outputs to 1000

## Slide 130
4-bit ring counter: How does it work
To initialize the counter set Start to 1.
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3

## Slide 131
4-bit ring counter: How does it work
After the NOT gate, this 1 goes as 0 to preset_n of
the first flip-flop and to clear_n of all remaining flip-flops.
1
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3

## Slide 132
4-bit ring counter: How does it work
This sets the output pattern to 1000,
i.e., only the first bit is one and the rest are zeros.
1
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0

## Slide 133
4-bit ring counter: How does it work
Setting Start to 0 has no effect on the outputs,
because both preset_n and clear_n are sensitive only to 0.
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0

## Slide 134
4-bit ring counter: How does it work
The initialization does not depend on the clock since both
preset_n and clear_n bypass the gates of the latches in the flip-flops.
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0

## Slide 135
4-bit ring counter: How does it work
That last 0 loops back to the D input of the first flip-flop.
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0
0

## Slide 136
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0
0

## Slide 137
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
1
0
0
1
0
0
0

## Slide 138
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
1
0
0
1
0
0
0

## Slide 139
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
0
1
0
0
1
0
0

## Slide 140
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
0
1
0
0
1
0
0

## Slide 141
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
0
0
1
0
0
1
1

## Slide 142
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
0
0
0
0
1
0
0
1
1

## Slide 143
4-bit ring counter: How does it work
Clock
Start
time
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0
0

## Slide 144
4-bit ring counter: How does it work
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Start
Q
0
Q
1
Q
2
Q
3
1
1
0
0
0
0
0
0
0
It is back to the start of the counting sequence,
which is: 1000, 0100, 0010, 0001.

## Slide 145
n-bit ring counter
[ Figure 5.28a from the textbook ]

## Slide 146: Ring Counter (alternative implementation)

## Slide 147
This implementation uses 2-bit up-counter followed by a 2-to-4 decoder.
The counter cycles through 00, 01, 10, 11, 00, …
Recall that the outputs of the decoder are one-hot encoded. Thus, there is only one 1 on its outputs.
Because the output of the counter is the input to the decoder, the outputs of the decoder cycle through: 1000, 0100, 0010, 0001, 1000, …
This is the counting sequence for a ring counter.
Alternative version of a 4-bit ring counter

## Slide 148
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
Alternative version of a 4-bit ring counter
[ Figure 5.28b from the textbook ]

## Slide 149
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
What are the components?

## Slide 150
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
2-Bit Synchronous Up-Counter

## Slide 151
2-Bit Synchronous Up-Counter
T
Q
Q
Clock
T
Q
Q
1
Clear_n

## Slide 152
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
2-to-4 Decoder with Enable Input
[ Figure 5.28b from the textbook ]

## Slide 153
[ Figure 4.14c from the textbook ]
En
2-to-4 Decoder with Enable Input

## Slide 154
[ Figure 4.14c from the textbook ]
1
(always enabled in this example)
2-to-4 Decoder with Enable Input

## Slide 155
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
[ Figure 5.28b from the textbook ]

## Slide 156
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 0
1
0
To initialize this circuit set Start to 1, which sets the counter to 00.

## Slide 157
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 0
1 0 0 0
1
0
This sets the outputs of the decoder to the start of the counting sequence.

## Slide 158
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 0
1 0 0 0
0
1
When Start is equal to 0, clear_n has no effect.

## Slide 159
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 0
1 0 0 0
0
1

## Slide 160
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 1
1 0 0 0
0
1
The counter increments the count on the positive clock edge ...

## Slide 161
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 1
0 1 0 0
0
1
… this updates the outputs of the decoder (which are one hot encoded).

## Slide 162
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 1
0 1 0 0
0
1

## Slide 163
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
1 0
0 0 1 0
0
1

## Slide 164
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
1 0
0 0 1 0
0
1

## Slide 165
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
1 1
0 0 0 1
0
1

## Slide 166
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
1 1
0 0 0 1
0
1

## Slide 167
clear_n
2-bit up-counter
Start
w
0
En
y
0
w
1
y
1
y
2
y
3
1
Q
1
Q
2
Q
3
2-to-4 decoder
Q
1
Q
0
Clock
Q
0
How Does It Work?
0 0
1 0 0 0
0
1
It is back to the start of the counting sequence,
which is: 1000, 0100, 0010, 0001.

## Slide 168: Johnson Counter

## Slide 169
How to build a 4-bit Johnson counter
To build a Johnson counter start with a shift register.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
In
Out
Q
0
Q
1
Q
2
Q
3

## Slide 170
How to build a 4-bit Johnson counter
Next, add a loop from the Q output of the last flip-flop to the first…
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
In
Out
Q
0
Q
1
Q
2
Q
3

## Slide 171
How to build a 4-bit Johnson counter
... and remove the In input line.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3

## Slide 172
How to build a 4-bit Johnson counter
Also, add a Reset_n line that goes to clear_n of all flip-flops.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n

## Slide 173
How to build a 4-bit Johnson counter
Finally, extend the output lines that form the count number.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3

## Slide 174
How to build a 4-bit Johnson counter
This is the final circuit diagram.
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3

## Slide 175: 4-Bit Johnson Counter
  Only 1-bit changes at a time
  Start with a reset of all flip-flops
  The counting sequence is: 0000, 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
  An n-bit Johnson counter has a counting sequence of length 2n

## Slide 176
Initialization: How does it work?
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3

## Slide 177
Initialization: How does it work?
To initialize the Johnson counter set Reset_n to 0 ...
0
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3

## Slide 178
Initialization: How does it work?
... this zeros the outputs of all flip-flops ...
0
0
0
0
0
0
0
0
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
0

## Slide 179
Initialization: How does it work?
0
0
0
0
0
0
0
0
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
0
1
1
... and also sets the Q output of the last flip-flop to 1.

## Slide 180
Counting: How does it work?
0
0
0
0
0
0
0
0
0
0
0
0
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
0
1
1

## Slide 181
Counting: How does it work?
1
0
0
0
0
0
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
To start counting, Reset_n needs to be set to 1.

## Slide 182
Counting: How does it work?
1
0
0
0
0
0
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 183
Counting: How does it work?
1
1
0
0
0
1
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 184
Counting: How does it work?
1
1
0
0
0
1
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 185
Counting: How does it work?
1
1
1
0
0
1
1
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 186
Counting: How does it work?
1
1
1
0
0
1
1
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 187
Counting: How does it work?
1
1
1
1
0
1
1
1
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 188
Counting: How does it work?
1
1
1
1
0
1
1
1
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 189
Counting: How does it work?
1
1
1
1
1
1
1
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 190
Counting: How does it work?
1
1
1
1
1
1
1
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 191
Counting: How does it work?
1
0
1
1
1
0
1
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 192
Counting: How does it work?
1
0
1
1
1
0
1
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 193
Counting: How does it work?
1
0
0
1
1
0
0
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 194
Counting: How does it work?
1
0
0
1
1
0
0
1
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 195
Counting: How does it work?
1
0
0
0
1
0
0
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 196
Counting: How does it work?
1
0
0
0
1
0
0
0
1
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
0
0
Clock
Reset_n
time

## Slide 197
Counting: How does it work?
1
0
0
0
0
0
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
Clock
Reset_n
time

## Slide 198
Counting: How does it work?
1
0
0
0
0
0
0
0
0
1
1
1
D
Q
Q
Clock
D
Q
Q
D
Q
Q
D
Q
Q
Out
Q
0
Q
1
Q
2
Q
3
Reset_n
Q
0
Q
1
Q
2
Q
3
1
1
1
It is back to the start of the counting sequence, which is:
0000, 1000, 1100, 1110, 1111, 0111, 0011, 0001.

## Slide 199
n-bit Johnson Counter
[ Figure 5.29 from the textbook ]

## Slide 200: Questions?

## Slide 201: THE END