## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Mealy State Model
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 10 is due on Monday Nov 11 @ 10 pm
Homework 11 is due on Monday Nov 18 @ 10 pm

## Slide 4
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
The general form of a synchronous sequential circuit
[ Figure 6.1 from the textbook ]

## Slide 5
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 6
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Mealy Type

## Slide 7: Sample Problem
Implement a 11 detector. In other words, the output should be equal to 1 if two consecutive 1’s have been detected on the input line.
The output should become 1 as soon as the second 1 is detected in the input.

## Slide 8
Moore Machine
Implementation

## Slide 9
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 10
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 11
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 12
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 13
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 14
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 15
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 16
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 17
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 18
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 19
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 20
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 21
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 22
Inferring the States

## Slide 23
[ Figure 6.8 from the textbook ]

## Slide 24: The New and Improved Circuit Diagram
Y1(w, y2, y1) = w
Y2(w, y2, y1) = wy1
z(y2, y1) = y2
[ Figure 6.17 from the textbook ]
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn

## Slide 25
Mealy Machine
Implementation

## Slide 26
State diagram of an FSM that realizes the task
[ Figure 6.23 from the textbook ]
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 27
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 28
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 29
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 30
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 31
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 32
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 33
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 34
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 35
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 36
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 37
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 38
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 39
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 40
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 41
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 42
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 43
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 44
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 45
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
Let’s Do a Simulation
input
output
A
B
Reset
w = 1
z = 0
¤
w = 0
z = 0
¤
w = 1
z = 1
¤
w = 0
z = 0
¤

## Slide 46
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤
Now Let’s Do the State Table for this FSM
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
B

## Slide 47
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤
Now Let’s Do the State Table for this FSM
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
A
B
0
0
B
A
B
0
1

## Slide 48
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
A
B
0
0
B
A
B
0
1
The State Table for this FSM
[ Figure 6.24 from the textbook ]

## Slide 49
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
A
B
0
0
B
A
B
0
1
Let’s Do the State-assigned Table
Present
Next state
Output
state
w
=
0
w
=
1
w
=
0
w
=
1
y
Y
Y
z
z
A
0
B
1

## Slide 50
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
A
B
0
0
B
A
B
0
1
Let’s Do the State-assigned Table
Present
Next state
Output
state
w
=
0
w
=
1
w
=
0
w
=
1
y
Y
Y
z
z
A
0
0
1
0
0
B
1
0
1
0
1

## Slide 51
The State-assigned Table
Present
Next state
Output
state
w
=
0
w
=
1
w
=
0
w
=
1
y
Y
Y
z
z
A
0
0
1
0
0
B
1
0
1
0
1
[ Figure 6.25 from the textbook ]

## Slide 52
The State-assigned Table
Present
Next state
Output
state
w
=
0
w
=
1
w
=
0
w
=
1
y
Y
Y
z
z
A
0
0
1
0
0
B
1
0
1
0
1
[ Figure 6.25 from the textbook ]
Y = D = w
z = wy

## Slide 53
The State-assigned Table
Present
Next state
Output
state
w
=
0
w
=
1
w
=
0
w
=
1
y
Y
Y
z
z
A
0
0
1
0
0
B
1
0
1
0
1
[ Figure 6.25 from the textbook ]
Y = D = w
z = wy
This assumes D flip-flop

## Slide 54
Clock
Resetn
D
Q
Q
w
z
y
[ Figure 6.26 from the textbook ]
Circuit Implementation of the FSM
Y = D = w
z = wy

## Slide 55
Clock
Resetn
D
Q
Q
w
z
(a) Circuit
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
y
w
z
y
(b) Timing diagram
[ Figure 6.26 from the textbook ]
Circuit & Timing Diagram

## Slide 56
What if we wanted the output signal to be delayed by 1 clock cycle?

## Slide 57
[ Figure 6.27a from the textbook ]
Circuit Implementation of the Modified FSM

## Slide 58
[ Figure 6.27a from the textbook ]
Circuit Implementation of the Modified FSM
This flip-flop delays the
output signal by one clock cycle

## Slide 59: We Have Seen This Diagram Before
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
Y1(w, y2, y1) = w
Y2(w, y2, y1) = wy1
z(y2, y1) = y2
[ Figure 6.17 from the textbook ]

## Slide 60
Circuit & Timing Diagram
[ Figure 6.27 from the textbook ]

## Slide 61
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
The general form of a synchronous sequential circuit
[ Figure 6.1 from the textbook ]

## Slide 62
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 63
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Mealy Type

## Slide 64
Moore Mealy

## Slide 65
Moore Mealy

## Slide 66
Mealy
Moore

## Slide 67
Mealy
Moore
Notice that the output of the Moore machine is delayed by one clock cycle

## Slide 68
Mealy
Moore
Clock cycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
1
0
0
1
1
0
0
input
output
input
output
Notice that the output of the Moore machine is delayed by one clock cycle

## Slide 69: Questions?

## Slide 70: THE END