## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2
Serial Adder
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 11 is due on Monday Nov 18 @ 10pm

## Slide 4: Quick Review

## Slide 5
[ Figure 3.1a from the textbook ]
Adding two bits
(there are four possible cases)

## Slide 6
[ Figure 3.1b from the textbook ]
Adding two bits
(the truth table)

## Slide 7
[ Figure 3.1c from the textbook ]
Adding two bits
(the logic circuit)

## Slide 8
[ Figure 3.1c-d from the textbook ]
The Half-Adder

## Slide 9
Bit position i
Addition of multibit numbers
[ Figure 3.2 from the textbook ]

## Slide 10
Problem Statement and Truth Table
[ Figure 3.3a from the textbook ]
[ Figure 3.2b from the textbook ]

## Slide 11
Let’s fill-in the two K-maps
[ Figure 3.3a-b from the textbook ]

## Slide 12
Let’s fill-in the two K-maps
[ Figure 3.3a-b from the textbook ]

## Slide 13
The circuit for the two expressions
[ Figure 3.3c from the textbook ]

## Slide 14
This is called the Full-Adder
[ Figure 3.3c from the textbook ]

## Slide 15
XOR Magic

## Slide 16
XOR Magic

## Slide 17
XOR Magic
Can you prove this?

## Slide 18
XOR Magic
(si can be implemented in two different ways)

## Slide 19
HA
HA
s
c
s
c
c
i
x
i
y
i
c
i
1
+
s
i
c
i
x
i
y
i
c
i
1
+
s
i
(a) Block diagram
(b) Detailed diagram
A decomposed implementation
of the full-adder circuit
[ Figure 3.4 from the textbook ]

## Slide 20
HA
HA
s
c
s
c
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 21
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 22
FA
We can place the arrows anywhere
xi
yi
si
ci+1
ci

## Slide 23
FA
x
n –
1
c
n
c
n
1
”
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
MSB position
LSB position
n-bit ripple-carry adder
[ Figure 3.5 from the textbook ]

## Slide 24
FA
x
n –
1
c
n
c
n
1
”
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
MSB position
LSB position
n-bit ripple-carry adder abstraction

## Slide 25
x
n –
1
c
n
y
n
1
–
s
n
1
–
x
1
y
1
s
1
x
0
y
0
s
0
c
0
n-bit ripple-carry adder abstraction

## Slide 26
The x and y lines are typically
grouped together for better visualization,
but the underlying logic remains the same
x
n –
1
c
n
y
n
1
–
s
n
1
–
x
1
y
1
s
1
y
0
s
0
c
0
x
0

## Slide 27: Serial Adder
The n-bit adder requires all bits to be provided at the same time.
In some cases, we may want to add the numbers as the bits come in.
Also, with an n-bit adder we are limited to n-bits. Circuits for larger n are more complex.
Can we add arbitrarily long numbers.

## Slide 28
Sum
A
B
+
=
Shift register
Shift register
Adder
FSM
Shift register
B
A
a
b
s
Clock
Block diagram for the serial adder
[ Figure 6.39 from the textbook ]

## Slide 29: Mealy Machine Implementation

## Slide 30
State diagram for the serial adder FSM
[ Figure 6.40 from the textbook ]

## Slide 31
State diagram for the serial adder FSM
[ Figure 6.40 from the textbook ]

## Slide 32
State diagram for the serial adder FSM
[ Figure 6.40 from the textbook ]

## Slide 33
State diagram for the serial adder FSM

## Slide 34
State diagram for the serial adder FSM

## Slide 35
State diagram for the serial adder FSM

## Slide 36
State diagram for the serial adder FSM
G
G
G
G
H
H
H
H
G
G
G
H
G
H
H
H

## Slide 37
State diagram for the serial adder FSM
G
G
G
G
H
H
H
H
G
G
G
H
G
H
H
H

## Slide 38
State diagram for the serial adder FSM
G
G
G
G
H
H
H
H
G
G
G
H
G
H
H
H

## Slide 39
State diagram for the serial adder FSM
G
G
G
G
H
H
H
H
G
G
G
H
G
H
H
H

## Slide 40
State diagram for the serial adder FSM
G
G
G
G
H
H
H
H
G
G
G
H
G
H
H
H

## Slide 41
State diagram for the serial adder FSM
[ Figure 6.40 & 6.41 from the textbook ]
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM

## Slide 42
State diagram for the serial adder FSM
[ Figure 6.40 & 6.41 from the textbook ]
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM

## Slide 43
State diagram for the serial adder FSM
[ Figure 6.40 & 6.41 from the textbook ]
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM

## Slide 44
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM
[ Figure 6.41 from the textbook ]

## Slide 45
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM
[ Figure 6.41 & 6.42 from the textbook ]
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
State-assigned table for the serial adder

## Slide 46
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM
[ Figure 6.41 & 6.42 from the textbook ]
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
State-assigned table for the serial adder

## Slide 47
Present
Next state
Output
s
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder FSM
[ Figure 6.41 & 6.42 from the textbook ]
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
State-assigned table for the serial adder

## Slide 48
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
Derivation of Y and s

## Slide 49
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Derivation of Y and s

## Slide 50
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Derivation of Y and s

## Slide 51
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
b
00
01
11
10
0
1
y
a
s
b
00
01
11
10
0
1
y
a
Y
Derivation of Y and s

## Slide 52
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
b
00
01
11
10
0
1
1
1
0
y
a
0
1
1
0
0
s
b
00
01
11
10
0
1
0
0
1
y
a
1
1
0
1
0
Y
Derivation of Y and s

## Slide 53
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
b
00
01
11
10
0
1
1
1
0
y
a
0
1
1
0
0
s
b
00
01
11
10
0
1
0
0
1
y
a
1
1
0
1
0
Y
Derivation of Y and s

## Slide 54
Present
Next state
Output
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
y | a | b | Y | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
b
00
01
11
10
0
1
1
1
0
y
a
0
1
1
0
0
s
b
00
01
11
10
0
1
0
0
1
y
a
1
1
0
1
0
Y
Y = ab + ay + by
s = XOR(XOR(a, b), y)
Derivation of Y and s

## Slide 55
The circuit for the two expressions
[ Figure 3.3c from the textbook ]

## Slide 56
The circuit for the two expressions
[ Figure 3.3c from the textbook ]
a
b
y
Y
s

## Slide 57
Full
adder
a
b
s
D
Q
Q
carry-out
Clock
Reset
Y
y
Circuit for the serial adder FSM
[ Figure 6.43 from the textbook ]
Y = ab + ay + by
s = XOR(XOR(a, b), y)
(sum bit from FA)
(carry bit from FA)

## Slide 58: Moore Machine Implementation

## Slide 59
H
1
s
1
=
¤
Reset
H
0
s
0
=
¤
01
10
11
11
01
10
G
1
s
1
=
¤
G
0
s
0
=
¤
01
10
00
01
00
10
11
00
00
11
State diagram for the Moore-type serial adder FSM
[ Figure 6.44 from the textbook ]

## Slide 60
H
1
s
1
=
¤
Reset
H
0
s
0
=
¤
01
10
11
11
01
10
G
1
s
1
=
¤
G
0
s
0
=
¤
01
10
00
01
00
10
11
00
00
11
State diagram for the Moore-type serial adder FSM
[ Figure 6.44 from the textbook ]
carry=0, sum=0
carry=0, sum=1
carry=1, sum=0
carry=1, sum=1

## Slide 61
H
1
s
1
=
¤
Reset
H
0
s
0
=
¤
01
10
11
11
01
10
G
1
s
1
=
¤
G
0
s
0
=
¤
01
10
00
01
00
10
11
00
00
11
State diagram for the Moore-type serial adder FSM
[ Figure 6.44 from the textbook ]
carry=0, sum=0
carry=0, sum=1
carry=1, sum=0
carry=1, sum=1

## Slide 62
Present
Next state
Output
state
ab
=00
01
10
11
s
G
0
G
0
G
1
G
1
H
0
0
G
1
G
0
G
1
G
1
H
0
1
H
0
G
1
H
0
H
0
H
1
0
H
1
G
1
H
0
H
0
H
1
1
State table for the Moore-type serial adder FSM
[ Figure 6.45 from the textbook ]
H
1
s
1
=
¤
Reset
H
0
s
0
=
¤
01
10
11
11
01
10
G
1
s
1
=
¤
G
0
s
0
=
¤
01
10
00
01
00
10
11
00
00
11

## Slide 63
Present
Next state
Output
state
ab
=00
01
10
11
s
G
0
G
0
G
1
G
1
H
0
0
G
1
G
0
G
1
G
1
H
0
1
H
0
G
1
H
0
H
0
H
1
0
H
1
G
1
H
0
H
0
H
1
1
State table for the Moore-type serial adder FSM
[ Figure 6.45 from the textbook ]

## Slide 64
Present
Next state
Output
state
ab
=00
01
10
11
s
G
0
G
0
G
1
G
1
H
0
0
G
1
G
0
G
1
G
1
H
0
1
H
0
G
1
H
0
H
0
H
1
0
H
1
G
1
H
0
H
0
H
1
1
State table for the Moore-type serial adder FSM
[ Figure 6.45 & 6.46 from the textbook ]
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
01
10
11

## Slide 65
Present
Next state
Output
state
ab
=00
01
10
11
s
G
0
G
0
G
1
G
1
H
0
0
G
1
G
0
G
1
G
1
H
0
1
H
0
G
1
H
0
H
0
H
1
0
H
1
G
1
H
0
H
0
H
1
1
State table for the Moore-type serial adder FSM
[ Figure 6.45 & 6.46 from the textbook ]
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1

## Slide 66
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
State-assigned table
for the Moore-type serial adder FSM
[ Figure 6.46 from the textbook ]

## Slide 67
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1, Y2, and s
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 |  | 
0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 68
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 |  | 
0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 69
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 

## Slide 70
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 
00
01
11
10
00
01
11
10
y
2
y
1
a b

## Slide 71
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 
00
01
11
10
00
01
0
1
1
1
0
1
0
0
0
1
1
1
0
1
0
0
11
10
y
2
y
1
a b

## Slide 72
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y1
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 
00
01
11
10
00
01
0
1
1
1
0
1
0
0
0
1
1
1
0
1
0
0
11
10
y
2
y
1
a b
Y1 = a + b + y2

## Slide 73
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 

## Slide 74
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1

## Slide 75
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
y
2
y
1
a b

## Slide 76
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
00
01
11
10
00
01
0
0
0
0
1
0
1
0
1
0
0
1
1
1
1
1
11
10
y
2
y
1
a b

## Slide 77
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
00
01
11
10
00
01
0
0
0
0
1
0
1
0
1
0
0
1
1
1
1
1
11
10
y
2
y
1
a b

## Slide 78
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving Y2
y2 | y1 | a | b | Y1 | Y2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
00
01
11
10
00
01
0
0
0
0
1
0
1
0
1
0
0
1
1
1
1
1
11
10
y
2
y
1
a b
Y2 = ab + ay2 + by2

## Slide 79
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving s
y2 | y1 | s
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 80
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving s
y2 | y1 | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 81
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving s
y2 | y1 | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0
1
0
1
y
2
y
1
s

## Slide 82
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving s
y2 | y1 | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0
1
0
1
0
1
y
2
0
1
y
1
s

## Slide 83
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
Deriving s
y2 | y1 | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0
1
0
1
0
1
y
2
0
1
y
1
s
s = y1

## Slide 84
Present
Next state
state
ab
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
s
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
State-assigned table
for the Moore-type serial adder FSM
[ Figure 6.46 from the textbook ]
s = y1
Y2 = ab + ay2 + by2
Y1 = a + b + y2

## Slide 85
Full
adder
a
b
D
Q
Q
Carry-out
Clock
Reset
D
Q
Q
s
Y
2
Y
1
Sum bit
y
2
y
1
Circuit for the Moore-type serial adder FSM
[ Figure 6.47 from the textbook ]
s = y1
Y2 = ab + ay2 + by2
(sum bit from FA)
(carry bit from FA)
Y1 = a + b + y2

## Slide 86
Full
adder
a
b
s
D
Q
Q
carry-out
Clock
Reset
Y
y
Circuit for the Mealy-type serial adder FSM
[ Figure 6.43 from the textbook ]
Y = ab + ay + by
s = XOR(XOR(a, b), y)
(sum bit from FA)
(carry bit from FA)

## Slide 87
Full
adder
a
b
D
Q
Q
Carry-out
Clock
Reset
D
Q
Q
s
Y
2
Y
1
Sum bit
y
2
y
1
Circuit for the Moore-type serial adder FSM
[ Figure 6.47 from the textbook ]
s = y1
Y2 = ab + ay2 + by2
(sum bit from FA)
(carry bit from FA)
Y1 = a + b + y2
This FF just delays the
output by 1 clock cycle

## Slide 88
Arbiter Circuit

## Slide 89: Goal
Design a machine that controls access by several devices to a shared resource.
The resource can be used by only one device at a time.
Any changes can occur only on the positive edge of the clock signal.
Each device provides one input to the FSM, which is called a request.
The FSM produces one output for each device, which is called a grant.

## Slide 90: Goal
The requests from the devices are prioritized.
If two requests are active at the same time, then only the device with the highest priority will be given access to the shared resource.
After a device is done with the shared resource, it must make its request signal equal to 0.
If there are no outstanding requests, then the FSM stays in an Idle state.

## Slide 91
Arbiter
Request1
Grant1
Request2
Grant2
Device 1
Device 2
Shared
resource
Grant3
Device 3
Request3
Conceptual Diagram

## Slide 92
Arbiter
Request1
Grant1
Request2
Grant2
Device 1
Device 2
Shared
resource
Grant3
Device 3
Request3
Conceptual Diagram
Request (r)
Grant (g)
[ Figure 9.20 from the textbook ]

## Slide 93
Idle
000
1xx
Reset
gnt1
g
1
¤
1
=
x1x
gnt2
g
2
¤
1
=
xx1
gnt3
g
3
¤
1
=
0xx
1xx
01x
x0x
001
xx0
[ Figure 6.72 from the textbook ]
State diagram for the arbiter

## Slide 94
Idle
000
1xx
Reset
gnt1
g
1
¤
1
=
x1x
gnt2
g
2
¤
1
=
xx1
gnt3
g
3
¤
1
=
0xx
1xx
01x
x0x
001
xx0
State diagram for the arbiter
Highest Priority Device

## Slide 95
Idle
000
1xx
Reset
gnt1
g
1
¤
1
=
x1x
gnt2
g
2
¤
1
=
xx1
gnt3
g
3
¤
1
=
0xx
1xx
01x
x0x
001
xx0
State diagram for the arbiter
Lowest Priority Device
Highest Priority Device

## Slide 96
Idle
000
1xx
Reset
gnt1
g
1
¤
1
=
x1x
gnt2
g
2
¤
1
=
xx1
gnt3
g
3
¤
1
=
0xx
1xx
01x
x0x
001
xx0
State diagram for the arbiter
The three request bits
r1 r2 r3

## Slide 97
Idle
000
1xx
Reset
gnt1
g
1
¤
1
=
x1x
gnt2
g
2
¤
1
=
xx1
gnt3
g
3
¤
1
=
0xx
1xx
01x
x0x
001
xx0
State diagram for the arbiter
Each device must
release the resource
after it is done using it

## Slide 98
r
1
r
2
r
1
r
2
r
3
Idle
Reset
gnt1
g
1
¤
1
=
gnt2
g
2
¤
1
=
gnt3
g
3
¤
1
=
r
1
r
1
r
1
r
2
r
3
r
2
r
3
r
1
r
2
r
3
[ Figure 6.73 from the textbook ]
Alternative style of state diagram for the arbiter

## Slide 99
This design has one flaw:
If device1 and device2 raise requests all the time, then device3 will never get serviced.

## Slide 100
This state diagram solves this problem

## Slide 101
Let's look at a simpler example with only two devices that need to use the shared resource

## Slide 102
Idle
00
1x
Reset
gnt1
g
1
¤
1
=
x1
gnt2
g
2
¤
1
=
0x
1x
01
x0
State diagram for the simpler arbiter

## Slide 103
State diagram for the arbiter circuit

## Slide 104
State Table

## Slide 105
State-Assigned Table
Present
Next state
state
r1r2
=00
01
10
11
Output
y
2
y
1
Y
2
Y
1
g1g2
0 0
0
0
1 0
0
1
0 1
0 0
0 1
0
0
0 0
0
1
0 1
1 0
1 0
0
0
1 0
0
0
1 0
0 1
1 1
d
d
d d
d
d
d d
d d
A
B
C

## Slide 106
Output Expressions

## Slide 107
Next State Expressions

## Slide 108
Circuit Diagram

## Slide 109: Questions?

## Slide 110: THE END