## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Boolean Algebra
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW1 is due today @ 10 pm
Sample solutions will be posted on Canvas after the deadline.
Look for the solutions under the “Files” tab.
No late homeworks will be accepted.

## Slide 4: Administrative Stuff
HW2 is out
It is due on Monday Sep 8 @ 10pm.
Submit it on Canvas before the deadline.

## Slide 5: Did you play with this toy?

## Slide 6: AND Gate

## Slide 7: OR Gate

## Slide 8: NOT Gate (the switch is ON but the light is OFF)

## Slide 9: NOT Gate (the switch is OFF but the light is ON)

## Slide 11: Boolean Algebra
George Boole
1815-1864
An algebraic structure consists of
  a set of elements {0, 1}
  binary operators {+, }
  and a unary operator { ’ } or { } or { ~ }
Introduced by George Boole in 1854
An effective means of describing circuits built with switches
A powerful tool that can be used for designing and analyzing logic circuits

## Slide 12: Different Notations for Negation
All three of these mean “negate x”
  x’
  x
  ~x

## Slide 13: Axioms of Boolean Algebra
1a. 0  0 = 0
1b. 1 + 1 = 1
2a. 1  1 = 1
2b. 0 + 0 = 0
3a. 0  1 = 1  0 = 0
3b. 1 + 0 = 0 + 1 = 1
4a. If x=0, then
4b. If x=1, then
x = 1
x = 0

## Slide 14: Single-Variable Theorems
5a. x  0 = 0
5b. x + 1 = 1
6a. x  1 = x
6b. x + 0 = x
7a. x  x = x
7b. x + x = x
8a. x 
8b. x +
9.
x = 0
x = 1
x = x

## Slide 15: Two- and Three-Variable Properties
10a. x  y = y  x
10b. x + y = y + x
11a. x  (y  z) = (x  y)  z
11b. x + (y + z) = (x + y) + z
12a. x  (y + z) = xy + xz
12b. x + y  z = (x + y)(x + z)
13a. x + x  y = x
13b. x  (x + y) = x
Commutative
Associative
Distributive
Absorption

## Slide 16: Two- and Three-Variable Properties
14a. x  y + x 
14b. (x + y)(x +
15a. x  y = x + y
15b. x + y = x  y
16a. x + xy = x + y
16b. x(x + y) = xy
17a. xy + yz + xz = xy + xz
17b. (x+y)(y+z)(x+z)=(x+y)(x+z)
Combining
DeMorgan’s
theorem
Consensus
y = x
y) = x

## Slide 17: Now, let’s prove all of these

## Slide 18: The First Four are Axioms (i.e., they don’t require a proof)
1a. 0  0 = 0
1b. 1 + 1 = 1
2a. 1  1 = 1
2b. 0 + 0 = 0
3a. 0  1 = 1  0 = 0
3b. 1 + 0 = 0 + 1 = 1
4a. If x=0, then
4b. If x=1, then
x = 1
x = 0

## Slide 19: But here are some other ways to think about them

## Slide 20
1
1
1
0
0
0
AND gate
OR gate

## Slide 21
1
1
1
0
0
0
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
OR gate

## Slide 22
1
1
1
0
0
0
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
OR gate

## Slide 23
0
0
0
1
1
1
AND gate
OR gate

## Slide 24
0
0
0
1
1
1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
OR gate

## Slide 25
1
0
1
0
1
0
1
0
0
0
1
1

## Slide 26
1
0
1
0
1
0
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
1
0
0
0
1
1
OR gate

## Slide 27
1
0
1
0
1
0
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
1
0
0
0
1
1
OR gate

## Slide 28
1
0
1
0
1
0
x1 | x2 | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
1
0
0
0
1
1
OR gate

## Slide 29
1
0
0
1

## Slide 30
NOT gate
1
0
0
1
x
x
0
1
1
0
NOT gate
x
x
0
1
1
0

## Slide 31: Single-Variable Theorems
5a. x  0 = 0
5b. x + 1 = 1
6a. x  1 = x
6b. x + 0 = x
7a. x  x = x
7b. x + x = x
8a. x 
8b. x +
9.
x = 0
x = 1
x = x

## Slide 33
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.

## Slide 34
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0  0 = 0 // axiom 1a

## Slide 35
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0  0 = 0 // axiom 1a
ii) If x = 1, then we have
1  0 = 0 // axiom 3a

## Slide 38
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0 + 1 = 1 // axiom 3b

## Slide 39
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0 + 1 = 1 // axiom 3b
ii) If x = 1, then we have
1 + 1 = 1 // axiom 1b

## Slide 41
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0  1 = 0 // axiom 3a
ii) If x = 1, then we have
1  1 = 1 // axiom 2a

## Slide 42
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0  1 = 0 // axiom 3a
ii) If x = 1, then we have
1  1 = 1 // axiom 2a

## Slide 44
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0 + 0 = 0 // axiom 2b
ii) If x = 1, then we have
1 + 0 = 1 // axiom 3b

## Slide 45
The Boolean variable x can have only two possible values: 0 or 1. Let’s look at each case separately.
i) If x = 0, then we have
0 + 0 = 0 // axiom 2b
ii) If x = 1, then we have
1 + 0 = 1 // axiom 3b

## Slide 47
i) If x = 0, then we have
0  0 = 0 // axiom 1a
ii) If x = 1, then we have
1  1 = 1 // axiom 2a

## Slide 48
i) If x = 0, then we have
0  0 = 0 // axiom 1a
ii) If x = 1, then we have
1  1 = 1 // axiom 2a

## Slide 50
i) If x = 0, then we have
0 + 0 = 0 // axiom 2b
ii) If x = 1, then we have
1 + 1 = 1 // axiom 1b

## Slide 51
i) If x = 0, then we have
0 + 0 = 0 // axiom 2b
ii) If x = 1, then we have
1 + 1 = 1 // axiom 1b

## Slide 53
i) If x = 0, then we have
0  1 = 0 // axiom 3a
ii) If x = 1, then we have
1  0 = 0 // axiom 3a

## Slide 54
i) If x = 0, then we have
0  1 = 0 // axiom 3a
ii) If x = 1, then we have
1  0 = 0 // axiom 3a

## Slide 56
i) If x = 0, then we have
0 + 1 = 1 // axiom 3b
ii) If x = 1, then we have
1 + 0 = 1 // axiom 3b

## Slide 57
i) If x = 0, then we have
0 + 1 = 1 // axiom 3b
ii) If x = 1, then we have
1 + 0 = 1 // axiom 3b

## Slide 59
i) If x = 0, then we have
x = 1 // axiom 4a
let y = x = 1, then we have
y = 0 // axiom 4b
Therefore,
x = x (when x =0)

## Slide 61
ii) If x = 1, then we have
x = 0 // axiom 4b
let y = x = 0, then we have
y = 1 // axiom 4a
Therefore,
x = x (when x =1)

## Slide 63
x
y
x
y
y
x
y
x

## Slide 64
x
y
x
y
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND gate
OR gate
y
x
y
x
The order of the inputs does not matter.

## Slide 66
x | y | z | x | y  z | x(yz)
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
Truth table for the left-hand side

## Slide 67
x | y | z | x | y  z | x(yz)
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 0 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 1 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 1 | 1 | 
Truth table for the left-hand side

## Slide 68
x | y | z | x | y  z | x(yz)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1
Truth table for the left-hand side

## Slide 69
x | y | z | x  y | z | (xy)z
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1
Truth table for the right-hand side

## Slide 70
These two are identical, which concludes the proof.

## Slide 72
x | y | z | x | y + z | x+(y+z)
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
Truth table for the left-hand side

## Slide 73
x | y | z | x | y + z | x+(y+z)
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 1 | 
0 | 1 | 0 | 0 | 1 | 
0 | 1 | 1 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 1 | 1 | 
Truth table for the left-hand side

## Slide 74
x | y | z | x | y + z | x+(y+z)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1
Truth table for the left-hand side

## Slide 75
x | y | z | x + y | z | (x+y)+z
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
Truth table for the right-hand side

## Slide 76
These two are identical, which concludes the proof.

## Slide 77: The Venn Diagram Representation
x
y
z
x
y
z
+

## Slide 78: Venn Diagram Basics
x
x
x
x
(b) Constant 0
(c) Variable
x
(d)
(a) Constant 1
x
[ Figure 2.14 from the textbook ]

## Slide 79: Venn Diagram Basics
x
y
z
x
x
y
x
y
(e)
(f)
(g)
(h)
x
y
x
y
+
x
y
z
+
x
y
y
[ Figure 2.14 from the textbook ]

## Slide 80: Let’s Prove the Distributive Properties

## Slide 81
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
x
x
y
x
y
x
+
z
x
y
z
+
(
)
(a)
(d)
(c)
(f)
x
z
y
z
+
(b)
(e)
[ Figure 2.15 from the textbook ]

## Slide 82
[ Figure 2.17 from the textbook ]

## Slide 83: Try to prove these ones at home

## Slide 84: DeMorgan’s Theorem

## Slide 85: Proof of DeMorgan’s theorem
[ Figure 2.13 from the textbook ]

## Slide 86: Proof of DeMorgan’s theorem

## Slide 87: Proof of DeMorgan’s theorem

## Slide 88: Proof of DeMorgan’s theorem

## Slide 89: Proof of DeMorgan’s theorem

## Slide 90: Proof of DeMorgan’s theorem

## Slide 91: Proof of DeMorgan’s theorem

## Slide 92: Proof of DeMorgan’s theorem
These two columns are equal. Therefore, the theorem is true.

## Slide 93: Alternative proof using Venn Diagrams
[ Figure 2.18 from the textbook ]

## Slide 95: Let’s prove the other DeMorgan’s theorem

## Slide 96: Let’s prove the other DeMorgan’s theorem

## Slide 97: Let’s prove the other DeMorgan’s theorem
0
1
1
1

## Slide 98: Let’s prove the other DeMorgan’s theorem
0
1
1
1
1
0
0
0

## Slide 99: Let’s prove the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0

## Slide 100: Let’s prove the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0
1
0
1
0

## Slide 101: Let’s prove the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0
1
0
1
0
1
0
0
0

## Slide 102: Let’s prove the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0
1
0
1
0
1
0
0
0
These two columns are equal, so the theorem is true.

## Slide 103: DeMorgan’s Theorem Generalizes to more than 2 variables

## Slide 104: DeMorgan’s Theorem Generalizes to more than 2 variables

## Slide 105: Try to prove these ones at home

## Slide 106: Venn Diagram Example Proof of Property 17a

## Slide 107: Left-Hand Side
x
y
z
x
y
x
y
z
x
z
y
x
z
y
z
x
y
x z
+
y
z
+
y
z
x
[ Figure 2.16 from the textbook ]

## Slide 108: Left-Hand Side
x
y
z
x
y
x
y
z
x
z
y
x
z
y
z
x
y
x z
+
y
z
+
y
z
x
[ Figure 2.16 from the textbook ]
Right-Hand Side
x
y
z
x
y
x
y
z
x
z
x
y
x
+
z
y
z
x

## Slide 109: Left-Hand Side
x
y
z
x
y
x
y
z
x
z
y
x
z
y
z
x
y
x z
+
y
z
+
y
z
x
[ Figure 2.16 from the textbook ]
Right-Hand Side
x
y
z
x
y
x
y
z
x
z
x
y
x
+
z
y
z
x
These two are equal

## Slide 110: Questions?

## Slide 111: THE END