## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Minimization
with K-Maps
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW4 is out
It is due on Monday Sep 22 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 4: Quick Review

## Slide 5: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 6: Expressions for the Maxterms
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 1’s
in the binary expansion
of the maxterm sub-index

## Slide 7: Expressions with three variables (for three-variable K-maps)

## Slide 8: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 0
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 9: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 10: Expressions with two variables (for three-variable K-maps)

## Slide 11: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 1
x1 x2
x1 x2
x1 x2
x1 x2

## Slide 12: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 0
x1 x3
x2 x3
x1 x3
x2 x3

## Slide 13: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 1
x1 x3
x2 x3
x1 x3
x2 x3

## Slide 14: Expressions with one variable (for three-variable K-maps)

## Slide 15: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
x1
x2
x1
x2

## Slide 16: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1
x3
x3

## Slide 17: Expressions with zero variables (for three-variable K-maps)

## Slide 18: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
0
1

## Slide 19: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder

## Slide 20: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5

## Slide 21: Adjacency Rules
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5
adjacent
columns

## Slide 22: Adjacency Rules
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5
adjacent
columns

## Slide 23: Grouping Size v.s. Term Size (for 3-variable K-maps)

## Slide 24: Grouping Size v.s. Term Size
3-variable term
2-variable term
1-variable term
0-variable term

## Slide 25: Grouping Size v.s. Term Size
3-variable term
2-variable term
1-variable term
0-variable term

## Slide 26: Grouping Size v.s. Term Size (for 4-variable K-maps)

## Slide 27: Grouping Size v.s. Term Size
3-variable term
2-variable term
1-variable term
0-variable term
4-variable term

## Slide 28: Grouping Size v.s. Term Size
3-variable term
2-variable term
1-variable term
0-variable term
4-variable term

## Slide 29: Grouping Size v.s. Term Size (for 2-variable K-maps)

## Slide 30: Grouping Size v.s. Term Size
2-variable term
1-variable term
0-variable term

## Slide 31: Grouping Size v.s. Term Size
2-variable term
1-variable term
0-variable term

## Slide 32: Grouping Size v.s. Term Size

## Slide 33
2-variable
K-map
3-variable
K-map
4-variable
K-map
2 3 4
1 2 3
0 1 2
N/A 0 1
N/A N/A 0

## Slide 34: Example: K-Map for the 2-to-1 Multiplexer

## Slide 35: 2-to-1 Multiplexer (Definition)
Has two inputs: x1 and x2
Also has another input line s
If s=0, then the output is equal to x1
If s=1, then the output is equal to x2

## Slide 36: Circuit for 2-to-1 Multiplexer
f
x
1
x
2
s
f
s
x
1
x
2
0
1
(c) Graphical symbol
(b) Circuit
[ Figure 2.33b-c from the textbook ]

## Slide 37: Truth Table for a 2-to-1 Multiplexer
[ Figure 2.33a from the textbook ]

## Slide 38: Let’s Draw the K-map
[ Figure 2.33a from the textbook ]

## Slide 39: Let’s Draw the K-map

## Slide 40: Let’s Draw the K-map

## Slide 41: Let’s Draw the K-map
0
1
0
0
0
1
1
1

## Slide 42: Let’s Draw the K-map
0
1
0
0
0
1
1
1

## Slide 43: Let’s Draw the K-map
0
1
0
0
0
1
1
1
f (s, x1, x2) =
x1 x2
s x1
+

## Slide 44: Let’s Draw the K-map
0
1
0
0
0
1
1
1
f (s, x1, x2) =
x1 x2
s x1
+
Something is wrong!

## Slide 45: Compare this with the SOP derivation

## Slide 46: Let’s Derive the SOP form

## Slide 47: Let’s Derive the SOP form

## Slide 48: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2
Where should we
put the negation signs?

## Slide 49: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2

## Slide 50: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+

## Slide 51: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+

## Slide 52: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+
f (s, x1, x2) =
s x1 (x2 + x2)
s (x1 +x1 )x2
+
+

## Slide 53: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+
f (s, x1, x2) =
s x1 (x2 + x2)
s (x1 +x1 )x2
+
+
f (s, x1, x2) =
s x1
s x2
+

## Slide 54: Let’s Draw the K-map again
[ Figure 2.33a from the textbook ]

## Slide 55: Let’s Draw the K-map again

## Slide 56: Let’s Draw the K-map again

## Slide 57: Let’s Draw the K-map again

## Slide 58: Let’s Draw the K-map again
s x1
x2
The order of the labeling matters.

## Slide 59: Let’s Draw the K-map again
s x1
x2

## Slide 60: Let’s Draw the K-map again
s x1
x2
0
1
0
0
0
1
1
1

## Slide 61: Let’s Draw the K-map again
s x1
x2
0
1
0
0
0
1
1
1

## Slide 62: Let’s Draw the K-map again
s x1
x2
0
1
0
0
0
1
1
1
f (s, x1, x2) =
s x1
s x2
+
This is correct!

## Slide 63: Two Different Ways to Draw the K-map
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 64: Another Way to Draw 3-variable K-map
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 65: There are 4 different versions!
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m2 | m6 | m4
 | 1 | m1 | m3 | m7 | m5
 | x3 |  | 
x1x2 |  | 0 | 1
 | 00 | m0 | m1
 | 01 | m2 | m3
 | 11 | m6 | m7
 | 10 | m4 | m5
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 66: Gray Code
Sequence of binary codes
Neighboring lines vary by only 1 bit
00
01
11
10
000
001
011
010
110
111
101
100

## Slide 67: Gray Code & K-map
s x1
x2

## Slide 68: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 69: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the LAST bit

## Slide 70: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the LAST bit

## Slide 71: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the FIRST bit

## Slide 72: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the FIRST bit

## Slide 73: Adjacency Rules
adjacent
columns
s x1
x2
000
010
110
100
001
011
111
101

## Slide 74: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These four neighbors
differ in the FIRST and LAST bit
They are similar in their MIDDLE bit

## Slide 75: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These four neighbors
differ in the FIRST and LAST bit
They are similar in their MIDDLE bit

## Slide 76: Four-Variable K-Map

## Slide 77
[ Figure 2.53 from the textbook ]
A four-variable Karnaugh map

## Slide 78
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 79: Adjacency Rules
adjacent
columns
adjacent
columns
adjacent
rows

## Slide 80: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus

## Slide 81: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 82: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 83: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 84
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map

## Slide 85
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map
0000
0100
1100
1000
0001
0101
1101
1001
0011
0111
1111
1011
0010
0110
1110
1010

## Slide 86
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 87
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 88: Five-Variable K-Map

## Slide 89
[ Figure 2.55 from the textbook ]
A five-variable Karnaugh map

## Slide 90: Six-Variable K-Map

## Slide 91
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map

## Slide 92
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map
A
B

## Slide 93
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map
A
B
C
E
F
D

## Slide 94: Seven-Variable K-Map

## Slide 95
A seven-variable Karnaugh map

## Slide 96
G = 0
G = 1
[Suggested in Karnaugh 1953]
A seven-variable Karnaugh map

## Slide 97: Strategy For Minimization

## Slide 98: Grouping Rules
Group “1”s with rectangles
Both sides a power of 2:
  1x1, 1x2, 2x1, 2x2, 1x4, 4x1, 2x4, 4x2, 4x4
Can use the same minterm more than once
Can wrap around the edges of the map
Some rules in selecting groups:
  Try to use as few groups as possible to cover all “1”s.
  For each group, try to make it as large as you can (i.e., if you can use a 2x2, don’t use a 2x1 even if that is enough).

## Slide 99: Terminology
  Literal: a variable, complemented or uncomplemented
  Some Examples:
  X1
  X2
_

## Slide 100: Terminology
Implicant: product term that indicates the input combinations for which the function output is 1
Example
  x1 - indicates that x1x2 and x1x2 yield output of 1
x
2
0
1
0
1
1
0
0
1
x
1
_
_
_
_

## Slide 101: Terminology
Prime Implicant
  Implicant that cannot be combined into another implicant with fewer literals
  Some Examples
x
1
x
2
x
3
0
1
1
1
1
1
1
0
00
01
11
10
0
1
x
1
x
2
x
3
0
1
1
1
1
1
1
0
00
01
11
10
0
1
Not prime
Prime

## Slide 102: Terminology
Essential Prime Implicant
  Prime implicant that includes a minterm not covered by any other prime implicant
  Some Examples
x
1
x
2
x
3
0
1
1
1
1
1
0
0
00
01
11
10
0
1

## Slide 103: Terminology
Cover
  Collection of implicants that account for all possible input valuations where output is 1
  Ex. x1’x2x3 + x1x2x3’ + x1x2’x3’
  Ex. x1’x2x3 + x1x3’
x
1
x
2
x
3
0
0
0
1
1
1
0
0
00
01
11
10
0
1

## Slide 104: Example
Give the Number of
  Implicants?
  Prime Implicants?
  Essential Prime Implicants?
x
1
x
2
x
3
1
1
1
1
0
0
1
0
00
01
11
10
0
1

## Slide 105: Why concerned with minimization?
Simplified function
Reduce the cost of the circuit
  Cost: Gates + Inputs
  Transistors

## Slide 106
[ Figure 2.56 from the textbook ]
Three-variable function f (x1, x2, x3) = ∑m(0, 1, 2, 3, 7)

## Slide 107: Example
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1

## Slide 108: Example
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1

## Slide 109: Example
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
3
x
4
x
2
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4

## Slide 110: Example
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
3
x
4
x
2
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4
x
1
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4
x
2
x
3
x
4
f =
+
+
+

## Slide 111: Example: Another Solution
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1

## Slide 112
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
Example: Another Solution
[ Figure 2.59 from the textbook ]

## Slide 113
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
2
x
4
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
3
Example: Another Solution

## Slide 114
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
2
x
4
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
3
Example: Another Solution
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
4
x
1
x
2
x
3
+
+
+
f =

## Slide 115
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
3
x
4
x
2
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4
x
1
x
2
x
4
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
3
Example: Both Are Valid Solutions
[ Figure 2.59 from the textbook ]

## Slide 116
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
00
01
11
10
1
1
x
1
x
3
x
4
x
2
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4
x
1
x
2
x
4
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
3
Example: Both Are Valid Solutions
x
1
x
2
x
4
x
1
x
2
x
3
x
1
x
2
x
4
x
1
x
2
x
3
+
+
+
f =
x
1
x
3
x
4
x
2
x
3
x
4
x
1
x
3
x
4
x
2
x
3
x
4
f =
+
+
+

## Slide 117: Minimization of Product-of-Sums Forms

## Slide 118: Do You Still Remember This Boolean Algebra Theorem?

## Slide 119: Let’s prove 14.b

## Slide 120: Let’s prove 14.b
0
1
1
1

## Slide 121: Let’s prove 14.b
0
1
1
1
1
0
1
1

## Slide 122: Let’s prove 14.b
0
1
1
1
1
0
1
1
0
0
1
1

## Slide 123: Let’s prove 14.b
0
1
1
1
1
0
1
1
0
0
1
1
0
0
1
1

## Slide 124: Let’s prove 14.b
0
1
1
1
1
0
1
1
0
0
1
1
0
0
1
1
They are equal.

## Slide 125: Grouping Example
x
2
0
1
0
1
0
1
1
1
x
1
x
2
0
1
0
1
1
0
1
1
x
1
M0
M2

## Slide 126: Grouping Example
x
2
0
1
0
1
0
1
1
1
x
1
x
2
0
1
0
1
1
0
1
1
x
1
M0
M2
x
2
0
1
0
1
0
0
1
1
x
1
M0 * M2
*
*
=
=

## Slide 127: Grouping Example
x
2
0
1
0
1
0
1
1
1
x
1
x
2
0
1
0
1
1
0
1
1
x
1
M0
M2
x
2
0
1
0
1
0
0
1
1
x
1
M0 * M2
*
*
=
=

## Slide 128: Grouping Example
x
2
0
1
0
1
0
1
1
1
x
1
x
2
0
1
0
1
1
0
1
1
x
1
M0
M2
x
2
0
1
0
1
0
0
1
1
x
1
M0 * M2
*
*
=
=

## Slide 129: Grouping Example
x
2
0
1
0
1
0
1
1
1
x
1
x
2
0
1
0
1
1
0
1
1
x
1
M0
M2
x
2
0
1
0
1
0
0
1
1
x
1
M0 * M2
*
*
=
=
*
( x1 + x2 )
( x1+ x2 )
=
x2
_
Property 14b (Combining)

## Slide 130: Expressions with three variables (for three-variable K-maps)

## Slide 131: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 1
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 0
 | 1 | 1 | 1 | 1 | 1
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )

## Slide 132: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 0 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1 | 0
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )

## Slide 133: Expressions with two variables (for three-variable K-maps)

## Slide 134: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 1
 | 1 | 0 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 1
 | 1 | 1 | 1 | 0 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 0
 | 1 | 1 | 1 | 1 | 0
( x1 + x2 )
( x1 + x2 )
( x1 + x2 )
( x1 + x2 )

## Slide 135: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 1 | 1 | 1 | 1
( x1 + x3 )
( x2 + x3 )
( x2 + x3 )
( x1 + x3 )

## Slide 136: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 0 | 0 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 1 | 1 | 0
( x1 + x3 )
( x2 + x3 )
( x2 + x3 )
( x1 + x3 )

## Slide 137: Expressions with one variable (for three-variable K-maps)

## Slide 138: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
( x1 )
( x2 )
( x2 )
( x1 )

## Slide 139: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
( x3 )
( x3 )

## Slide 140: Expressions with zero variables (for three-variable K-maps)

## Slide 141: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
0
1

## Slide 142: Some Examples

## Slide 143
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)

## Slide 144
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)
f (x1, x2, x3) = ( x1 + x3 ) ( x1 + x3 )

## Slide 145
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)

## Slide 146
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)
f (x1, x2, x3 , x4) = ( x3 + x4 ) ( x2 + x3 ) ( x1 + x2 + x3 + x4 )

## Slide 147: Questions?

## Slide 148: THE END