## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Incompletely Specified Functions &
Multiple-Output Circuits
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW4 is due on Monday Sep 22 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 4: Administrative Stuff
HW5 is due on Monday Sep 29 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 5: Administrative Stuff
Midterm Exam #1
When: Friday Sep 26.
What: Chapter 1 and Chapter 2 plus number systems
The exam will be closed book but open notes (you can bring up to 3 pages of handwritten notes).
It will be in this room.
Sample exams are posted on the class web page.

## Slide 6: Topics for the Midterm Exam
Binary Numbers
Octal Numbers
Hexadecimal Numbers
Conversion between the different number systems
Truth Tables
Boolean Algebra
Logic Gates
Circuit Synthesis with AND, OR, NOT
Circuit Synthesis with NAND, NOR
Converting an AND/OR/NOT circuit to NAND circuit
Converting an AND/OR/NOT circuit to NOR circuit
SOP and POS expressions

## Slide 7: Topics for the Midterm Exam
Mapping a Circuit to Verilog code
Mapping Verilog code to a circuit
Multiplexers
Venn Diagrams
K-maps for 2, 3, and 4 variables
Minimization of Boolean expressions using theorems
Minimization of Boolean expressions with K-maps
Incompletely specified functions (with don’t cares)
Functions with multiple outputs
Something from Star Wars

## Slide 8: One-Variable K-Map

## Slide 9: One-Variable K-map
(a) Truth table
(b) Karnaugh map
0
1
m
0
m
1
x
1
x
1
0
1
m
0
m
1
f

## Slide 10: One-Variable K-map
(a) Truth table
(b) Karnaugh map
0
1
1
0
x
1
x1
x
1
0
1
1
0
f

## Slide 11: Two-Variable K-Map

## Slide 12: Two-Variable K-map
x
2
(a) Truth table
(b) Karnaugh map
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
m
0
m
1
m
3
m
2
x
1
[ Figure 2.49 from the textbook ]

## Slide 13: These are all valid groupings
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
x
2
0
1
0
1
0
1
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
x1 x2
_
_
x1 x2
_
x1 x2
_
x1 x2

## Slide 14: These are all valid groupings
x
2
0
1
0
1
1
0
0
1
x
1
x
2
0
1
0
1
0
1
1
0
x
1
x
2
0
1
0
1
1
1
0
0
x
1
x
2
0
1
0
1
0
0
1
1
x
1
x1
_
x1
x2
_
x2

## Slide 15: This one is valid too
x
2
0
1
0
1
1
1
1
1
x
1
In this case the result is the constant function 1.

## Slide 16: Why are these two not valid?
x
2
0
1
0
1
1
0
1
0
x
1
x
2
0
1
0
1
0
1
0
1
x
1

## Slide 17: Minimization Example with a two-variable K-map
[ Figure 2.50 from the textbook ]
1

## Slide 18: Three-Variable K-Map

## Slide 19
Three-Variable K-map
[ Figure 2.51 from the textbook ]

## Slide 20
Location of three-variable minterms
Notice the placement of
  Variables
  Binary pair values
  Minterms

## Slide 21: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder

## Slide 22: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5

## Slide 23: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 0 | 0
Can’t group diagonally.

## Slide 24: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 1 | 1
Can’t group three in a row.
Each side must be a power of 2.

## Slide 25: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Can’t group zeros and ones together.

## Slide 26: Three-Variable K-map
[ Figure 2.52 from the textbook ]

## Slide 27: From Boolean Expression to K-map

## Slide 28: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | m0 | m2 | m6 | m4
 | 1 | m1 | m3 | m7 | m5
F = A C + A B + A B C

## Slide 29: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 |  |  |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 30: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 31: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 32: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 |  |  | 
F = A C + A B + A B C

## Slide 33: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 |  |  | 
F = A C + A B + A B C

## Slide 34: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 | 1 |  | 
F = A C + A B + A B C

## Slide 35: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C

## Slide 36: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C
A

## Slide 37: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C = A
A

## Slide 38: Different Ways to Draw the K-map

## Slide 39: Two Different Ways to Draw the K-map
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 40: Another Way to Draw 3-variable K-map
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 41: There are 4 different versions!
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m2 | m6 | m4
 | 1 | m1 | m3 | m7 | m5
 | x3 |  | 
x1x2 |  | 0 | 1
 | 00 | m0 | m1
 | 01 | m2 | m3
 | 11 | m6 | m7
 | 10 | m4 | m5
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 42: Why is it OK to combine a group of four ones?

## Slide 43: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Theorem 14a is behind the K-Map theory.
But that theorem is just for two variables.
Why is this grouping of four ones possible?

## Slide 44: The K-Map theory uses the combining theorems of Boolean algebra

## Slide 45: The K-Map theory uses the combining theorems of Boolean algebra
optimization by 1’s

## Slide 46: The K-Map theory uses the combining theorems of Boolean algebra
optimization by 0’s

## Slide 47: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0

## Slide 48: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 49: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z
_ _
( x y + x y ) z
_
( x y + x y ) z

## Slide 50: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = (x y + x y) z + (x y + x y) z

## Slide 51: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = (x y + x y) z + (x y + x y) z
_
y z (by 14a)
y z (by 14a)

## Slide 52: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = y z + y z

## Slide 53: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = y z + y z
y (by 14a)

## Slide 54: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
f = y

## Slide 55: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Answer: We can combine them because Theorem 14a
is applied three times, not just once.

## Slide 56: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0

## Slide 57: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 58: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 59: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z
_ _
x ( y z + y z )
_
x ( y z + y z )

## Slide 60: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = x (y z + y z) + x (y z + y z)

## Slide 61: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = x (y z + y z) + x (y z + y z)
_
x y (by 14a)
x y (by 14a)

## Slide 62: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = x y + x y

## Slide 63: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = x y + x y
y (by 14a)

## Slide 64: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
f = y

## Slide 65: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Answer: We can combine them because Theorem 14a
is applied three times, not just once.

## Slide 66: Four-Variable K-Map

## Slide 67
[ Figure 2.53 from the textbook ]
A four-variable Karnaugh map

## Slide 68
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 69
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map

## Slide 70
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map
0000
0100
1100
1000
0001
0101
1101
1001
0011
0111
1111
1011
0010
0110
1110
1010

## Slide 71: Adjacency Rules
adjacent
columns
adjacent
columns
adjacent
rows

## Slide 72: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus

## Slide 73: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 74: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 75
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 76
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 77
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 78
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 79
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 80
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 81: Other Four-Variable K-map Examples
[ Figure 2.54 from the textbook ]

## Slide 82: POS Minimization

## Slide 83
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)

## Slide 84
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)
f (x1, x2, x3) = ( x1 + x3 ) ( x1 + x2 )

## Slide 85
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)

## Slide 86
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)
f (x1, x2, x3 , x4) = ( x3 + x4 ) ( x2 + x3 ) ( x1 + x2 + x3 + x4 )

## Slide 87: Example: Incompletely Specified Function

## Slide 88: Three Ways to Specify the Function
f(x1, x2, x3, x4) = Σ m(2, 4, 5, 6, 10) + D(12, 13, 14, 15)

## Slide 89: Three Ways to Specify the Function
f(x1, x2, x3, x4) = Σ m(2, 4, 5, 6, 10) + D(12, 13, 14, 15)
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
0
0
1
0
1
1
1
0
0
1
0
d
d
d
d

## Slide 90: SOP implementation
x
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
x
2
x
3
x
3
4
(a) SOP implementation
[ Figure 2.62 from the textbook ]

## Slide 91: POS implementation
x
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
x
2
x
3
+
(
)
3
x
4
+
(
)
(b) POS implementation
[ Figure 2.62 from the textbook ]

## Slide 92: Example: A circuit with multiple outputs

## Slide 93: Seven-Segment Indicator

## Slide 94: Seven-Segment Indicator

## Slide 95: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1

## Slide 96: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d

## Slide 97: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d

## Slide 98: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
00
01
11
10
00
01
11
10

## Slide 99: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
1
d
1
1
1
d
d
1
1
d
d
00
01
11
10

## Slide 100: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
1
d
1
1
1
d
d
1
1
d
d
00
01
11
10

## Slide 101: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
1
1
0
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
In this case all d's were treated as 1's.

## Slide 102: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d

## Slide 103: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
00
01
11
10
00
01
11
10

## Slide 104: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
0
d
0
0
0
d
d
1
1
d
d
00
01
11
10

## Slide 105: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
0
d
0
0
0
d
d
1
1
d
d
00
01
11
10

## Slide 106: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d 1 d d
1 d d d 0 d d 1 d d d 0 d d
1 d d d 0 d d 1 d d d 1 d d
1 d d d 0 d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
0
1
0
0
0
0
0
0
0
0
1
1
1
1
00
01
11
10
In this case some d's were treated as 1's, others as 0's.

## Slide 107: Seven-Segment Indicator

## Slide 108: Another Example

## Slide 109
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
[ Figure 2.64 from the textbook ]

## Slide 110
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2

## Slide 111
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_

## Slide 112
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_

## Slide 113
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_

## Slide 114
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_

## Slide 115
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_
x1 x3
_

## Slide 116
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 117
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 118
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 119
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 120
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 121
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 122
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
[ Figure 2.64 from the textbook ]

## Slide 123: Individual vs Joint Optimization

## Slide 124: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 125: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 126: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 127: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
cost = 14
cost = 15

## Slide 128: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
cost = 14
cost = 15
TOTAL cost: 29

## Slide 130: Individual vs Joint Optimization
[ Figure 2.65 from the textbook ]
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
(b) Optimal realization of
1
f
3
f
4
(c) Optimal realization of
f
3
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
Individual
Joint

## Slide 131: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2

## Slide 132: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
shared gate

## Slide 133: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
another shared gate

## Slide 134: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
cost = 23

## Slide 135: Questions?

## Slide 136: THE END