## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Multiplication
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
No HW is due today
HW 6 is due on Monday Oct. 13 @ 10 pm.
Posted on the class web page.

## Slide 4: Administrative Stuff
Labs this week
Mini-Project
This is worth 3% of your grade (x2 labs)
https://www.ece.iastate.edu/~alexs/classes/ 2025_Fall_2810/labs/Project-Mini/

## Slide 5: Multiplication and division by 10 in the decimal system

## Slide 6: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = ?
542 x 10 = ?
1245 x 10 = ?

## Slide 7: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = 40
542 x 10 = 5420
1245 x 10 = 12450

## Slide 8: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = 40
542 x 10 = 5420
1245 x 10 = 12450
You simply add a zero as the rightmost number

## Slide 9: Decimal Division by 10
What happens when we divide a number by 10?
  14 / 10 = ?
540 / 10 = ?
1240 / 10 = ?

## Slide 10: Decimal Division by 10
What happens when we divide a number by 10?
  14 / 10 = 1 //integer division
540 / 10 = 54
1240 / 10 = 124
You simply delete the rightmost number

## Slide 11: Multiplication and division by 2 in the binary system

## Slide 12: Binary Multiplication by 2
What happens when we multiply a number by 2?
  011 times 2 = ?
101 times 2 = ?
110011 times 2 = ?

## Slide 13: Binary Multiplication by 2
What happens when we multiply a number by 2?
  011 times 2 = 0110
101 times 2 = 1010
110011 times 2 = 1100110
You simply add a zero as the rightmost number

## Slide 14: Binary Multiplication by 4
What happens when we multiply a number by 4?
  011 times 4 = ?
101 times 4 = ?
110011 times 4 = ?

## Slide 15: Binary Multiplication by 4
What happens when we multiply a number by 4?
  011 times 4 = 01100
101 times 4 = 10100
110011 times 4 = 11001100
add two zeros in the last two bits and shift everything else to the left

## Slide 16: Binary Multiplication by 2N
What happens when we multiply a number by 2N?
  011 times 2N = 01100…0 // add N zeros
  101 times 4 = 10100…0 // add N zeros
  110011 times 4 = 11001100…0 // add N zeros

## Slide 17: Binary Division by 2
What happens when we divide a number by 2?
  0110 divided by 2 = ?
1010 divides by 2 = ?
110011 divides by 2 = ?

## Slide 18: Binary Division by 2
What happens when we divide a number by 2?
  0110 divided by 2 = 011
1010 divides by 2 = 101
110011 divides by 2 = 11001
You simply delete the rightmost number

## Slide 19: Multiplication of two unsigned binary numbers

## Slide 20: Decimal Multiplication By Hand
[http://www.ducksters.com/kidsmath/long_multiplication.php]

## Slide 21: Binary Multiplication By Hand
[Figure 3.34a from the textbook]

## Slide 22: Binary Multiplication By Hand
[Figure 3.34b from the textbook]

## Slide 23: Binary Multiplication By Hand
[Figure 3.34c from the textbook]

## Slide 24
Figure 3.35. A 4x4 multiplier circuit.

## Slide 25
Figure 3.35. A 4x4 multiplier circuit.

## Slide 26: Sign Extension

## Slide 27: Sign extension for positive numbers
If we want to represent the same positive number with more bits, we simply pad it on the left with zeros.
For example:
0110 (+6 with 4-bits)
00110 (+6 with 5-bits)
000110 (+6 with 6-bits)

## Slide 28: Sign extension for negative numbers
If we want to represent the same negative number with more bits, we simply pad it on the left with ones.
For example:
1011 (-5 with 4-bits)
11011 (-5 with 5-bits)
111011 (-5 with 6-bits)

## Slide 29: Multiplication of two signed binary numbers

## Slide 30: Positive Multiplicand Example
[Figure 3.36a in the textbook]

## Slide 31: Positive Multiplicand Example
[Figure 3.36a in the textbook]
add an extra bit
to avoid overflow

## Slide 32: Negative Multiplicand Example
[Figure 3.36b in the textbook]

## Slide 33: Negative Multiplicand Example
[Figure 3.36b in the textbook]
add an extra bit
to avoid overflow
but now it is 1

## Slide 34: What if the Multiplier is Negative?
Negate both numbers.
This will make the multiplier positive.
Then proceed as normal.
This will not affect the result.
Example: 5*(- 4) = (- 5)*(4)= - 20

## Slide 35: Arithmetic Comparison Circuits

## Slide 36
Truth table for a one-bit digital comparator
[http://en.wikipedia.org/wiki/Digital_comparator]

## Slide 37
[http://www.personal.psu.edu/users///c/w/cwb5096/Old%20Site/index_files/cmpenlab4.htm]
A one-bit digital comparator circuit

## Slide 38
Truth table for a two-bit digital comparator
[http://en.wikipedia.org/wiki/Digital_comparator]

## Slide 39
[http://forum.allaboutcircuits.com/showthread.php?t=10561]
A two-bit digital comparator circuit

## Slide 40
[ Figure 4.22 from the textbook ]
A four-bit comparator circuit

## Slide 41
[ Figure 3.45 from the textbook ]
Another four-bit comparator circuit

## Slide 42
[ Figure 3.45 from the textbook ]
Another four-bit comparator circuit

## Slide 43
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
Compare 6 with 5 by subtraction (6-5).

## Slide 44
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0

## Slide 45
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
0 1 1 0
1 0 1 0
1 0 0 0 1
+
1

## Slide 46
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
0 1 1 0
1 0 1 0
1 0 0 0 1
+
1
Ignore

## Slide 47
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
1
. . . 1
0 1 1 0
1 0 1 0
1 0 0 0 1
+

## Slide 48
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
1
. . . 1
0 1 1 0
1 0 1 0
1 0 0 0 1
+

## Slide 49: Binary Coded Decimal (BCD)

## Slide 50
Table of Binary-Coded Decimal Digits

## Slide 51: Addition of BCD digits
[Figure 3.38a in the textbook]

## Slide 52: Addition of BCD digits
[Figure 3.38a in the textbook]
The result is greater than 9, which is not a valid BCD number

## Slide 53: Addition of BCD digits
[Figure 3.38a in the textbook]
add 6

## Slide 54: Addition of BCD digits
[Figure 3.38b in the textbook]

## Slide 55: Addition of BCD digits
[Figure 3.38b in the textbook]
The result is 1, but it should be 7

## Slide 56: Addition of BCD digits
[Figure 3.38b in the textbook]
add 6

## Slide 57: Why add 6?
Think of BCD addition as a mod 16 operation
Decimal addition is mod 10 operation

## Slide 58: BCD Arithmetic Rules
Z = X + Y
If Z <= 9, then S=Z and carry-out = 0
If Z > 9, then S=Z+6 and carry-out =1

## Slide 59
Block diagram for a one-digit BCD adder
[Figure 3.39 in the textbook]

## Slide 60: How to check if the number is > 9?
7 - 0111
8 - 1000
9 - 1001
10 - 1010
11 - 1011
12 - 1100
13 - 1101
14 - 1110
15 - 1111

## Slide 61
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 62
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 63
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
f = z3z2 + z3z1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 64
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
f = z3z2 + z3z1
In addition, also check if there was a carry
f = carry-out + z3z2 + z3z1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 65
module
bcdadd(Cin,
X,
Y,
S, Cout);
input
Cin;
input
[3:0] X,
Y;
output
reg [3:0] S;
output
reg Cout;
reg
[4:0] Z;
always
@ (X,
Y,
Cin)
begin
Z
=
X
+
Y
+
Cin;
if
(Z
<
10)
{Cout,
S}
=
Z;
else
{Cout,
S}
=
Z
+
6;
end
endmodule
Verilog code for a one-digit BCD adder
[Figure 3.40 in the textbook]

## Slide 66
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder

## Slide 67
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
carry-out + z3z2 + z3z1

## Slide 68
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1

## Slide 69
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1

## Slide 70
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0

## Slide 71
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
add 6
implicit 0

## Slide 72
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?

## Slide 73
c
i
x
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
[ Figure 3.4b from the textbook ]

## Slide 74
c
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
0

## Slide 75
c
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
0
0
0

## Slide 76
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
0

## Slide 77
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
0
y
i

## Slide 78
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i

## Slide 79
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
It reduces to a half-adder.

## Slide 80
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
But if we only need the sum bit …

## Slide 81
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
s
i
… it reduces to an XOR.

## Slide 82
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
z3 z2 z1 z0

## Slide 83
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
z3 z2 z1 z0

## Slide 84
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
implicit 0
z3 z2 z1 z0

## Slide 85
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
carry 3
z3
c3
z3 z2 z1 z0

## Slide 86
Block diagram for a one-digit BCD adder
[Figure 3.39 in the textbook]

## Slide 87
Block diagram for a one-digit BCD adder
[Figure 3.39 in the textbook]
We can get by with a 2-bit adder and one XOR gate.

## Slide 88
Block diagram for a one-digit BCD adder
[Figure 3.39 in the textbook]
This bus mux is not needed. It reduces to 2 wires that carry the adjust signal and feed into the 2-bit adder.

## Slide 89
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
0
z3 z2 z1 z0
This is the bus mux!
If adjust is equal to one it outputs +6, i.e., 11 (with an implicit zero).
adjust

## Slide 90
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
0
0
0
0
z3 z2 z1 z0
This is the bus mux!
If adjust is equal to zero it outputs 0, i.e., 00 (with an implicit zero).
adjust

## Slide 91: Questions?

## Slide 92: THE END