## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Floating Point Numbers
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW 6 is out
It is due on Monday Oct 13 @ 10pm.

## Slide 4: More Details on Comparison Circuits

## Slide 5: Comparison of 1-bit numbers

## Slide 6: Equal
x | y | x = y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: Equal
x | y | x = y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x
y
x = y

## Slide 8: Not Equal
x | y | x != y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: Not Equal
x | y | x != y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x
y
x != y

## Slide 10: Less
x | y | x < y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x
y

## Slide 11: Less or Equal
x | y | x <= y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x
y

## Slide 12: Less or Equal
x | y | x < y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | x = y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x <= y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
or
=

## Slide 13: Greater
x | y | x > y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x
y

## Slide 14: Greater or Equal
x | y | x >= y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x
y

## Slide 15: Greater or Equal
x | y | x > y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | x = y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x >= y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
or
=

## Slide 16: Some Interesting Dualities

## Slide 17: Equal
x | y | x = y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x != y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Not Equal

## Slide 18: Greater
x | y | x > y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | x <= y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Less or Equal

## Slide 19: Greater or Equal
x | y | x >= y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | x < y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Less

## Slide 20: Some Interesting Dualities
Equal = Not Equal
Greater = Less or Equal
Less = Greater or Equal

## Slide 21: Example: The i281 CPU architecture

## Slide 22: Comparison of n-bit signed numbers (stored in 2’s complement representation)

## Slide 23: Comparison of n-bit signed numbers (stored in 2’s complement representation)
The comparison is done with subtraction and then looking at the flags.

## Slide 24: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)

## Slide 25
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The Flags Register

## Slide 26
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The Flags Register
CF OF NF ZF

## Slide 27
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The Arithmetic Logic Unit
(ALU)

## Slide 28
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
These two control inputs determine
the type of arithmetic operation

## Slide 29: This ALU Can Perform 4 Operations
ALU_SELECT1 | ALU_SELECT0 | Operation
0 | 0 | SHIFTL
0 | 1 | SHIFTR
1 | 0 | ADD
1 | 1 | SUB/CMP
i281 CPU

## Slide 30: This ALU Can Perform 4 Operations
ALU_SELECT1 | ALU_SELECT0 | Operation
0 | 0 | SHIFTL
0 | 1 | SHIFTR
1 | 0 | ADD
1 | 1 | SUB/CMP
C12
C13
Names of these
control lines
i281 CPU

## Slide 31: This ALU Can Perform 4 Operations
ALU_SELECT1 | ALU_SELECT0 | Operation
0 | 0 | SHIFTL
0 | 1 | SHIFTR
1 | 0 | ADD
1 | 1 | SUB/CMP
C12
C13
Both SUB and CMP are implemented
as subtraction. They both set the flags.
The difference is that CMP does not write
back the result of the subtraction to the registers.
Only the side effect through the flags remains.
i281 CPU

## Slide 32
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The Arithmetic Logic Unit
(ALU)

## Slide 33: The ALU
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
i281 CPU

## Slide 34: The Adder / Subtractor
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
i281 CPU

## Slide 35: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
add / sub
This is an 8-bit ripple-carry adder. Note that the X and Y lines are swapped.
i281 CPU

## Slide 36: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
i281 CPU

## Slide 37: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
negative
zero
negative and zero can be
computed here as well
i281 CPU

## Slide 38: The ALU Flag Calculator
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
i281 CPU

## Slide 39: The ALU Flag Calculator
I0
I1
I2
I3
I4
I5
I6
I7
negative
zero
i281 CPU

## Slide 40: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)

## Slide 41: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)
In some CPU architectures the carry flag
means borrow. And it could be inverted
relative to the previous diagram.

## Slide 42: Comparison of Signed Numbers
Equal ZF = 1
Not equal ZF = 0
Greater ZF = 0 and NF = OF
Greater or Equal NF = OF
Less NF != OF
Less or Equal ZF = 1 or NF != OF

## Slide 43: Comparison of Signed Numbers
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 44: These 7 Instructions Update the Flags
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 45
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
Flags Write Enable

## Slide 46: These 7 Instructions Use the Flags
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 47
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
PC Mux

## Slide 48
JUMP * 1
BRE * B1
BRNE * B2
BRG * B3
BRGE * B4
i281 CPU

## Slide 49: Comparison of Signed Numbers
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 50: Comparison of Signed Numbers
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )
B1
B2
B3
B4

## Slide 51: Comparison of Signed Numbers
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )
The i281 CPU does not implement these checks. Instead, it relies on
the programmer/compiler to rearrange the code to use the other checks.

## Slide 52: Comparison examples with 4-bit signed numbers

## Slide 53
[ Figure 3.45 from the textbook ]
A four-bit comparator circuit

## Slide 54
[ Figure 3.45 from the textbook ]
A four-bit comparator circuit
This circuit only subtracts.
That is why these are NOTs instead of XORs.

## Slide 55
A four-bit comparator circuit
OF
NF
ZF
alternative names
for the flags

## Slide 56
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
Compare 6 with 5: (+6) - (+5)

## Slide 57
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )
Compare 6 with 5: (+6) - (+5)

## Slide 58
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
Equal 0
Not equal 0
Greater 0 • XNOR( 0, 0 )
Greater or Equal XNOR( 0, 0 )
Less XOR( 0, 0 )
Less or Equal 0 + XOR( 0, 0 )
Compare 6 with 5: (+6) - (+5)

## Slide 59
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
Equal 0
Not equal 1
Greater 1
Greater or Equal 1
Less 0
Less or Equal 0
Compare 6 with 5: (+6) - (+5)

## Slide 61
Compare negative 2 with 3: (-2) - (+3)
1
0
1
0
1
1
0
1
1
1
1
1
1
0
0
0
1
0
1
1
1
1
0
0
0
1
0
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 62
1
0
1
0
1
1
0
1
1
1
1
1
1
0
0
0
1
0
1
1
1
1
0
0
0
1
0
Equal 0
Not equal 0
Greater 0 • XNOR( 1, 0 )
Greater or Equal XNOR( 1, 0 )
Less XOR( 1, 0 )
Less or Equal 0 + XOR( 1, 0 )
Compare negative 2 with 3: (-2) - (+3)

## Slide 63
1
0
1
0
1
1
0
1
1
1
1
1
1
0
0
0
1
0
1
1
1
1
0
0
0
1
0
Equal 0
Not equal 1
Greater 0
Greater or Equal 0
Less 1
Less or Equal 1
Compare negative 2 with 3: (-2) - (+3)

## Slide 65
Compare 1 with negative 7: (+1) - (-7)
0
1
0
0
0
0
1
1
0
0
0
1
0
1
1
0
1
0
0
0
0
1
1
1
1
1
0
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 66
Compare 1 with negative 7: (+1) - (-7)
0
1
0
0
0
0
1
1
0
0
0
1
0
1
1
0
1
0
0
0
0
1
1
1
1
1
0
Equal 0
Not equal 0
Greater 0 • XNOR( 1, 1 )
Greater or Equal XNOR( 1, 1 )
Less XOR( 1, 1 )
Less or Equal 0 + XOR( 1, 1 )

## Slide 67
Compare 1 with negative 7: (+1) - (-7)
0
1
0
0
0
0
1
1
0
0
0
1
0
1
1
0
1
0
0
0
0
1
1
1
1
1
0
Equal 0
Not equal 1
Greater 1
Greater or Equal 1
Less 0
Less or Equal 0

## Slide 69
Compare 3 with 3: (+3) - (+3)
0
0
0
0
1
1
1
1
0
1
0
1
1
0
1
0
0
0
0
0
1
1
1
1
0
0
1
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 70
Compare 3 with 3: (+3) - (+3)
0
0
0
0
1
1
1
1
0
1
0
1
1
0
1
0
0
0
0
0
1
1
1
1
0
0
1
Equal 1
Not equal 1
Greater 1 • XNOR( 0, 0 )
Greater or Equal XNOR( 0, 0 )
Less XOR( 0, 0 )
Less or Equal 1 + XOR( 0, 0 )

## Slide 71
Compare 3 with 3: (+3) - (+3)
0
0
0
0
1
1
1
1
0
1
0
1
1
0
1
0
0
0
0
0
1
1
1
1
0
0
1
Equal 1
Not equal 0
Greater 0
Greater or Equal 1
Less 0
Less or Equal 1

## Slide 72: Comparison of Unsigned Numbers
(not supported by the i281 CPU)

## Slide 73: Comparison of Unsigned Numbers
Also done with subtraction and then looking at the flags,
but the logic expressions are now different.

## Slide 74
[ Figure 3.45 from the textbook ]
A four-bit comparator circuit

## Slide 75
A four-bit comparator circuit
C
(carry)

## Slide 76
A four-bit comparator circuit
C
(carry)
CF
OF
NF
ZF
alternative names
for the flags

## Slide 77: Comparison of Unsigned Numbers
Equal
Not equal
Greater
Greater or Equal
Less
Less or Equal

## Slide 78: Comparison of Unsigned Numbers
Equal
Not equal
Greater / Above
Greater or Equal / Above or Equal
Less / Below
Less or Equal / Below or Equal

## Slide 79: Comparison of Unsigned Numbers
Equal ZF = 1
Not equal ZF = 0
Greater ZF = 0 and CF = 1
Greater or Equal CF = 1
Less CF = 0
Less or Equal ZF = 1 or CF = 0

## Slide 80: Comparison of Unsigned Numbers
Equal ZF
Not equal ZF
Greater ZF • CF
Greater or Equal CF
Less CF
Less or Equal ZF + CF

## Slide 81: Comparison of Unsigned Numbers
Equal ZF
Not equal ZF
Above ZF • CF
Above or Equal CF
Below CF
Below or Equal ZF + CF

## Slide 82: Floating Point Numbers

## Slide 83: The story with floats is more complicated IEEE 754-1985 Standard
[http://en.wikipedia.org/wiki/IEEE_754]

## Slide 84
In the example shown above, the sign bit is zero, the exponent is 124, and the significand is 1.01 (in binary, which is 1.25 in decimal). The represented number is
(-1)0 × 2(124 - 127) × 1.25 = +0.15625.
[http://en.wikipedia.org/wiki/IEEE_754]

## Slide 85
[Figure 3.37 from the textbook]
Sign
32 bits
23 bits of mantissa
excess-127
exponent
8-bit
52 bits of mantissa
11-bit excess-1023
exponent
64 bits
Sign
S
M
S
M
(a) Single precision
(b) Double precision
E
+
E
0 denotes
–
1 denotes
Float (32-bit) vs. Double (64-bit)

## Slide 86: On-line IEEE 754 Converter
https://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 87: Representing 2.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 88: Representing 2.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 89: Representing 2.0
128
0
0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 90: Representing 2.0
2(128-127)
(-1)0
(1 + 0)
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 91: Representing 2.0
2(128-127)
(-1)0
(1 + 0)
×
×
= 2.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 92: Representing 2.0
21
1.0
1
×
×
= 2.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 94: Representing 4.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 95: Representing 4.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 96: Representing 4.0
129
0
0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 97: Representing 4.0
2(129-127)
(-1)0
(1 + 0)
×
×
= 4.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 98: Representing 4.0
22
1.0
1
×
×
= 4.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 100: Representing 8.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 101: Representing 16.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 102: Representing -16.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 103: Representing 1.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 104: Representing 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 105: Representing 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .

## Slide 106: Representing 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .
. . .

## Slide 107: Representing 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .
= 0.5

## Slide 108: Representing 3.0
128
0
0.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 109: Representing 3.0
2(128-127)
(-1)0
(1 + 0.5)
×
×
= 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 110: Representing 3.0
2(128-127)
(-1)0
(1 + 0.5)
×
×
= 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
This 1 is given to you for free.
It is part of the formula/standard.

## Slide 111: Representing 3.0
21
1.5
1
×
×
= 3.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 113: Representing 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 114: Representing 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .

## Slide 115: Representing 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .
= 0.5

## Slide 116: Representing 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
2-1
2-2
2-3
2-23
. . .
= 0.25

## Slide 117: Representing 3.5
128
0
0.5 + 0.25
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 118: Representing 3.5
2(128-127)
(-1)0
(1 + 0.5 + 0.25)
×
×
= 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 119: Representing 3.5
2(128-127)
(-1)0
(1 + 0.5 + 0.25)
×
×
= 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]
This 1 is given to you for free.
It is part of the formula/standard.

## Slide 120: Representing 3.5
21
1.75
1
×
×
= 3.5
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 122: Representing 5.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 123: Representing 6.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 124: Representing -7.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 125: Representing 0.8
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 126: Representing 0.8
This decimal number cannot be stored perfectly in this format!
The bits in the mantissa are periodic and will extend to infinity.
Think of storing 1/3 = 0.33333(3) with fixed number of decimal digits.
This is similar: 0.810 has no finite representation in IEEE 754.

## Slide 127: Representing 0.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 128: Representing -0.0
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 129: Representing +Infinity
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 130: Representing -Infinity
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 131: Representing NaN
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 132: Representing NaN
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 133: Representing NaN
[https://www.h-schmidt.net/FloatConverter/IEEE754.html]

## Slide 134
[http://babbage.cs.qc.cuny.edu/IEEE-754.old/References.xhtml]

## Slide 135
[Figure 3.37 from the textbook]
Sign
32 bits
23 bits of mantissa
excess-127
exponent
8-bit
52 bits of mantissa
11-bit excess-1023
exponent
64 bits
Sign
S
M
S
M
(a) Single precision
(b) Double precision
E
+
E
0 denotes
–
1 denotes
Float (32-bit) vs. Double (64-bit)

## Slide 136: Sample Midterm2 Problem

## Slide 137: Sample Midterm2 Problem

## Slide 138: Sample Midterm2 Problem

## Slide 139: Sample Midterm2 Problem

## Slide 140: Some Issues When Storing Double Numbers

## Slide 141: Memory Analogy
Address 0
Address 1
Address 2
Address 3
Address 4
Address 5
Address 6

## Slide 142: Memory Analogy (32 bit architecture)
Address 0
Address 4
Address 8
Address 12
Address 16
Address 20
Address 24

## Slide 143: Memory Analogy (32 bit architecture)
Address 0x00
Address 0x04
Address 0x08
Address 0x0C
Address 0x10
Address 0x14
Address 0x18
Hexadecimal
Address 0x0A
Address 0x0D

## Slide 144: Storing a Double
Address 0x08
Address 0x0C

## Slide 145: Storing 3.14
3.14 in binary IEEE-754 double precision (64 bits)
sign exponent mantissa
0 10000000000 1001000111101011100001010001111010111000010100011111
In hexadecimal this is (hint: groups of four):
0100 0000 0000 1001 0001 1110 1011 1000 0101 0001 1110 1011 1000 0101 0001 1111
4 0 0 9 1 E B 8 5 1 E B 8 5 1 F

## Slide 146: Storing 3.14
So 3.14 in hexadecimal IEEE-754 is 40091EB851EB851F
This is 64 bits.
On a 32 bit architecture there are 2 ways to store this
Small address: 40091EB8 51EB851F
Large address: 51EB851F 40091EB8
Big-Endian
Little-Endian
Motorola 6800
Intel x86
Example CPUs:

## Slide 147: Storing 3.14
Address 0x08
Address 0x0C
40 09 1E B8
51 EB 85 1F
Address 0x08
Address 0x0C
40 09 1E B8
51 EB 85 1F
Big-Endian
Little-Endian

## Slide 148: Storing 3.14 on a Little-Endian Machine (these are the actual bits that are stored)
Address 0x08
Address 0x0C
01010001 11101011 10000101 00011111
01000000 00001001 00011110 10111000
Once again, 3.14 in IEEE-754 double precision is:
sign exponent mantissa
0 10000000000 1001000111101011100001010001111010111000010100011111

## Slide 149: They are stored in binary (the hexadecimals are just for visualization)
Address 0x08
Address 0x0C
4 0 0 9 1 E B 8
5 1 E B 8 5 1 F
01010001 11101011 10000101 00011111
01000000 00001001 00011110 10111000

## Slide 150: Big-Endian
(8-bit architecture)
(16-bit architecture)
http://en.wikipedia.org/wiki/Endianness

## Slide 151: Little Endian
http://en.wikipedia.org/wiki/Endianness
(8-bit architecture)
(16-bit architecture)

## Slide 152: Big-Endian/Little-Endian analogy
[image fom http://www.simplylockers.co.uk/images/PLowLocker.gif]

## Slide 153: Big-Endian/Little-Endian analogy
[image fom http://www.simplylockers.co.uk/images/PLowLocker.gif]

## Slide 154: Big-Endian/Little-Endian analogy
[image fom http://www.simplylockers.co.uk/images/PLowLocker.gif]

## Slide 155: What would be printed? (don’t try this at home)
double pi = 3.14;
printf(“%d”,pi);
Result: 1374389535
Why?
  3.14 = 40091EB851EB851F (in double format)
  Stored on a little-endian 32-bit architecture
    51EB851F (1374389535 in decimal)
    40091EB8 (1074339512 in decimal)

## Slide 156: What would be printed? (don’t try this at home)
double pi = 3.14;
printf(“%d %d”, pi);
Result: 1374389535 1074339512
Why?
  3.14 = 40091EB851EB851F (in double format)
  Stored on a little-endian 32-bit architecture
    51EB851F (1374389535 in decimal)
    40091EB8 (1074339512 in decimal)
    The second %d uses the extra bytes of pi that were not printed by the first %d

## Slide 157: What would be printed? (don’t try this at home)
double a = 2.0;
printf(“%d”,a);
Result: 0
Why?
  2.0 = 40000000 00000000 (in hex IEEE double format)
  Stored on a little-endian 32-bit architecture
    00000000 (0 in decimal)
    40000000 (1073741824 in decimal)

## Slide 158: What would be printed? (an even more advanced example)
int a[2]; // defines an int array
a[0]=0;
a[1]=0;
scanf(“%lf”, &a[0]); // read 64 bits into 32 bits
// The user enters 3.14
printf(“%d %d”, a[0], a[1]);
Result: 1374389535 1074339512
Why?
  3.14 = 40091EB851EB851F (in double format)
  Stored on a little-endian 32-bit architecture
    51EB851F (1374389535 in decimal)
    40091EB8 (1074339512 in decimal)
  The double 3.14 requires 64 bits which are stored in the two consecutive 32-bit integers named a[0] and a[1]

## Slide 159: Questions?

## Slide 160: THE END