## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Decoders and Encoders
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW6 is due today
HW7 is out. It is due on Monday Oct 20 @ 10pm.

## Slide 4
Quick Review

## Slide 5: Graphical Symbol for a 2-1 Multiplexer
f
s
x
1
x
2
0
1
[ Figure 2.33c from the textbook ]

## Slide 6: Circuit for 2-1 Multiplexer
f
x
1
x
2
s
f
s
x
1
x
2
0
1
(c) Graphical symbol
(b) Circuit
[ Figure 2.33b-c from the textbook ]
f (s, x1, x2) =
s x1
s x2
+

## Slide 7
0
w
0
w
1
0
1
w
2
w
3
0
1
f
0
1
s
1
s
Using three 2-to-1 multiplexers
to build one 4-to-1 multiplexer
[ Figure 4.3 from the textbook ]

## Slide 8: Graphical Symbol and Truth Table
[ Figure 4.2a-b from the textbook ]

## Slide 9
4-to-1 Multiplexer (SOP circuit)
[ Figure 4.2c from the textbook ]
f = s1 s0 w0 + s1 s0 w1 + s1 s0 w2 + s1 s0 w3

## Slide 10
4-to-1 Multiplexer (SOP circuit)
f = s1 s0 w0 + s1 s0 w1 + s1 s0 w2 + s1 s0 w3
these are the four minterms in terms of s1 and s2

## Slide 11
4-to-1 Multiplexer (SOP circuit)
f = s1 s0 w0 + s1 s0 w1 + s1 s0 w2 + s1 s0 w3
these are the four w inputs to the 4-to-1 MUX

## Slide 12
16-1 Multiplexer with 4-to-1 Multiplexers
s
1
w0
w1
w2
w3
s
0
s
3
s
2
f
w4
w5
w6
w7
w8
w9
w10
w11
w12
w13
w14
w15
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11

## Slide 13: Shannon’s Expansion Theorem (general case with one select variable)

## Slide 14
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
This form is suitable for implementation with a 2-to-1 multiplexer.

## Slide 15
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
w1 set to 0

## Slide 16
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
w1 set to 1

## Slide 17
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:

## Slide 18
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:

## Slide 19
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
select variable
(negated)

## Slide 20
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
select variable
(not negated)

## Slide 21
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
cofactor

## Slide 22
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
cofactor

## Slide 23
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
f
w
1
0
1

## Slide 24
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
f
w
1
0
1
f0
f1

## Slide 25
Shannon’s Expansion Theorem
Any Boolean function can be rewritten in the form:
f
w
1
0
1
f0
f1

## Slide 26: Shannon’s Expansion Theorem (example with only one select variable) (used for 2-to-1 mux implementation)

## Slide 27
Shannon’s Expansion Theorem Example

## Slide 28
set w1 = 0
Shannon’s Expansion Theorem Example

## Slide 29
set w1 = 0
0 •
0 •
0
w1
w2 w3
Shannon’s Expansion Theorem Example

## Slide 30
set w1 = 1
Shannon’s Expansion Theorem Example

## Slide 31
set w1 = 1
1 •
1 •
1
w1
w2 + w3
Shannon’s Expansion Theorem Example

## Slide 32
Shannon’s Expansion Theorem Example
started with this

## Slide 33
Shannon’s Expansion Theorem Example
factored it in this form

## Slide 34
Shannon’s Expansion Theorem Example
which fits the general formula

## Slide 35
f
w
3
w
1
w
2
0
1
Shannon’s Expansion Theorem Example

## Slide 36
f
w
3
w
1
w
2
0
1
Shannon’s Expansion Theorem Example

## Slide 37
f
w
3
w
1
w
2
0
1
Shannon’s Expansion Theorem Example

## Slide 38
0
0
0
1
1
0
1
1
0
0
0
1
0
0
0
1
1
0
1
1
0
1
1
1
w
1
w
2
w
3
f
0
0
0
0
1
1
1
1
0
1
f
w
1
Earlier we derived the same result from the truth table using the divide-and-conquer method (a.k.a., Shannon’s theorem)
[ Figure 4.10a from the textbook ]
w
2
w
3
w
2
w
3
+
(b) Circuit
(b) Truth table
f
w
3
w
1
w
2
0
1

## Slide 39: Shannon’s Expansion Theorem (general case with two select variables)

## Slide 40
Shannon’s Expansion Theorem
(In terms of more than one variable)
This form is suitable for implementation with a 4-to-1 multiplexer.

## Slide 41
Shannon’s Expansion Theorem
(In terms of more than one variable)
These are the four possible minterms with two variables.

## Slide 42
Shannon’s Expansion Theorem
(In terms of more than one variable)
These are the four cofactors, one for each of the minterms.

## Slide 43
Shannon’s Expansion Theorem
(In terms of more than one variable)
f
w
1
f00
f01
w
2
f10
f11
00
01
10
11

## Slide 44
Shannon’s Expansion Theorem
(In terms of more than one variable)
f
w
1
f00
f01
w
2
f10
f11
00
01
10
11

## Slide 45: Decoders

## Slide 46: 2-to-4 Decoder (Definition)
Has two inputs: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to 1
If w1=0 and w0=1, then the output y1 is set to 1
If w1=1 and w0=0, then the output y2 is set to 1
If w1=1 and w0=1, then the output y3 is set to 1
Only one output is set to 1. All others are set to 0.

## Slide 47: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]

## Slide 48: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]
The outputs are “one-hot” encoded

## Slide 49: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]

## Slide 50: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
m0
m2
m3
m1
These AND gates
implement the four
minterm functions

## Slide 51: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]
m0 m1 m2 m3
m0
m1
m2
m3

## Slide 52: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
0
0

## Slide 53: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
0
0
1
1
0
1
1
0
0
0

## Slide 54: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
0
0
1
1
0
1
1
0
0
0
1
0
0
0

## Slide 55: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
0
1
0
1
1
1
0
0
1
0
0
0
0
1

## Slide 56: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
1
0
1
0
0
0
1
1
0
1
0
1
0
0

## Slide 57: The Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]
1
1
0
0
1
0
0
1
1
1
0
0
1
0

## Slide 58: Decoder with an Enable Input

## Slide 59: Adding an Enable Input
[ Figure 4.13c from the textbook ]

## Slide 60: Adding an Enable Input
[ Figure 4.14c from the textbook ]
En

## Slide 61: 2-to-4 Decoder with an Enable Input
When En=1 this circuit behaves
like the one without enable.
En
1
1
1
1
1

## Slide 62: 2-to-4 Decoder with an Enable Input
En
0
0
0
0
0
0
0
0
0
When En=0 all outputs are set
to 0 and the decoder is disabled.

## Slide 63: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]

## Slide 64: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]
x indicates that it does not matter
what the value of this variable is
for this row of the truth table

## Slide 65: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]
0 0 0 0 0 0 0
0 0 1 0 0 0 0
0 1 0 0 0 0 0
0 1 1 0 0 0 0

## Slide 66: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]
0 0 0 0 0 0 0
0 0 1 0 0 0 0
0 1 0 0 0 0 0
0 1 1 0 0 0 0
1 0 0 1 0 0 0
1 0 1 0 1 0 0
1 1 0 0 0 1 0
1 1 1 0 0 0 1

## Slide 67: Graphical Symbol for a Binary n-to-2n Decoder with an Enable Input
[ Figure 4.14d from the textbook ]
A binary decoder with n inputs has 2n outputs
The outputs of an enabled binary decoder are “one-hot” encoded,
meaning that only a single bit is set to 1, i.e., it is hot.

## Slide 68: How can we build larger decoders?
3-to-8 ?
4-to-16?
5-to-??

## Slide 69
w
8
w
11
s
1
w
0
s
0
w
3
w
4
w
7
w
12
w
15
s
3
s
2
f
Hint: How did we build a 16-1 Multiplexer
[ Figure 4.4 from the textbook ]

## Slide 70
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]

## Slide 71
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
What is this?

## Slide 72
w
0
y
0
y
1
En
What is this?

## Slide 73
w
0
y
0
y
1
En
What is this?
This is a 1-to-2 decoder with an enable input.

## Slide 74
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]

## Slide 75
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 76
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
1
0
0
0
0
0
1
0
0
0
1
0
1
1
0
1

## Slide 77
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
1
0
0
0
0
0
0
0
1
1
0
0
1
0
1
1
0
1

## Slide 78
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
1
0
0
0
0
0
0
1
0
1
0
1
0
1
1
0
1

## Slide 79
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
1
0
0
0
0
1
1
1
0
1
0
1
1
0
1

## Slide 80
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
1
0
1
0
0
1
0
1
1
1
1
0

## Slide 81
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
1
0
0
0
1
1
0
1
0
1
1
1
1
0

## Slide 82
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
1
0
0
1
0
1
1
0
1
1
1
1
0

## Slide 83
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
0
1
1
1
1
1
0
1
1
1
1
0

## Slide 84
4-to-16 decoder built using a decoder tree
[ Figure 4.16 from the textbook ]
w
0
En
y
0
w
1
y
1
y
2
y
3
y
8
y
9
y
10
y
11
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
w
0
En
y
0
w
1
y
1
y
2
y
3
y
12
y
13
y
14
y
15
w
0
En
y
0
w
1
y
1
y
2
y
3
w
3
En
w

## Slide 85
Let’s build a
5-to-32 decoder

## Slide 86
Let’s build a
5-to-32 decoder
y0 – y15
y16 – y31
En

## Slide 87
Let’s build a
5-to-32 decoder
y0 – y15
y16 – y31
En
w4
w0
w1
w0
w1
w2
w3
w2
w3

## Slide 88: Demultiplexers

## Slide 89: 1-to-4 Demultiplexer (Definition)
Has one data input line: D
Has two output select lines: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to D
If w1=0 and w0=1, then the output y1 is set to D
If w1=1 and w0=0, then the output y2 is set to D
If w1=1 and w0=1, then the output y3 is set to D
Only one output is set to D. All others are set to 0.

## Slide 90
Graphical Symbol for a 1-to-4 Demultiplexer
w
0
D
y
0
w
1
y
1
y
2
y
3

## Slide 91
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]

## Slide 92
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]
output
select
lines
the
four
output
lines
data
input
line
D

## Slide 93
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
1
0
1
0
0
0

## Slide 94
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
0
0
0
0
0
0

## Slide 95
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
1
0
1
0
0
0

## Slide 96
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
1
1
0
0
1
0
0

## Slide 97: Multiplexers (Implemented with Decoders)

## Slide 98
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]

## Slide 99
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]
w0
0
0
0
w0
0
0
1
0
0
0

## Slide 100
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]
0
w1
0
0
w1
1
0
0
1
0
0

## Slide 101
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]
0
0
w2
0
w2
0
1
0
0
1
0

## Slide 102
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]
0
0
0
w3
w3
1
1
0
0
0
1

## Slide 103
4-to-1 Multiplexer (SOP circuit)
[ Figure 4.2c from the textbook ]
f = s1 s0 w0 + s1 s0 w1 + s1 s0 w2 + s1 s0 w3

## Slide 104: Encoders

## Slide 105: Encoders (there are several types)

## Slide 106: Binary Encoders

## Slide 107: 4-to-2 Binary Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two outputs: y1 and y0
Only one input is set to 1 (“one-hot” encoded). All others are set to 0.
If w0=1 then y1=0 and y0=0
If w1=1 then y1=0 and y0=1
If w2=1 then y1=1 and y0=0
If w3=1 then y1=1 and y0=1

## Slide 108
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Truth table for a 4-to-2 binary encoder

## Slide 109
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Truth table for a 4-to-2 binary encoder
The inputs are “one-hot” encoded

## Slide 110
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Circuit for a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 111
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
?
Circuit for a 4-to-2 binary encoder

## Slide 112
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
It is assumed that the
inputs are one hot encoded
Circuit for a 4-to-2 binary encoder

## Slide 113
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder

## Slide 114
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder
As this level of abstraction, we
need that w0 input for this to be
a proper 4-to-2 binary encoder.

## Slide 115
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder

## Slide 116
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
1
0
0
1
0
0
Circuit for a 4-to-2 binary encoder

## Slide 117
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
1
0
0
1
0
Circuit for a 4-to-2 binary encoder

## Slide 118
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
1
1
0
0
0
1
Circuit for a 4-to-2 binary encoder

## Slide 119
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 120
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 121
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
0
d
1
0
d
d
d
d
d
d
d
1
d
d
d
00
01
11
10
w1 w0
y0 = (w1 + w3)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 122
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
1
d
1
0
d
d
d
d
d
d
d
0
d
d
d
00
01
11
10
w1 w0
y1 = (w3 + w2)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 123
2
n
inputs
w
0
w
2
n
1
–
y
0
y
n
1
–
n
outputs
The Most General Case:
2n-to-n binary encoder
[ Figure 4.18 from the textbook ]

## Slide 124: Priority Encoders

## Slide 125: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )

## Slide 126: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 ) w0
y1=1 and y0=0 ( if w2=1 and w3=0 ) w0 , w1
y1=1 and y0=1 ( if w3=1 ) w0 , w1 , w2
these have lower priorities
and can be either 0 or 1.

## Slide 127: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )
z =0 if w3=w2=w1=w0=0; otherwise, z=1.

## Slide 128
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 129
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 130
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Truth table for a 4-to-2 priority encoder
1 x x x
0 1 x x
0 0 1 x
0 0 0 1
0 0 0 0

## Slide 131
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
d
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0
y1 = w3 + w2

## Slide 132
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
y0 = w3 + w1 w2
w3 w2
d
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0

## Slide 133
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0
z = w3 + w2 + w1 + w0

## Slide 134
Circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 135
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder

## Slide 136
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 137
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 138
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3
Try to prove that this is equivalent to the circuit that was derived above.

## Slide 139
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = ?
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 140
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = (w0 + w1 + w2 + w3)
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 141
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = ?

## Slide 142
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = w3 + w1 w2

## Slide 143
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = ?
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 144
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = w3 + w2
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 145
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Therefore, this circuit for the
4-to-2 priority encoder is equivalent to …
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 146
… this circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 147: Questions?

## Slide 148: THE END