## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Code Converters
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW 7 is out
It is due on Monday (Oct 20) @ 10pm
We will start with Chapter 5 on Friday.

## Slide 4
Quick Review

## Slide 5: Decoders

## Slide 6: 2-to-4 Decoder (Definition)
Has two inputs: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to 1
If w1=0 and w0=1, then the output y1 is set to 1
If w1=1 and w0=0, then the output y2 is set to 1
If w1=1 and w0=1, then the output y3 is set to 1
Only one output is set to 1. All others are set to 0.

## Slide 7: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]

## Slide 8: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]
The outputs are “one-hot” encoded

## Slide 9: Truth Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]

## Slide 10: Adding an Enable Input
[ Figure 4.13c from the textbook ]
En

## Slide 11: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]
x indicates that it does not matter
what the value of these variable is
for this row of the truth table

## Slide 12
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]

## Slide 13
A 4-to-16 decoder built using a decoder tree
[ Figure 4.16 from the textbook ]
w
0
En
y
0
w
1
y
1
y
2
y
3
y
8
y
9
y
10
y
11
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
w
0
En
y
0
w
1
y
1
y
2
y
3
y
12
y
13
y
14
y
15
w
0
En
y
0
w
1
y
1
y
2
y
3
w
3
En
w

## Slide 14: Graphical Symbol for a Binary n-to-2n Decoder with an Enable Input
[ Figure 4.14d from the textbook ]
A binary decoder with n inputs has 2n outputs
The outputs of an enabled binary decoder are “one-hot” encoded,
meaning that only a single bit is set to 1, i.e., it is hot.

## Slide 15: Demultiplexers

## Slide 16: 1-to-4 Demultiplexer (Definition)
Has one data input line: D
Has two output select lines: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to D
If w1=0 and w0=1, then the output y1 is set to D
If w1=1 and w0=0, then the output y2 is set to D
If w1=1 and w0=1, then the output y3 is set to D
Only one output is set to D. All others are set to 0.

## Slide 17
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]

## Slide 18
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]
output
select
lines
the
four
output
lines
data
input
line
D

## Slide 19: Encoders

## Slide 20: Binary Encoders

## Slide 21: 4-to-2 Binary Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two outputs: y1 and y0
Only one input is set to 1 (“one-hot” encoded). All others are set to 0.
If w0=1 then y1=0 and y0=0
If w1=1 then y1=0 and y0=1
If w2=1 then y1=1 and y0=0
If w3=1 then y1=1 and y0=1

## Slide 22
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Truth table for a 4-to-2 binary encoder
The inputs are “one-hot” encoded

## Slide 23
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 24
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 25
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
0
d
1
0
d
d
d
d
d
d
d
1
d
d
d
00
01
11
10
w1 w0
y0 = (w1 + w3)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 26
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
1
d
1
0
d
d
d
d
d
d
d
0
d
d
d
00
01
11
10
w1 w0
y1 = (w3 + w2)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 27
2
n
inputs
w
0
w
2
n
1
–
y
0
y
n
1
–
n
outputs
A 2n-to-n binary encoder
[ Figure 4.18 from the textbook ]

## Slide 28: Priority Encoders

## Slide 29: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )

## Slide 30: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 ) w0
y1=1 and y0=0 ( if w2=1 and w3=0 ) w0 , w1
y1=1 and y0=1 ( if w3=1 ) w0 , w1 , w2
these have lower priorities
and can be either 0 or 1.

## Slide 31: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )
z =0 if w3=w2=w1=w0=0; otherwise z=1.

## Slide 32
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 33
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)
These two are don’t cares, because the y values don’t matter in this case.
In other words, when z=0 there are no priority inputs that are set to 1.

## Slide 34
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 35
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Truth table for a 4-to-2 priority encoder
1 x x x
0 1 x x
0 0 1 x
0 0 0 1
0 0 0 0

## Slide 36
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
d
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0
y1 = w3 + w2

## Slide 37
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
y0 = w3 + w1 w2
w3 w2
d
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0

## Slide 38
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0
z = w3 + w2 + w1 + w0

## Slide 39
Circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 40
Circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0
In this circuit w0 is used.

## Slide 41
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder

## Slide 42
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 43
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 44
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3
Try to prove that this is equivalent to the circuit that was derived above.

## Slide 45
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = ?
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 46
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = (w0 + w1 + w2 + w3)
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 47
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = ?

## Slide 48
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = w3 + w1 w2

## Slide 49
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = ?
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 50
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = w3 + w2
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 51
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Therefore, this circuit for the
4-to-2 priority encoder is equivalent to …
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 52
… this circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 53: Code Converters

## Slide 54: Code Converter (Definition)
Converts from one type of input encoding to a different type of output encoding.

## Slide 55: Code Converter (Definition)
Converts from one type of input encoding to a different type of output encoding.
A decoder does that as well, but its outputs are always one-hot encoded so the output code is really only one type of output code.
A binary encoder does that as well but its inputs are always one-hot encoded so the input code is really only one type of input code.

## Slide 56
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 57
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 58
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 59
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 60
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 61
What is the circuit for this code converter?
x3 x2 x1 x0

## Slide 62
What is the circuit for this code converter?
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 7, 8, 9, 10, 12, 14, 15)

## Slide 63
What is the circuit for this code converter?
1
0
0
1
1
1
1
1
1
0
1
1
1
1
0
1
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 7, 8, 9, 10, 12, 14, 15)

## Slide 64
What is the circuit for this code converter?
x3 x2 x1 x0

## Slide 65
What is the circuit for this code converter?
1
0
0
1
1
1
0
1
1
1
1
1
0
1
1
0
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 8, 9, 11, 12, 13, 14)

## Slide 66: Example Problems from Chapter 4

## Slide 67: Example 1: SOP vs Decoders
Implement the function
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)
by using a 3-to-8 binary decoder and one OR gate.

## Slide 68
w3
w2
w1
w2
w1
w0
1
En
y0
y1
y2
y3
y5
y4
y6
y7
[ Figure 4.44 from the textbook ]
Solution Circuit
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)

## Slide 69
w3
w2
w1
w2
w1
w0
1
En
y0
y1
y2
y3
y5
y4
y6
y7
[ Figure 4.44 from the textbook ]
Solution Circuit
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)
Notice this swap
of variables in
the two lists.
Need to match the
least significant
with the least
significant in both.

## Slide 70: Example 2: Implement an 8-to-3 binary encoder
[ Figure 4.45 from the textbook ]

## Slide 71: Example 2: Implement an 8-to-3 binary encoder
[ Figure 4.45 from the textbook ]
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7
These formulas work due to
the one-hot encoded property
of the inputs.

## Slide 72: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 73: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 74: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 75
Circuit for the 8-to-3 binary encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 76: Example 3: Implement an 8-to-3 priority encoder

## Slide 77: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x

## Slide 78: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0

## Slide 79: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0

## Slide 80: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0
z = i0+i1+i2+i3+i4+i5+i6+i7
i0 = w7 w6 w5 w4 w3 w2 w1 w0
i1 = w7 w6 w5 w4 w3 w2 w1
i2 = w7 w6 w5 w4 w3 w2
i3 = w7 w6 w5 w4 w3
i4 = w7 w6 w5 w4
i5 = w7 w6 w5
i6 = w7 w6
i7 = w7

## Slide 81
Circuit for the 8-to-3 binary encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0

## Slide 82
Circuit for the 8-to-3 priority encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0
z
i7 i6 i5 i4 i3 i2 i1 i0

## Slide 83: Example 4:Circuit implementation using a multiplexer
Implement the function
f(w1, w2, w3, w4, w5) = w1w2w4w5 + w1w2 + w1w3 + w1w4 + w3w4w5
using a 4-to-1 multiplexer

## Slide 84: Some Boolean Algebra Leads To
w1w2w4w5 + w1w2 + w1w3 + w1w4 + w3w4w5
w1w4 (w5 w2) + w4 (w3w5) + w1 (w2 + w3) + w1w4 (1)
w1w4 (w5 w2) + ( w1+w1)w4 (w3w5) + w1( w4+w4) (w2 + w3) + w1w4 (1)
w1w4 (w5 w2) + w1w4 (w3w5) + w1w4 (w2 + w3) + w1w4 ( w3w5 + (w2+w3) + 1)
w1w4 (w5 w2) + w1w4 (w3w5) + w1w4 (w2 + w3) + w1w4 (1)
Note that the split is by w1 and w4, not w1 and w2

## Slide 85
[ Figure 4.46 from the textbook ]
Solution Circuit
01
00
10
11

## Slide 86
Some Final Things from Chapter 4

## Slide 87: Shifter Circuit

## Slide 88
[ Figure 4.50 from the textbook ]
Hold / Shift-Right Circuit

## Slide 89
[ Figure 4.50 from the textbook ]
Hold / Shift-Right Circuit
4-bit input
4-bit output

## Slide 90
No shift if the control signal is 0
0

## Slide 91
No shift if the control signal is 0
0

## Slide 92
No shift if the control signal is 0
0
w3
w2
w1
w0
No shift in this case.

## Slide 93
No shift if the control signal is 0
0
w3
w2
w1
w0
No shift in this case.
0

## Slide 94
Shift right if the control signal is 1
1

## Slide 95
Shift right if the control signal is 1
1

## Slide 96
Shift right if the control signal is 1
1
0
w3
w2
w1
Shift to the right by 1 bit

## Slide 97
A shifter circuit
1
0
w3
w2
w1
Shift to the right by 1 bit
w0

## Slide 98: Barrel Shifter

## Slide 99
[ Figure 4.51 from the textbook ]
A barrel shifter circuit

## Slide 100
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
0
w3
w2
w1
w0

## Slide 101
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 102
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 103
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 104
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 105
[ Figure 4.51 from the textbook ]
A barrel shifter circuit

## Slide 106: Arithmetic Logic Unit (ALU)

## Slide 107: Shifter Circuit of the i281 CPU

## Slide 108
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 109
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
Write
Select
Read
Select
Read
Select
Write
Select
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux
Input
Input
Input

## Slide 110
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 111
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic Logic Unit

## Slide 112: The ALU
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 113: The Shifter Circuit
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 114: The i281 CPU Shifter Circuit
Select
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 115
0
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 116
1
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 117: Shift Left
0
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 118: Shift Left
0
1 0
1
1 0
0
1 0
1
1 0
1
1 0
0
1 0
0
1 0
1
1 0
1
1 0
0
1
1
0
0
1
1
0
1
i281 CPU

## Slide 119: Shift Right
1
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 120: Shift Right
1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1
1
0
0
1
1
0
1
1
1
0
0
1
1
0
1
0
i281 CPU

## Slide 121: Bus Multiplexer

## Slide 122: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]

## Slide 123: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]
8-bit bus

## Slide 124: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]
8-bit bus
For each lane:
every car is a 1,
every gap is a 0.
A7 A6 A5 A4 A3 A2 A1 A0
Time

## Slide 125: Bus Multiplexer Analogy
[https://www.researchgate.net/figure/An-example-of-traffic-jam-around-a-junction-where-several-lanes-join_fig1_221567960 ]

## Slide 126: Bus Multiplexer Analogy
A1 A0
B1 B0
F1 F0
select

## Slide 127: Bus Multiplexer Analogy
A1 A0
B1 B0
F1 F0
select
One restriction of digital
multiplexers is that they
cannot mix bits from A and B
when outputting F. At each time
step it is only A or only B.

## Slide 128: The Internal ALU Bus Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 129: 2-to-1 Bus Multiplexer (with 8-bit lines)
0
1
Z7 … Z0
U7 … U0
V7 … V0
8
8
c12
8

## Slide 130
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12

## Slide 131
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12
0

## Slide 132
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12
1

## Slide 133: 2-to-1 Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 134: 2-to-1 Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 135: 2-to-1 Multiplexer
input_0
input_1
select

## Slide 136: The adder/subtractor of the i281 CPU

## Slide 137
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic Logic Unit

## Slide 138: The Adder / Subtractor
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
i281 CPU

## Slide 139: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
add / sub
This is an 8-bit ripple-carry adder. Note that the X and Y lines are swapped.
i281 CPU

## Slide 140: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
i281 CPU

## Slide 141: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
negative
zero
negative and zero can be
computed here as well
i281 CPU

## Slide 142: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)

## Slide 143: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)
In some CPU architectures the carry flag
means borrow. And it could be inverted
relative to the previous diagram.

## Slide 144: The flag calculator of the i281 CPU

## Slide 145: The ALU Flag Calculator
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 146: The ALU Flag Calculator
I0
I1
I2
I3
I4
I5
I6
I7
negative
zero

## Slide 147: ALU Outputs to the Flags Register
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
4 Outputs to the
Flags Register

## Slide 148: Questions?

## Slide 149: THE END