## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2: Synchronous Sequential Circuits Basic Design Steps
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 10 is due on Monday Nov. 10 @ 10pm.

## Slide 4: Administrative Stuff
We are starting with Chapter 6 from the textbook

## Slide 5
First Design Pattern:
Moore Machines

## Slide 6: Moore Machine: A Type of Finite State Machine (FSM)
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.3 from the textbook ]

## Slide 7
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
Finite number of states (nodes).
Discrete state transitions (edges).
Only “in” one state at a time.
One reset state
Every state has an outgoing state transition for each possible input.
[ Figure 6.3 from the textbook ]

## Slide 8
The next state depends on both
the current state and the current input.
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.3 from the textbook ]

## Slide 9
The output depends only on the current state.
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.3 from the textbook ]

## Slide 10
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 11
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
input
output

## Slide 12: Let’s do a simulation

## Slide 13
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 14
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 15
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 16
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 17
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 18
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 19
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 20
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 21
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 22
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 23
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 24
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 25
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 27
In general, we need to start tracing from the beginning to know which state the FSM is in. It may not be clear from a short sequence of outputs.
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 28
Inferring the States

## Slide 29
Inferring the States
A
B
C
A
A
A
A
B
B
C
C

## Slide 30
What is the meaning of each state?
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 31: What is a State?
It is not really a memory of every past input
(We might run out of space to remember it all!)
Rather, it is a characterization or snapshot of the pattern of inputs that have come before.

## Slide 32: Moore Machine Implementation
The state diagram is just an illustration to help us describe and reason about how the FSM will behave in each of its states.
So, how do we turn it into a circuit?

## Slide 33: Moore Machine Implementation
Combinational
circuit
Memory Elements
Clock
Combinational
circuit
Z
W
Note: The W and Z lines need not be wires. They can be buses.
[ Figure 6.1 from the textbook ]

## Slide 34: State Storage
Combinational
circuit
Flip-Flop Array
Clock
Combinational
circuit
Z
Q(t)
W
Any usable “memory” of the preceding input sequence
is encoded in the flip-flop array.
Q(t+1)

## Slide 35: FSM States
The Flip-Flop array stores an encoding of the current state.
Q(t+1)
Clock
Q(t)

## Slide 36: FSM States
The Flip-Flop array stores an encoding of the current state.
Q(t+1)
Clock
Q(t)
current state

## Slide 37: FSM States
The Flip-Flop array stores an encoding of the current state.
Q(t+1)
Clock
Q(t)
next state

## Slide 38: State Storage
Combinational
circuit
Flip-Flop Array
Clock
Combinational
circuit
Z
Q(t)
W
Any usable “memory” of the preceding input sequence
is encoded in the flip-flop array.
Q(t+1)
current
state
next
state

## Slide 39: State Encoding
Each of the states in our design is identified by a distinct code.
If we use 3 flip-flops, then the FSM can have up to 23 = 8 distinct states.
So, when the flip-flop array contains the code 011, we say that the machine is in state 011.

## Slide 40: Synchronous Design
Every active clock edge causes a state transition.
Combinational
circuit
Flip-Flop Array
Clock
Combinational
circuit
Z
W
Q(t)
Q(t+1)

## Slide 41: Synchronous Design
We expect the input signals to be stable
before the active clock edge occurs.
Combinational
circuit
Flip-Flop Array
Clock
Combinational
circuit
Z
W
Q(t)
Q(t+1)

## Slide 42: Synchronous Design
There is a whole other class of sequential circuits that are asynchronous, but we will not study them in this course.
Combinational
circuit
Flip-Flop Array
Clock
Combinational
circuit
Z
W
Q(t)
Q(t+1)

## Slide 43: Sequential Circuits: Key Ideas
The current output depends on something about the preceding sequence of inputs (and maybe the current output).
Using memory elements (i.e., flip-flops), we design the circuit to remember some relevant information about the prior inputs.

## Slide 44: Moore Machine Example

## Slide 45
We need to find both the next state logic and the output logic implied by this machine.
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.3 from the textbook ]

## Slide 46
Present
Next state
Output
state
w
=
0
w
=
1
z
A
B
C
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 47
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.4 from the textbook ]

## Slide 48: How to represent the States?
One way is to encode each state with a 2-bit binary number
A ~ 00
B ~ 01
C ~ 10

## Slide 49: How to represent the states?
One way is to encode each state with a 2-bit binary number
A ~ 00
B ~ 01
C ~ 10
How many flip-flops do we need?

## Slide 50: Let’s use two flip-flops to hold the machine’s state

## Slide 51
Clock
y
1
y
2
Y
2
Y
1

## Slide 52
Let’s pick D Flip-Flops.
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 53
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 54
Two zeros on the output JOINTLY represent state A.
Clock
y
1
y
2
Y
2
Y
1
0
0
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 55
This flip-flop output pattern represents state B.
Clock
y
1
y
2
Y
2
Y
1
0
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 56
This flip-flop output pattern represents state C.
Clock
y
1
y
2
Y
2
Y
1
1
0
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 57
What does this flip-flop output pattern represent?
Clock
y
1
y
2
Y
2
Y
1
1
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 58
This would be state D, but we don't have one
in this example. So, this is an impossible state.
Clock
y
1
y
2
Y
2
Y
1
1
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 59
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 60
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
Q(t) = y2 y1
Q(t+1) = Y2Y1
D
Q
Q
D
Q
Q

## Slide 61
We need to find logic expressions for
Y1(w, y1, y2), Y2(w, y1, y2), and z(y1, y2).
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 62
We need to find logic expressions for
Y1(w, y1, y2), Y2(w, y1, y2), and z(y1, y2).
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 63
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Suppose we encoded our states in the same order in which they were labeled:
A ~ 00
B ~ 01
C ~ 10
[ Figure 6.4 from the textbook ]

## Slide 64
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
z
A
00
B
01
C
10
11
The finite state machine will never reach a state encoded as 11.
[ Figure 6.6 from the textbook ]

## Slide 65
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
10
0
C
10
00
10
1
11
dd
dd
d
2
y
We arbitrarily chose these as our state encodings. We could have used others.
[ Figure 6.6 from the textbook ]

## Slide 66
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
[ Figure 6.6 from the textbook ]

## Slide 67
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 68
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 69
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 70
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 71
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 72
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 73
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 74
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 75
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
w
00
01
11
10
0
1
0
1
0
y
2
y
1
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
d
d
0
0
0
0
0
0
1
0
1
0
1
0
d
y
1
0
1
y
2
Y 1
Y 2
z
Note that the textbook draws these K-Maps
differently from all previous K-maps
(the most significant bit indexes the rows).

## Slide 76
Y
1
wy
1
y
2
=
Y
2
wy
1
y
2
wy
1
y
2
+
=
z
y
1
y
2
=
Y
1
wy
1
y
2
=
Y
2
wy
1
wy
2
+
=
z
y
2
=
w
y
1
y
2
+
(
)
=
Ignoring don't cares
Using don't cares
Don’t care conditions simplify the combinatorial logic
[ Figure 6.7 from the textbook ]
w
00
01
11
10
0
1
0
1
0
y
2
y
1
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
d
d
0
0
0
0
0
0
1
0
1
0
1
0
d
y
1
0
1
y
2
Y 1
Y 2
z

## Slide 77
[ Figure 6.8 from the textbook ]
Draw the Circuit Diagram

## Slide 78
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
Draw the Circuit Diagram
this is the
next-state logic

## Slide 79
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
z = y2
Draw the Circuit Diagram
this is the
output logic
this is the
next-state logic

## Slide 80
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
z = y2
Draw the Circuit Diagram
these are the
flip-flops

## Slide 81
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 82
[ Figure 6.8 from the textbook ]
Don’t Forget to Add the Reset Line

## Slide 83
[ Figure 6.8 from the textbook ]
Don’t Forget to Add the Reset Line
Reset

## Slide 84
[ Figure 6.8 from the textbook ]
When the reset signal is equal to zero it puts the machine back to its start state, which is state 00 (or A)
in this case.
0
0
0
State A=00

## Slide 85
[ Figure 6.8 from the textbook ]
0
0
0
1
1
State A=00
When the reset signal is equal to zero it puts the machine back to its start state, which is state 00 (or A)
in this case.

## Slide 86
0
1
0
0
0
0
1
1
0
0
0
1
1
1
State A=00
State = y2 y1

## Slide 87
0
1
0
0
0
0
1
1
0
0
0
1
1
0
State A=00

## Slide 88
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00

## Slide 89
1
1
0
0
1
0
1
1
0
0
0
1
1
1
State A=00

## Slide 90
1
1
0
0
1
0
1
1
0
0
0
1
1
0
State A=00

## Slide 91
1
1
0
1
0
1
1
0
0
1
1
1
0
01
State B=01

## Slide 92
0
1
0
1
0
0
1
0
0
1
1
1
0
1
State B=01

## Slide 93
0
1
0
1
0
0
1
0
0
1
1
1
0
0
State B=01

## Slide 94
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00

## Slide 95
1
1
0
0
1
0
1
1
0
0
0
1
1
1
State A=00

## Slide 96
1
1
0
0
1
0
1
1
0
0
0
1
1
0
State A=00

## Slide 97
1
1
0
1
0
1
1
0
0
1
1
1
0
01
State B=01

## Slide 98
1
1
0
1
0
1
1
0
0
1
1
1
0
1
State B=01

## Slide 99
1
1
0
1
0
1
1
0
0
1
1
1
0
0
State B=01

## Slide 100
1
1
1
0
0
1
0
1
1
0
1
0
1
01
State C=10
output z=1

## Slide 101
0
1
1
0
0
0
0
1
1
0
1
0
1
1
State C=10
output z=1

## Slide 102
0
1
1
0
0
0
0
1
1
0
1
0
1
0
State C=10
output z=1

## Slide 103
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00

## Slide 104
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
[ Figure 6.9 from the textbook ]

## Slide 105
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1

## Slide 106
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1

## Slide 107
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
A
1
0
B
0
1
C
0
0
A
0
0
A
0
0
A
0
0
A
1
0
B
1
0
B
0
1
C
0
1
C

## Slide 108
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
A
B
C
A
A
A
A
B
B
C
C

## Slide 109
Summary: Designing a Moore Machine
Obtain the circuit specification.
Derive a state diagram.
Derive the state table.
Decide on a state encoding.
Encode the state table.
Derive the output logic and next-state logic.
Draw the circuit diagram
Add a reset signal.

## Slide 110: Questions?

## Slide 111: THE END