## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2: State Assignment Problem
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 10 is due on Nov 10 @ 10pm
Homework 11 is due on Nov 17 @ 10pm

## Slide 4: Quick Review

## Slide 5
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
The general form of a synchronous sequential circuit
[ Figure 6.1 from the textbook ]

## Slide 6
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 7
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Mealy Type

## Slide 8: Moore Machine
The machine’s current state and current inputs are used to decide which next state to transition into.
The machine’s current state decides the current output.
Named after Edward Moore (1925-2003) who published the idea in 1956.
Moore, E. (1956). "Gedanken-experiments on Sequential Machines". Automata Studies, Annals of Math. Studies. Princeton Univ. Press (34): 129–153.

## Slide 9: Mealy Machine
The machine’s current state and current inputs are used to decide which next state to transition into.
The machine’s current state and current input values decide the current output.
Named after George Mealy (1927 – 2010) who published the idea in 1955.
Mealy, G. (1955). “A method for synthesizing sequential circuits” The Bell System Technical Journal, Volume: 34, Issue: 5, Sept. 1955.

## Slide 10
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Today’s lecture is about the mapping
from states to flip-flop outputs

## Slide 11
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Today’s lecture is about the mapping
from states to flip-flop outputs
It applies to both Mealy and Moore machines…

## Slide 12
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Today’s lecture is about the mapping
from states to flip-flop outputs
… but all examples will be for Moore machines.

## Slide 13
Designing a Moore Machine
Obtain the circuit specification.
Derive a state diagram.
Derive the state table.
Decide on a state encoding.
Encode the state table.
Derive the output logic and next-state logic.
Draw the circuit diagram
Add a reset signal.

## Slide 14: Example #1

## Slide 15
We need to find both the next state logic and
the output logic implied by this machine.
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.3 from the textbook ]

## Slide 16
Present
Next state
Output
state
w
=
0
w
=
1
z
A
B
C
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 17
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
C: z = 1
Reset
B: z = 0
A: z = 0
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
[ Figure 6.4 from the textbook ]

## Slide 18: State Encoding for Example #1: A=00, B=01, C=10 (Uses Two Flip-Flops)

## Slide 19: How to represent the states?
One way is to encode each state with a 2-bit binary number
A = 00
B = 01
C = 10

## Slide 20: How to represent the states?
One way is to encode each state with a 2-bit binary number
A = 00
B = 01
C = 10
How many flip-flops do we need?

## Slide 21: Let’s use two flip flops to hold the state of this machine

## Slide 22
Clock
y
1
y
2
Y
2
Y
1

## Slide 23
Let’s pick D Flip-Flops.
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 24
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 25
Two zeros on the output JOINTLY represent state A.
Clock
y
1
y
2
Y
2
Y
1
0
0
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 26
This flip-flop output pattern represents state B.
Clock
y
1
y
2
Y
2
Y
1
0
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 27
This flip-flop output pattern represents state C.
Clock
y
1
y
2
Y
2
Y
1
1
0
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 28
What does this flip-flop output pattern represent?
Clock
y
1
y
2
Y
2
Y
1
1
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 29
This would be state D, but we don't have one
in this example. So this is an impossible state.
Clock
y
1
y
2
Y
2
Y
1
1
1
D
Q
Q
D
Q
Q
State = y2 y1

## Slide 30
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 31
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
Q(t) = y2 y1
Q(t+1) = Y2Y1
D
Q
Q
D
Q
Q

## Slide 32
We need to find logic expressions for
Y1(w, y1, y2), Y2(w, y1, y2), and z(y1, y2).
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 33
We need to find logic expressions for
Y1(w, y1, y2), Y2(w, y1, y2), and z(y1, y2).
[ Figure 6.5 from the textbook ]
Next State Logic
Output Logic
Clock
y
1
z
w
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 34
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Suppose we encoded our states in the same order in which they were labeled:
A ~ 00
B ~ 01
C ~ 10
[ Figure 6.4 from the textbook ]

## Slide 35
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
z
A
00
B
01
C
10
11
The finite state machine will never reach a state encoded as 11.
[ Figure 6.6 from the textbook ]

## Slide 36
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
10
0
C
10
00
10
1
11
dd
dd
d
2
y
We arbitrarily chose these as our state encodings. We could have used others.
[ Figure 6.6 from the textbook ]

## Slide 37
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
[ Figure 6.6 from the textbook ]

## Slide 38
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 39
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 40
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 41
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 42
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | d | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 43
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | d | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 44
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y

## Slide 45
Present
Next state
state
w
=
0
w
=
1
Output
y
1
Y
2
Y
1
Y
2
Y
1
z
00
00
01
0
01
00
10
0
10
00
10
1
11
dd
dd
d
2
y
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
[ Figure 6.6 from the textbook ]

## Slide 46
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | d | d
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | d
w
00
01
11
10
0
1
0
1
0
y
2
y
1
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
d
d
0
0
0
0
0
0
1
0
1
0
1
0
d
y
1
0
1
y
2
Y 1
Y 2
z
Note that the textbook draws these K-Maps
differently from all previous K-maps
(the most significant bit indexes the rows).

## Slide 47
Y
1
wy
1
y
2
=
Y
2
wy
1
y
2
wy
1
y
2
+
=
z
y
1
y
2
=
Y
1
wy
1
y
2
=
Y
2
wy
1
wy
2
+
=
z
y
2
=
w
y
1
y
2
+
(
)
=
Ignoring don't cares
Using don't cares
Don’t care conditions simplify the combinatorial logic
[ Figure 6.7 from the textbook ]
w
00
01
11
10
0
1
0
1
0
y
2
y
1
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
d
d
0
0
0
0
0
0
1
0
1
0
1
0
d
y
1
0
1
y
2
Y 1
Y 2
z

## Slide 48
[ Figure 6.8 from the textbook ]
Draw the Circuit Diagram

## Slide 49
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
Draw the Circuit Diagram
this is the
next-state logic

## Slide 50
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
z = y2
Draw the Circuit Diagram
this is the
output logic

## Slide 51
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
z = y2
Draw the Circuit Diagram
these are the
flip-flops

## Slide 52
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 53
[ Figure 6.8 from the textbook ]
Don’t Forget to Add the Reset Line

## Slide 54
[ Figure 6.8 from the textbook ]
Don’t Forget to Add the Reset Line
Reset

## Slide 55
[ Figure 6.8 from the textbook ]
When the reset signal is equal to zero it puts the machine back to its start state, which is state 00 (or A)
in this case.
0
0
0
State A=00

## Slide 56
[ Figure 6.8 from the textbook ]
0
0
0
1
1
State A=00
When the reset signal is equal to zero it puts the machine back to its start state, which is state 00 (or A)
in this case.

## Slide 57
0
1
0
0
0
0
1
1
0
0
0
1
1
1
State A=00
State = y2 y1

## Slide 58
0
1
0
0
0
0
1
1
0
0
0
1
1
0
State A=00
State = y2 y1

## Slide 59
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00
State = y2 y1

## Slide 60
1
1
0
0
1
0
1
1
0
0
0
1
1
1
State A=00
State = y2 y1

## Slide 61
1
1
0
0
1
0
1
1
0
0
0
1
1
0
State A=00
State = y2 y1

## Slide 62
1
1
0
1
0
1
1
0
0
1
1
1
0
01
State B=01
State = y2 y1

## Slide 63
0
1
0
1
0
0
1
0
0
1
1
1
0
1
State B=01
State = y2 y1

## Slide 64
0
1
0
1
0
0
1
0
0
1
1
1
0
0
State B=01
State = y2 y1

## Slide 65
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00
State = y2 y1

## Slide 66
1
1
0
0
1
0
1
1
0
0
0
1
1
1
State A=00
State = y2 y1

## Slide 67
1
1
0
0
1
0
1
1
0
0
0
1
1
0
State A=00
State = y2 y1

## Slide 68
1
1
0
1
0
1
1
0
0
1
1
1
0
01
State B=01
State = y2 y1

## Slide 69
1
1
0
1
0
1
1
0
0
1
1
1
0
1
State B=01
State = y2 y1

## Slide 70
1
1
0
1
0
1
1
0
0
1
1
1
0
0
State B=01
State = y2 y1

## Slide 71
1
1
1
0
0
1
0
1
1
0
1
0
1
01
State C=10
output z=1
State = y2 y1

## Slide 72
0
1
1
0
0
0
0
1
1
0
1
0
1
1
State C=10
output z=1
State = y2 y1

## Slide 73
0
1
1
0
0
0
0
1
1
0
1
0
1
0
State C=10
output z=1
State = y2 y1

## Slide 74
0
1
0
0
0
0
1
1
0
0
0
1
1
01
State A=00
State = y2 y1

## Slide 75
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
[ Figure 6.9 from the textbook ]

## Slide 76
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1

## Slide 77
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1

## Slide 78
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
A
1
0
B
0
1
C
0
0
A
0
0
A
0
0
A
0
0
A
1
0
B
1
0
B
0
1
C
0
1
C

## Slide 79
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
A
B
C
A
A
A
A
B
B
C
C

## Slide 80
Summary: Designing a Moore Machine
Obtain the circuit specification.
Derive a state diagram.
Derive the state table.
Decide on a state encoding.
Encode the state table.
Derive the output logic and next-state logic.
Draw the circuit diagram
Add a reset signal.

## Slide 81: Alternative State Encoding for Example #1: A=00, B=01, C=11 (Also Uses Two Flip-Flops)

## Slide 82: A Better State Encoding
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Suppose we encoded our states another way:
A = 00
B = 01
C = 11

## Slide 83
Clock
y
1
y
2
Y
2
Y
1

## Slide 84
Let’s pick D Flip-Flops.
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 85
We will call y1 and y2 the present state variables.
We will call Y1 and Y2 the next state variables.
[ Figure 6.5 from the textbook ]
Clock
y
1
y
2
Y
2
Y
1
D
Q
Q
D
Q
Q

## Slide 86
Two zeros on the output JOINTLY represent state A.
Clock
y
1
y
2
Y
2
Y
1
0
0
D
Q
Q
D
Q
Q

## Slide 87
This flip-flop output pattern represents state B.
Clock
y
1
y
2
Y
2
Y
1
0
1
D
Q
Q
D
Q
Q

## Slide 88
This flip-flop output pattern represents state C.
Clock
y
1
y
2
Y
2
Y
1
1
1
D
Q
Q
D
Q
Q

## Slide 89
What does this flip-flop output pattern represent?
Clock
y
1
y
2
Y
2
Y
1
1
0
D
Q
Q
D
Q
Q

## Slide 90
This would be state D, but we don't have one
in this example. So this is an impossible state.
Clock
y
1
y
2
Y
2
Y
1
1
0
D
Q
Q
D
Q
Q

## Slide 91: A Better State Encoding
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Suppose we encoded our states another way:
A = 00
B = 01
C = 11

## Slide 92: A Better State Encoding
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
z
A = 00
B = 01
C = 11

## Slide 93: A Better State Encoding
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d
A = 00
B = 01
C = 11

## Slide 94: Let's Derive the Logic Expressions
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d
[ Figure 6.16 from the textbook ]

## Slide 95
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d
[ Figure 6.16 from the textbook ]

## Slide 96
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 97
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 98
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 99
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 100
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 101
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 102
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 103
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 104
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 105
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 106
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | d | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 107
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 108
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 109
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | d | 
1 | 1 | 1 | 1 | 
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 110
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 111
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 112
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 113
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
11
0
C
11
00
11
1
10
dd
dd
d

## Slide 114
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1

## Slide 115
w | y2 | y1 | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | d | d
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | 1
Q(t) = y2y1 and Q(t+1) = Y2Y1
y2 | y1 | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | d
1 | 1 | 1
w
00
01
11
10
0
1
0
0
1
1
y
2
y
1
0
0
d
Y2
d
Y2(w, y2, y1) = wy1
Y1
Y1(w, y2, y1) = w
w
00
01
11
10
0
1
0
1
1
y
2
y
1
0
1
d
d
0
0
1
0
1
0
1
y
1
0
d
y
2
z
z(y2, y1) = y2
Deriving the Logic Expressions

## Slide 116
w
00
01
11
10
0
1
0
1
0
y
2
y
1
d
d
0
0
0
Y 1
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
0
0
0
1
Y 2
0
1
0
1
0
d
y
1
0
1
y
2
z
Original State Encodings
New State Encodings
w
00
01
11
10
0
1
0
0
1
1
y
2
y
1
0
0
d
Y2
d
Y1
w
00
01
11
10
0
1
0
1
1
y
2
y
1
0
1
d
d
0
0
1
0
1
0
1
y
1
0
d
y
2
z

## Slide 117: The New and Improved Circuit Diagram
Y1(w, y2, y1) = w
Y2(w, y2, y1) = wy1
z(y2, y1) = y2
[ Figure 6.17 from the textbook ]
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn

## Slide 118: The New and Improved Circuit Diagram
Y1(w, y2, y1) = w
Y2(w, y2, y1) = wy1
z(y2, y1) = y2
[ Figure 6.17 from the textbook ]
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
next-state logic
output logic
flip-flops

## Slide 119
[ Figure 6.8 from the textbook ]
Y2= w (y1 + y2)
Y1= w y1 y2
z = y2
The Previous Circuit Diagram

## Slide 120
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit
Moore Type

## Slide 121
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
0
0
0
0
1
1
0

## Slide 122
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
0
0
0
0
1
0
0

## Slide 123
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
0
0
0
0
1
01
0

## Slide 124
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
1
1
0
0
1
1
1

## Slide 125
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
1
1
0
0
1
0
1

## Slide 126
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
1
1
1
1
1
01
1

## Slide 127
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
0
0
1
0
1
1
0

## Slide 128
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
0
0
1
0
1
0
0

## Slide 129
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
0
0
0
0
1
01
0

## Slide 130
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
1
1
0
0
1
1
1

## Slide 131
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
1
1
0
0
1
0
1

## Slide 132
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
1
1
1
1
1
01
1

## Slide 133
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
1
1
1
1
1
1
1

## Slide 134
State B=01
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
1
1
1
1
1
1
0
1

## Slide 135
State C=11
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
1
1
1
1
1
1
1
01
1
output z=1

## Slide 136
State C=11
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
1
1
0
0
1
0
1
1
0
output z=1

## Slide 137
State C=11
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
1
1
0
0
1
0
1
0
0
output z=1

## Slide 138
State A=00
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
z
y
1
y
2
Resetn
0
0
0
0
0
0
1
01
0

## Slide 139
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z

## Slide 140
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
1
1
0
0
0
0
0
0
0
0
1
0
1
0
1
1
1
1

## Slide 141
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
1
0
1
1
0
0
0
0
0
0
0
0
1
0
1
0
1
1
1
1

## Slide 142
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
0
0
A
1
0
B
1
1
C
0
0
A
0
0
A
0
0
A
0
0
A
1
0
B
1
0
B
1
1
C
1
1
C

## Slide 143
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
z
A
B
C
A
A
A
A
B
B
C
C

## Slide 144: Main Idea
Different state assignments for the same Moore machine typically lead to different circuits.
Some may use fewer logic elements than others.
But they all do the same thing
(i.e., implement the same Moore machine).

## Slide 145: Example #2

## Slide 146
[ Figure 6.10 from the textbook ]
Register Swap Controller

## Slide 147
[ Figure 6.10 from the textbook ]
Register Swap Controller
Design a Moore machine control circuit for swapping the contents of registers R1 and R2 by using R3 as a temporary.

## Slide 148
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
If an output is not given, then assume that it is 0.
[ Figure 6.11 from the textbook ]
State Diagram

## Slide 149
Animated Register Swap

## Slide 150
Animated Register Swap
0xFF
0x42
0xC9
These are the original values of the 8-bit registers

## Slide 151
Animated Register Swap
0xFF
0x42
0xC9
1
For clarity, only inputs that are equal to 1 will be shown.

## Slide 152
Animated Register Swap
0xFF
0x42
0xC9
1
1
1

## Slide 153
Animated Register Swap
0xFF
0x42
0xC9
1
1
1
0x42

## Slide 154
Animated Register Swap
0xFF
0x42
0x42
1
1
1

## Slide 155
Animated Register Swap
0xFF
0x42
0x42
1
1
1

## Slide 156
Animated Register Swap
0xFF
0x42
0x42
1
1
1
0xFF

## Slide 157
Animated Register Swap
0xFF
0xFF
0x42
1
1
1

## Slide 158
Animated Register Swap
0xFF
0xFF
0x42
1
1
1

## Slide 159
Animated Register Swap
0xFF
0xFF
0x42
1
1
1
0x42

## Slide 160
Animated Register Swap
0x42
0xFF
0x42
1
1
1

## Slide 161
Animated Register Swap
0x42
0xFF
0x42
1

## Slide 162
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
If an output is not given, then assume that it is 0.
[ Figure 6.11 from the textbook ]
State Diagram

## Slide 163: Some Questions
How many flip-flops are we going to use?
How many logic expressions do we need to find?

## Slide 164
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
Flip-Flop Array
Clock
W
Next State Logic
Q(t)
Q(t+1)
Output Logic
Z

## Slide 165
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
Flip-Flop Array
Clock
w
Next State Logic
y[1:2]
Y[1:2]
Output Logic
R1out
R1in
R3in
R2out
R2in
R3out
Done

## Slide 166
Present
Next state
Outputs
state
A
B
C
D
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=

## Slide 167
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done

## Slide 168
As we saw before, we can expect that some state encodings will be better than others.
We will consider three encoding schemes.

## Slide 169: Encoding #1: A=00, B=01, C=10, D=11 (Uses Two Flip-Flops)

## Slide 170: State Table
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
[ Figure 6.12 & 6.13 from the textbook ]
State-Assigned Table

## Slide 171: State Table
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
[ Figure 6.12 & 6.13 from the textbook ]
State Assigned Table
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 172: State Table
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Assigned Table
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
[ Figure 6.12 & 6.13 from the textbook ]

## Slide 173: State Table
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
[ Figure 6.12 & 6.13 from the textbook ]
State Assigned Table

## Slide 174
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Let's derive the next-state expressions.

## Slide 175
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
Pay attention to the way the columns
of the truth table are labeled.

## Slide 176
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
w
00
01
11
10
0
1
y
2
y
1
Y
2

## Slide 177
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 0 0 1
1 0 0 1
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 0 1
0 1 0 1

## Slide 178
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 0 0 1
1 0 0 1
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 0 1
0 1 0 1

## Slide 179
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 0 0 1
1 0 0 1
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 0 1
0 1 0 1

## Slide 180
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
Let's derive the output expressions

## Slide 181
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
Let's derive the output expressions.
We need to derive only these 3 unique ones.

## Slide 182
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0

## Slide 183
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
R1in = R3out = Done = y1 y2
R1out = R2in = y1 y2
R2out = R3in = y1 y2

## Slide 184
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 185
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
10
1
0
0
0
1
0
0
1
0
C
10
11
1
1
1
0
0
1
0
0
0
D
11
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y1 y2
y1 y2
y1 y2

## Slide 186
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in

## Slide 187
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
0
0
1
0
0
0
0
0
0
1
0
0
0
0
1
1
0
0
0
0
0
0

## Slide 188
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
0
0
1
0
0
0
0
0
0
1
0
0
0
0
1
1
0
0
0
0
0
0

## Slide 189
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
0
0
A
1
0
B
0
0
A
0
0
A
0
1
C
0
0
A
0
0
A
1
1
D
0
0
A
0
0
A
0
0
A

## Slide 190
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
A
B
A
A
C
A
A
D
A
A
A

## Slide 191
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
A
B
A
A
C
A
A
D
A
A
A
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=

## Slide 192
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
1
0
1
0
1
0
1
0
Clock
w
y
1
y
2
1
0
R2out
1
0
1
0
Done
, R3in
R1out
, R2in
R3out
, R1in
A
B
A
A
C
A
A
D
A
A
A
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=

## Slide 193: Encoding #2: A=00, B=01, C=11, D=10 (Also Uses Two Flip-Flops)

## Slide 194
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.18 from the textbook ]

## Slide 195
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.18 from the textbook ]
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 196
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.18 from the textbook ]
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 197
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.18 from the textbook ]

## Slide 198
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Let's derive the next-state expressions

## Slide 199
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 200
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
w
00
01
11
10
0
1
y
2
y
1
Y
2
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 201
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 1 0 0
1 1 0 0
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 1 0
0 1 1 0
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 202
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 1 0 0
1 1 0 0
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 1 0
0 1 1 0
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1

## Slide 203
y2 | y1 | w | Y2 | Y1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
w
00
01
11
10
0
1
y
2
y
1
Y
1
0 1 0 0
1 1 0 0
w
00
01
11
10
0
1
y
2
y
1
Y
2
0 1 1 0
0 1 1 0
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
Y
1
wy
2
y
1
y
2
+
=
Y
2
y
1
=

## Slide 204
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
Let's derive the output expressions

## Slide 205
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
Let's derive the output expressions
Once again, we only need to derive
these three unique ones.

## Slide 206
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 | 0 |  | 
0 | 1 | 0 |  | 
1 | 0 | 0 |  | 
1 | 1 | 1 |  | 
C
D
Note that C and D are swapped in the truth table
due to the new state encoding that was chosen.
A
B

## Slide 207
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
C
D
A
B

## Slide 208
R1out
R1in
R2out
R2in
R3out
R3in
Done
w = 0
w = 1
Present
Next state
state
Outputs
A
00
00
0
1
0
0
0
0
0
0
0
B
01
11
1
1
0
0
1
0
0
1
0
C
11
10
1
0
1
0
0
1
0
0
0
D
10
00
0
0
0
1
0
0
1
0
1
Y2Y1
Y2Y1
y2y1
y2 | y1 | R1out | R1in | R2out
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
C
D
A
B
R1out = R2in = y1 y2
R2out = R3in = y1 y2
R1in = R3out = Done = y1 y2

## Slide 209: Let's Complete the Circuit Diagram
R1out = R2in = y1 y2
R2out = R3in = y1 y2
R1in = R3out = Done = y1 y2
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
Y2 = y1
Y1 = w y2 + y1 y2

## Slide 210: Let's Complete the Circuit Diagram
R1out = R2in = y1 y2
R2out = R3in = y1 y2
R1in = R3out = Done = y1 y2
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
y
1
y
2
R2out
R3in
R1out
R2in
R3out
R1in
Done
Y2 = y1
Y1 = w y2 + y1 y2

## Slide 211: Let's Complete the Circuit Diagram
R1out = R2in = y1 y2
R2out = R3in = y1 y2
R1in = R3out = Done = y1 y2
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
y
1
y
2
R2out
R3in
R1out
R2in
R3out
R1in
Done
Y2 = y1
Y1 = w y2 + y1 y2

## Slide 212: Let's Complete the Circuit Diagram
R1out = R2in = y1 y2
R2out = R3in = y1 y2
R1in = R3out = Done = y1 y2
Y2 = y1
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
y
1
y
2
R2out
R3in
R1out
R2in
R3out
R1in
Done
Y1 = w y2 + y1 y2

## Slide 213: Encoding #3: A=0001, B=0010, C=0100, D=1000 (One-Hot Encoding – Uses Four Flip-Flops)

## Slide 214: One-Hot State Encoding
So far, we have been encoding states in a way that minimizes the number of flip-flops.
But sometimes we can decrease the complexity of our logic if we encode states more sparsely.

## Slide 215: Encoding for State A
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
1
0
0
0

## Slide 216: Encoding for State B
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
0
1
0
0

## Slide 217: Encoding for State C
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
0
0
1
0

## Slide 218: Encoding for State D
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
0
0
0
1

## Slide 219
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
Register Swap Controller

## Slide 220
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
Let’s use four flip-flops and the following
one-hot state encoding scheme:
A = 0001
B = 0010
C = 0100
D = 1000
Register Swap Controller

## Slide 221
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.21 from the textbook ]
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1

## Slide 222
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.21 from the textbook ]
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1

## Slide 223
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.21 from the textbook ]
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1

## Slide 224
Present
Next state
Outputs
state
A
A
B
0
0
0
0
0
0
0
B
C
C
0
0
1
0
0
1
0
C
D
D
1
0
0
1
0
0
0
D
A
A
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
State Table (same as before)
State-Assigned Table
[ Figure 6.12 & 6.21 from the textbook ]
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1

## Slide 225
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Let's Derive the Next-State Expressions

## Slide 226
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Let's Derive the Next-State Expressions
We need to do four 5-variable K-maps!
Y1(w, y4, y3, y2, y1)
Y2(w, y4, y3, y2, y1)
Y3(w, y4, y3, y2, y1)
Y4(w, y4, y3, y2, y1)

## Slide 227
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Y1(w, y4, y3, y2, y1) = wy1 + y4
Y2(w, y4, y3, y2, y1) = wy1
Y3(w, y4, y3, y2, y1) = y2
Y4(w, y4, y3, y2, y1) = y3
Let's Derive the Next-State Expressions
Or we can be smarter than that 

## Slide 228
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Y1(w, y4, y3, y2, y1) = wy1 + y4 (why?)
Y2(w, y4, y3, y2, y1) = wy1 (why?)
Y3(w, y4, y3, y2, y1) = y2 =1 only in B
Y4(w, y4, y3, y2, y1) = y3 =1 only in C
Let's Derive the Next-State Expressions
Or we can be smarter than that 

## Slide 229
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Let's Derive the Output Expressions

## Slide 230
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Let's Derive the Output Expressions
We need to do seven 4-variable K-maps!
R1out(y4, y3, y2, y1)
R1in (y4, y3, y2, y1)
R2out(y4, y3, y2, y1)
R2in (y4, y3, y2, y1)
R3out(y4, y3, y2, y1)
R3in (y4, y3, y2, y1)
Done(y4, y3, y2, y1)

## Slide 231
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Let's Derive the Output Expressions
Or we can be smarter than that by exploiting the one-hot encoded property
R1out(y4, y3, y2, y1) = y3 equal to 1 only in State C
R1in (y4, y3, y2, y1) = y4 equal to 1 only in State D
R2out(y4, y3, y2, y1) = y2 equal to 1 only in State B
R2in (y4, y3, y2, y1) = y3 equal to 1 only in State C
R3out(y4, y3, y2, y1) = y4 equal to 1 only in State D
R3in (y4, y3, y2, y1) = y2 equal to 1 only in State B
Done(y4, y3, y2, y1) = y4 equal to 1 only in State D

## Slide 232: Let's Complete the Circuit Diagram
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
w
Clock

## Slide 233: Let's Complete the Circuit Diagram
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
w
Clock

## Slide 234: Let's Complete the Circuit Diagram
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
R2out
R3in
R1out
R2in
R3out
R1in
Done
w
Clock

## Slide 235: Let's Complete the Circuit Diagram
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
R2out
R3in
R1out
R2in
R3out
R1in
Done

## Slide 236: Let's Complete the Circuit Diagram
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
R2out
R3in
R1out
R2in
R3out
R1in
Done

## Slide 237: Encoding #4: A=0001, B=0010, C=0100, D=1000 (same as before, but shows an alternative implementation with a 4-bit ring counter)

## Slide 238
D:
R
3
out
1
=
R
1
in
1
=
Done
1
=
,
,
w
0
=
w
1
=
C:
R
1
out
1
=
R
2
in
1
=
,
B:
R
2
out
1
=
R
3
in
1
=
,
w
1
=
A: No Transfer
w
0
=
w
1
=
w
0
=
w
1
=
Reset
w
0
=
[ Figure 6.11 from the textbook ]
Exploit the Structure of the FSM
The solution with the ring counter
works only when the traversal
through the states of the FSM
is one-directional and cannot
be interrupted by the
value of w once it has started.

## Slide 239
clear_n
2-bit up-counter
w
0
En
y
0
w
1
y
1
y
2
y
3
1
2-to-4 decoder
Q
1
Q
0
Clock
Q
1
Q
2
Q
3
Q
0
Start
Alternative version of a 4-bit ring counter
[ Figure 5.28b from the textbook ]

## Slide 240
clear_n
2-bit up-counter
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
Q
2
Q
3
Q
4
Q
1
Start
Switch to 1-based indexing of the outputs
Alternative version of a 4-bit ring counter
Switch to 1-based indexing of the outputs
(this is done to be consistent with the previous example)

## Slide 241
clear_n
2-bit up-counter
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
Q
2
Q
3
Q
4
Q
1
Start
Also, omit these labels
Alternative version of a 4-bit ring counter

## Slide 242
clear_n
2-bit up-counter
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
Start
Alternative version of a 4-bit ring counter
with enable

## Slide 243
[ Figure 4.14c from the textbook ]
En
2-to-4 Decoder with Enable Input

## Slide 244
En
2-to-4 Decoder with Enable Input
y1
y2
y3
y4
Switch to 1-based indexing of the outputs
(this is done to be consistent with the previous example)

## Slide 245
1
(always enabled in this example)
2-to-4 Decoder with Enable Input
y1
y2
y3
y4

## Slide 246
clear_n
2-bit up-counter
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
Start
Alternative version of a 4-bit ring counter
with synchronous clear

## Slide 247
2-Bit Synchronous Up-Counter
(with synchronous clear)
1
D
Q
Q
Clock
D
Q
Q
Clear_n
Q0
Q1
This counter can be cleared only on the positive clock edge.

## Slide 248: Let's Complete the Circuit Diagram
clear_n
2-bit up-counter
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
Start

## Slide 249: Let's Complete the Circuit Diagram
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock

## Slide 250: Let's Complete the Circuit Diagram
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
R2out
R3in
R1out
R2in
R3out
R1in
Done

## Slide 251: Let's Complete the Circuit Diagram
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
R2out
R3in
R1out
R2in
R3out
R1in
Done
w y1 + y4
This is the same as
in the previous example

## Slide 252: The Solution for Encoding #3
R1out = R2in = y3
R2out = R3in = y2
R1in = R3out = Done = y4
Y2 = w y1
Y3 = y2
Y4 = y3
Y1 = w y1 + y4
D
Q
Q
D
Q
Q
Y
2
Y
1
w
Clock
y
1
y
2
D
Q
Q
Y
3
y
3
D
Q
Q
Y
4
y
4
R2out
R3in
R1out
R2in
R3out
R1in
Done

## Slide 253
Present
Next State
State
Outputs
A
0
001
0001
0010
0
0
0
0
0
0
0
B
0
010
0100
0100
0
0
1
0
0
1
0
C
0
100
1000
1000
1
0
0
1
0
0
0
D
1
000
0001
0001
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
Y4Y3Y2Y1
Y4Y3Y2Y1
Y1(w, y4, y3, y2, y1) = wy1 + y4
Next-State Expression for Y1 (in Encoding #3)

## Slide 254
Present
Next State
State
Outputs
A
0
001
1
0
0
0
0
0
0
0
0
B
0
010
0
0
0
0
1
0
0
1
0
C
0
100
0
0
1
0
0
1
0
0
0
D
1
000
1
1
0
1
0
0
1
0
1
w = 0
w = 1
R1out
R1in
R2out
R2in
R3out
R3in
Done
y4y3y2y1
clear
clear
clear(w, y4, y3, y2, y1) = wy1 + y4
We get the same expression for clear
This needs to be negated, because the counter in the new solution uses clear_n.

## Slide 255
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
R2out
R3in
R1out
R2in
R3out
R1in
Done
w y1 + y4
This is the same as
in the previous example
We get the same expression for clear

## Slide 256
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
0
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 257
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
01
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 258
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
1
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 259
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
0
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 260
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
01
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 261
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
0
0
1
0
1
1
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 262
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
0
0
1
0
1
0
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 263
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 1
0 1 0 0
0
0
1
0
0
01
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
1
0
0

## Slide 264
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 1
0 1 0 0
0
0
0
1
0
1
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
1
0
0

## Slide 265
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 1
0 1 0 0
0
0
0
1
0
0
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
1
0
0

## Slide 266
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 0
0 0 1 0
0
0
0
1
0
01
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
1
0

## Slide 267
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 0
0 0 1 0
0
0
0
1
0
1
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
1
0

## Slide 268
How Does It Work?
0
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 0
0 0 1 0
0
0
0
1
0
0
1
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
1
0

## Slide 269
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 1
0 0 0 1
0
1
0
1
0
01
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
1

## Slide 270
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 1
0 0 0 1
0
1
0
1
0
1
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
1

## Slide 271
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
1 1
0 0 0 1
0
1
0
1
0
0
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
1

## Slide 272
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
01
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 273
How Does It Work?
1
clear_n
2-bit up-counter
w
w
0
En
y
1
w
1
y
2
y
3
y
4
1
2-to-4 decoder
Q
1
Q
0
Clock
0 0
1 0 0 0
1
0
0
1
1
1
0
R2out
R3in
R1out
R2in
R3out
R1in
Done
0
0
0

## Slide 274: Questions?

## Slide 275: THE END