## Slide 1: Fundamentals of Computer Networking
Ref. book: Anurag Kumar, D. Manjunath, Joy Kuri, Communication Networking: An Analytical Approach, Morgan Kaufmann, 2004.
Acknowledgement: this lecture is partially based on the slides of Dr. D. Manjunath
Hongwei Zhang
hongwei@iastate.edu, 515 294 2143
http://www.ece.iastate.edu/~hongwei
Notes: Chapter 2, 4, 5

## Slide 2: Outline
Functional elements of networking
Deterministic traffic models and network calculus
Stochastic analysis

## Slide 3: Outline
Functional elements of networking
Deterministic traffic models and network calculus
Stochastic analysis

## Slide 4: Functional Elements of Networking
Networking as resource sharing
Functional elements
  Multiplexing
  Switching
  Routing
  Network management
  Traffic controls and timescales

## Slide 5: Functional Elements of Networking
Networking as resource sharing
Functional elements
  Multiplexing
  Switching
  Routing
  Network management
  Traffic controls and timescales

## Slide 6: A layered view
A three-layered view of a communication network. “Networking” is concerned with resource sharing mechanisms that efficiently share the bit carrier infrastructure, and control the quality of service provided to the various applications using the network

## Slide 7: Computer OS Analogy
Networking is concerned with distributed algorithms for efficient sharing of bit carrier network resources. Very similar to OS of a computer helping applications to use and share hardware resources
Distributed
algorithms for
information transport
(e.g., X.25, Internet, CPN)
Applications
Computer
operating system
(e.g., Unix, Linux, Windows)
Network of
communication links
Hardware
(e.g., processor, memory,
disk drives, sound card)
(e.g., calculation, accounting,
database)
Distributed
information
applications
(e.g., www, e-commerce, teleconf, CPS)

## Slide 8: Functional Elements of Networking
Networking as resource sharing
Functional elements
  Multiplexing
  Switching
  Routing
  Network management
  Traffic controls and timescales

## Slide 9: Functional elements: consider a sample information flow
After source prepares the bits for transportation, “network” decides how to route flow over physical network
Infrastructure is shared by many such flows. Hence network has to decide how to multiplex this flow with other flows.
Flow may traverse multiple links. At junction of two links, switch flow elements to target link.
Need to monitor network behavior and collect status information; possibly handle situations for which network is not engineered. i.e., perform network management.

## Slide 10: Multiplexing
Sharing a communication link is multiplexing
  Systematically merging several data flows into one bit-pipe
Two types of multiplexing:
  Circuit multiplexing
  Packet multiplexing

## Slide 11: Circuit Multiplexing on a Link
Link capacity is statically partitioned into channels (possibly different capacities)
  Frequency, Time, Space and Code Division Multiplexing
Each conversation (flow) is allocated to a channel for the entire duration of call — the call holds the channel
Connection setup is required to allocate resources
  Fixed rate allocated at time of connection setup determines the peak rate at which the source can transmit data
  A call (request for resources) can be blocked if all the channels are busy

## Slide 12
Performance measures:
  Connection setup delay
  Call blocking probability
A typical design problem:
  What should be the link capacity for a given load and specified blocking probability?
The link may also have to handle different classes of flows, each with a different blocking probability requirement

## Slide 13: Circuit multiplexing: resource allocation model
Static partitioning of bandwidth in a circuit switched network

## Slide 14: Inefficiency of Circuit Multiplexing: Not Always?
Traditional Internet traffic sources and some cyber-physical network (CPN) sources generate data in bursts:
  Traditional Internet
    Voice: Talk and silence spurts
    Video: Scene changes
    Telnet: Typing behaviour
    Web browsing patterns: Think times between downloads
  Event detection CPN applications
Some CPN sources may generate periodic traffic, which is suitable for (virtual) circuit multiplexing

## Slide 15: Motivation for packet multiplexing
Bursty traffic sources
  Average rate is much lower than peak rate
  Capacity is wasted during “lean periods”

## Slide 16: Packet multiplexing
No partitioning of the bit pipe
  Apply entire bit rate to a source and hence, each packet gets the entire bit pipe for shorter periods of time
Packets need to contain header and trailer information to identify with a specific information flow (source, destination, application, etc.)

## Slide 17
Source peak rate can exceed link rate
  Packets may need to be queued;
  If buffer capacity is not sufficient, packets may be dropped and hence lost
Abstraction:
  Link is a server serving customers waiting in a queue
Performance measures:
  Packet delay
  Loss characteristics

## Slide 18: Multiplexing summary

## Slide 19: Switching: motivation
A six node network constructed in three ways—(a) A brute force way. (b) Every node is connected to a central switch that selectively establishes paths between nodes and (c) Hierarchical network with inter-switch links with possibly multiplexing on it.

## Slide 20: Switching
Information flow will traverse more than one link
  Switch is required at junction of two or more links
Switch selectively establishes and releases connections between communication links to allow sharing of these links among a number of flows (connections)
Switch moves information from link to link by demultiplexing on the inbound link and multiplexing on the selected outbound link
Notes: A switch is required with circuit multiplexing and centralised packet multiplexing

## Slide 21: Components of a packet switch

## Slide 22: Functions of a switch
Two categories, also called planes, of functions
  data plane
  control plane
Data plane functions
  Demultiplex the flow (e.g., packet or time slot) on the input link
  Switch the flow element onto the appropriate output link
  Multiplex the flows on the output link
  Fast timescale functions: performed per packet/frame
    Specialized hardware may be used for these high speed functions
Notes: Every packet or slot in a TDM frame needs to be processed

## Slide 23
Control plane functions
  Connection setup and resource allocation/reservation
    Achieved through source-network and switch-switch signaling
    Functions performed over connection (flow) arrival timescales
    General purpose processors can be used
  Routing and local conditions information dissemination
    Usually performed at timescales at which traffic characteristics change
Notes: Increasing interest in parallelization

## Slide 24: Design issues in a packet switch
Control and signaling functions include
  populating the routing table
  participating in distributed algorithms associated, for example, with routing
Datagram packet switches:
  every packet of a flow is treated independent of previous packets in the flow: queueing, address lookup, packet classification, etc.
Virtual circuit packet switches:
  Connection setup to allocate path and resources on links on path to the flow
  Packets are assigned link level labels, and switched based on labels
Performance measures
  switching delay in getting to the output queue
  packet loss rate
Notes: Input and output lines could be slotted or unslotted
  Correspondingly, packets lengths and interarrival time have discrete or continuous distributions
Packet lengths could be fixed or variable

## Slide 25: Routing
A route is an ordered sequence of links between a source and a destination
A network node, or a switch, performs the routing function along with multiplexing and switching;
Nonetheless, routing is a “network wide” function and the nodes collaborate in making routing decisions

## Slide 26: Design and Performance Issues
Routing protocols:
  What information to exchange, how often, how to exchange
  Source routing vs. hop-by-hop routing
  Hop-by-hop routing: distance vector vs. path-vector vs. link-state routing
Routing Algorithms:
  Objective functions for best effort routing and QoS routing

## Slide 27
Performance measures
  Connection blocking probability
    only relevant in circuit multiplexed networks
  Load imposed on the network
  Adaptation to changes in the network conditions
Notes: In datagram networks, connections are not set up. Hence no concept of connection blocking.
Virtual circuit based networks use packet multiplexing but set up a connection before data transfer begins to alert the switches of the creation of a flow

## Slide 28: Network management
Handle conditions for which the network is not engineered
  Different from ‘congestion control’ where the overload conditions are short lived
All operational networks define a management architecture to collect information and control the network resources
  Performance data are collected by managed network devices, these in turn are gathered by a network management station in the network that will analyze the data that has been collected

## Slide 29
The management architecture provides some control functions that can be performed on remote managed devices by management stations either in a programmed manner or through an operator
Security issues are also handled by a network management architecture

## Slide 30: Traffic controls and timescales
Network functions cover a wide variety of timescales
  a few microseconds to minutes to months and years
Four relative timescales:
  Packet timescale (packet transmission time; seconds or milliseconds/ microseconds)
  Session, call or flow timescale (typically minutes)
  Busy hour or traffic variation timescale (typically hours)
  Provisioning timescale (usually hours to days or weeks/months/years)

## Slide 31: Summary: Functional Elements of Networking
Networking as resource sharing
Functional elements
  Multiplexing
  Switching
  Routing
  Network management
  Traffic controls and timescales

## Slide 32: Outline
Functional elements of networking
Deterministic traffic models and network calculus
Stochastic analysis

## Slide 33: Deterministic traffic models & network calculus
Events and processes: universal concepts
Deterministic traffic models and network calculus
Connection setup: RSVP approach

## Slide 34: Deterministic traffic models & network calculus
Events and processes: universal concepts
Deterministic traffic models and network calculus
Connection setup: RSVP approach

## Slide 35: Introduction

## Slide 37: Model and notation
Assume output queueing
time

## Slide 38
Also called non-idling scheduler

## Slide 40
A packet arrival at t is included in the cumulative arrivals counted by A(t)

## Slide 41: Some simple analysis
For work-conserving/non-idling schedulers

## Slide 43: Finite buffer

## Slide 44: Finite buffer: conservation law

## Slide 45: Deterministic traffic models & network calculus
Events and processes: universal concepts
Deterministic traffic models and network calculus
Connection setup: RSVP approach

## Slide 46: Reich’s Equation
Reich’s Equation
The supremum is achieved when s = v, i.e., the last time before t when buffer was empty

## Slide 47: Network calculus
A view of network calculus: Work with sample paths of a random process.
  Networks see a sample path of a random process, e.g., X(t, )
  Network calculus is a sample path analysis in which the sample path satisfies certain properties.
  It can be assumed that these properties are satisfied by all sample paths. Thus network calculus or the deterministic analysis is a worst-case analysis.
An example objective is to obtain X(t) from A(t) and C of a work conserving scheduler
  We are also interested in other processes such as D(t) and other performance parameters such as worst-case latency

## Slide 48: Derivation of Reich’s equation

## Slide 51
Combine equations (-1) and (0), we get Reich’s Equation
The supremum is achieved when s = v, i.e., the last time before t when buffer was empty

## Slide 52: An equation for the departure process D(t)

## Slide 53: Interpretation of Reich’s Equation

## Slide 54: Alternative/direct derivation of D(t) equation

## Slide 55: Direct derivation of D(t) (contd.)

## Slide 56: A convolution operation: *
nondecreasing

## Slide 58: Remarks

## Slide 59: Remarks (contd.)

## Slide 60: Illustration
slope
r
A
(
t
)
B
(
t
)
s
t
slope
C
t
slope
r

t
slope
C
B
(
t
)
(
B
*
A
)(
t
)
B()+A(t-)

## Slide 61: Compare * with standard convolution

## Slide 63: An example

## Slide 65: Properties of *

## Slide 66: Service curves
the

## Slide 68: Example network elements: packetizer
Notes: (t)

## Slide 69: Example elements: constant rate server

## Slide 71: Network elements: packetizer + constant rate server

## Slide 72: Network elements in tandem

## Slide 73: Latency rate servers in tandem

## Slide 75: Delay in a service element

## Slide 77: Stream traffic, QoS, envelop, regulator

## Slide 78: Envelope (contd.)

## Slide 80: Regulator

## Slide 81: Regulator example: leaky bucket

## Slide 82

Token arrival process

## Slide 83
E(t) = 0 for t < 0

## Slide 87: Sequence of regulators

## Slide 88: An example

## Slide 89: Network performance and design
With envelop E(t)

## Slide 91


## Slide 93
Otherwise, Cmin is not the minimum capacity (see book by Anurag Kumar et al.)

## Slide 95: Theory applied in practice: an example

## Slide 97: Deterministic traffic models & network calculus
Events and processes: universal concepts
Deterministic traffic models and network calculus
Connection setup: RSVP approach

## Slide 98: RSVP and IntServ

## Slide 99
G
k
=
`
G
k
-
1
G
1
G
0
c
C
LAN
K
K
-
1
c
c
1
0
WAN
- LAN router
max packet
length
L
(, , R)

transmission rate at each link i is Gi
Notes: Transmission rate at each link i is \tau_i

## Slide 102: How to compute c in RSVP?

## Slide 103: Outline
Functional elements of networking
Deterministic traffic models and network calculus
Stochastic analysis
Notes: To check: “A basic stochastic network calculus”, 2006

## Slide 104: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 105: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 106: Recap of deterministic analysis

## Slide 107: Review: Law of large numbers & central limit theorem

## Slide 108: Deterministic analysis can yield loose bounds: an motivating example

## Slide 114: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 115: Stochastic traffic model

## Slide 116: Model for a single stream source

## Slide 118: Superposition of sources

## Slide 119
# of active sources

## Slide 122: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 123: Some (additional) notation

## Slide 124: Performance measures

## Slide 127: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 128: Little’s Theorem

## Slide 130: Derivation

## Slide 136: Discussion

## Slide 137: Invariance of mean system time

## Slide 139: Generalization of Little’s Theorem: Brumelle’s Theorem

## Slide 141: Recall: queueing system notation

## Slide 142: Mean queue length in an M/G/1 queue

## Slide 144: M/G/1 queue: remarks

## Slide 145: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 146: Multiplexer analysis

## Slide 147: Recall: Birkhoff’s Ergodic Theorem

## Slide 148: Analysis with marginal buffering (i.e., bufferless)

## Slide 151: Marginal buffering: example

## Slide 152: Recall: inequalities

## Slide 154
by

## Slide 155
Special case: let y = 0

## Slide 156: Recall: limit theorems

## Slide 157: Link design: taking advantage of statistical multiplexing

## Slide 159: Analysis using central limit theorem

## Slide 161: Analysis using Chernoff bound

## Slide 164
From (ii) and (iii): for  > E(X1), l() is nondecreasing

## Slide 165: Example 5.4: the two-state Markov source

## Slide 169: Cramer’s theorem

## Slide 171: Multiplexing gain, link engineering, and admission control

## Slide 172
But, given the same resource provisioning, N would be larger in packet switching.

## Slide 174: Analysis with arbitrary buffering

## Slide 175: Stationary queue length: continuous time

## Slide 179: Stationary queue length: discrete time

## Slide 180: Queue length analysis using Chernoff’s Bound: Effective bandwidth

## Slide 181
Then
, for some constant K

## Slide 184
)

## Slide 186: Example

## Slide 188: Some properties of e()

## Slide 191: Calculating () for a Discrete Time Markov Source

## Slide 196: Stationary Buffer Distribution Asymptotics: A Review

## Slide 197: Remark
A capacity of C = ()/  is not only sufficient but also necessary for achieving the desired QoS objective 
  See analysis on PP. 227 – 230 of Anurag book for the analysis

## Slide 198: An Approximation to the Stationary Buffer Distribution

## Slide 201: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 202
For large x,

## Slide 204
(only) for small x
Notes: n2, n1: # of sources

## Slide 206: Guerin, Ahmadi, Nagshineh (GAN) approach

## Slide 208
Xmax affects whether C0 or CEBW is chosen

## Slide 209: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 210: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 211: Stochastic analysis with shaped traffic
Leaky bucket (LB) shaped traffic
Challenge for stochastic analysis and traffic engineering with LB parameters alone is that they only specify the worst case behavior and do not uniquely specify a statistical characterization of the source
Solution
  To analyze by assuming, for each source, a model compatible with the LB parameters but one that leads to the worst performance
  Thus, the problem reduces to one of determining the worst case stochastic models for a set of independent LB shaped sources

## Slide 212: The case of marginal buffering
For m statistically independent sources with LB parameters (i, i, Ri), 1  i  m
For maximizing packet loss rate,
  Each source be an on-off source (taking values Ri and 0) with mean rate ri
    Packet loss rate is maximized when ri = I
For maximizing fraction of packets lost,
  Each source be an on-off source (taking values Ri and 0) with mean rate ri
    Nonetheless, packet loss rate is not maximized in general when ri = i

## Slide 213: The case of arbitrary buffering
LB parameters: (, , R)
  Extremal on-off source: switching between R and 0, with maximum possible burst length /(R-)
In general, extremal on-off source does not give the worst performance
Two-level source can yield worse performance
  Intuition: by being active longer, the source can sustain congestion longer, thus causing loss for other sources in the multiplexer
T
1
T
1
T
1
T
2
T
2
r
R

## Slide 214: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 215: Challenges of multihop networks
Need to characterize the departure process of each flow from each hop
Flows become dependent within the network, and dependence is very difficult to characterize
A network may carry both elastic and stream traffic, and the different flows interact whose impact is difficult to account for in design
  E.g., resources are used for stream traffic in the absence of elastic traffic bursts

## Slide 216: Status of the art
End-to-end stochastic analysis of multihop packet networks has not yet yielded a complete solution
  With solutions to limited situation only, e.g., the effective envelope approach (see Section 5.10 of R0)
  Definition: for a given>0, a function E(t) is an -effective envelope for A(t) if, for every t and 0, Pr(A(t+)-A(t)> E())  
One (approximate) approach: splitting end-to-end QoS objectives (e.g., latency) into per-hop objectives
  Existence of optimal splitting

## Slide 217: Stochastic Analysis
Loose bounds by deterministic calculus
Stochastic traffic models
Performance measures
Little’s Theorem, Brumelle’s Theorem and applications
Multiplexer analysis with stationary and ergodic traffic
Effective bandwidth approach to admission control
Stochastic analysis with shaped traffic
Multihop networks
Long-range-dependent traffic

## Slide 218: Long-range-dependent traffic

## Slide 222: Additional readings
Admission control and QoS
  E. W. Knightly and N. B. Shroff, “Admission control for statistical QoS: Theory and practice”, IEEE Network Magazine, pp. 20-29, March/April 1999
Long range dependent (LRD) traffic
  W. E. Leland et al., “On the self-similar nature of Ethernet traffic”, IEEE/ACM Transactions on Networking, 2(1):1-15, Feb. 1994
  W. Willinger et al., “Self-similarity in high-speed packet traffic: analysis and modeling of Ethernet traffic measurements”, Statistical Science, 10(1):67-85, 1995

## Slide 223: Summary
Functional elements of networking
  Networking as resource sharing
  Functional elements: multiplexing, switching, routing, network management
Deterministic traffic models and network calculus
  (min, +) calculus: convolution operator
    Arrival process, service process, departure process
    Delay-rate servers, tandem networks
    Max. delay analysis for FIFO servers
  Traffic regulator: leaky bucket
  Capacity planning
Stochastic analysis
  Little’s Theorem
  Probability inequalities
  Effective bandwidth
  Admission control