## Slide 1: Cyber-Physical Scheduling for Predictable Reliability of Inter-Vehicle Communications
Chuan Li, Hongwei Zhang, Jayanthi Rao, Le Yi Wang, George Yin

## Slide 2
solo vehicle
connected & automated vehicle
Notes: Other paradigm shift in transportation engineering exist, e.g., in infrastructure

## Slide 3: Connected & Automated Vehicles
R. Johri, J. Rao, H. Yu, H. Zhang, “A Multi-Scale Spatiotemporal Perspective of Connected and Automated Vehicles: Applications and Networking”, IEEE Intelligent Transportation Systems, 8(2):65-73, 2016
Active Safety
Fuel Economy & Emission Control
Networked Vehicle Automation
Infotainment
Small Spatiotemporal Scale
Sensing and Control
Notes: Pre-crash sensing (PCS)
Emergency brake lights (EBL)
Collaborative collision warning (CCW)
Left turn assistant (LTA)
Lane change warning (LCW)
Traffic signal violation warning (TSV)
Stop sign violation warning (SSV)
Curve speed warning (CSW)
Stop-start
Platoon
Preview-based fuel economy optimization (PFO)
Low emission zone (LEZ)
Fuel-economy-oriented trip planning (FEP)
Adaptive vehicle tuning (AVT)
Collaborative failure-mode-effect-management (CFEM)
Traffic jam assist (TJA)
Supercruise with opportunistic lane change (SCLC)
Automated valet/street parking (AP)
Extended surrounding sensing (ESS)
Geographic proximity applications (GPA)
Real-time cloud services to vehicle (RTCS)
Remote vehicle command (RVC)
Remote vehicle status (RVS)
Crowd-sourced sensing (CSS)
Delay-insensitive downloads (DID)
Cloud-based diagnostics/prognostics/analytics (CDPA)
Multi-Scale Spatiotemporal Perspective

## Slide 4: Active Safety
Eliminate up to 90% accidents
Save 1.3 million lives and avoid 45 million injuries per year
Eliminate 23% congestion
Notes: ===
Crash Avoidance Metrics Partnership (CAMP) industry consortium
  Ford, GM, Mercedes–Benz, Toyota, Honda, Nissan, Hyundai/Kia, Volkswagen
USDOT initiatives
  Safety Pilot Model Deployment in Ann Arbor
    2,800+ vehicles & multiple road side equipment
  Planned large scale pilot deployments across USA
  Michigan testbeds
Safety Pilot Model Deployment in Ann Arbor
  2,800+ vehicles & multiple road side equipment
Michigan testbed(s)
  79+ roadside equipment sites
    12 freeway, 42 signalized intersections
    45 square miles of coverage
    75 center-line miles of roadway
      Interstate and divided highway: ~32 center-line miles
      Signalized intersections: ~43 center-line miles
  10 vehicles with on-board equipment
    Electronic equipment cost over 60% of overall vehicle cost
Smart transportation
  DSRC/IEEE802.11p, WAVE

## Slide 5: Vehicle Platooning
Simple platooning strategy saves up to 16% fuel consumption!
Notes: Having vehicles coordinate their driving behavior based on in-situ road and traffic conditions can also significantly enhance fuel efficiency and reduce emissions. For instance, by having vehicles form platoons and coordinate their acceleration, deceleration, and inter-vehicle distance, we can easily save up to 16% fuel consumption based on existing road tests. In transportation, every 1% fuel savings is actually significant!
===
Grand Cooperative Driving Challenge, Netherlands (2011)
Safe Road Trains for the Environment (SARTRE), Sweden (2009-2012)
Field trials showed 8%-16% reduction in fuel consumption from semi-automated ‘road trains’ (SARTRE, Energy ITS)
SARTRE project:
Observations from SARTRE project: 10-20% fuel economy savings
Up to 90 miles per hour with inter-vehicle distance no more than four meters

## Slide 6
Wireless as a Basic Enabler!
Notes: Other paradigm shift in transportation engineering exist, e.g., in infrastructure

## Slide 7: IEEE 802.11p
Foundation for today’s DSRC implementation
Inherit basic principles of WiFi
  Carrier Sensing Multiple Access (CSMA)
  OFDM
WiFi has never been designed for safety-critical control 

## Slide 8: Control of co-channel interference: a basic challenge in wireless communication
Open problem for over 40 years
  ALOHA protocol considered interference from concurrent transmitters (1970)
  Hidden terminal issue first identified by Leonard Kleinrock (1975)
Lack of field-deployable approaches to predictable interference control
Notes: N. Abramson (1970). "The ALOHA System - Another Alternative for Computer Communications" (PDF). Proc. 1970 Fall Joint Computer Conference. AFIPS Press
ALOHAnet, also known as the ALOHA System,[1][2] or simply ALOHA, was a pioneering computer networking system developed at the University of Hawaii. ALOHAnet became operational in June, 1971, providing the first public demonstration of a wireless packet data network.[3][4]
The ALOHAnet used a new method of medium access (ALOHA random access) and experimental ultra high frequency (UHF) for its operation, since frequency assignments for communications to and from a computer were not available for commercial applications in the 1970s. But even before such frequencies were assigned there were two other media available for the application of an ALOHA channel – cables and satellites. In the 1970s ALOHA random access was employed in the widely used Ethernet cable based network[5] and then in the Marisat (now Inmarsat) satellite network.[6]
In the early 1980s frequencies for mobile networks became available, and in 1985 frequencies suitable for what became known as Wi-Fi were allocated in the US. These regulatory developments made it possible to use the ALOHA random access techniques in both Wi-Fi and in mobile telephone networks.
ALOHA channels were used in a limited way in the 1980s in 1G mobile phones for signaling and control purposes.[7] In the late 1980s, the European standardisation group GSM who worked on the Pan-European Digital mobile communication system GSM greatly expanded the use of ALOHA channels for access to radio channels in mobile telephony. In addition SMS message texting was implemented in 2G mobile phones. In the early 2000s additional ALOHA channels were added to 2.5G and 3G mobile phones with the widespread introduction of GPRS, using a slotted ALOHA random access channel combined with a version of the Reservation ALOHA scheme first analyzed by a group at BBN

## Slide 9: Wireless Interference Model: A Basis for Interference-Oriented Scheduling
Predicts whether a set of concurrent transmissions may interfere with one another
Two commonly-used interference models
  Protocol model
  Physical model
Notes: One basic reason for the low performance of existing protocols is due the lack of a wireless interference model that can serve as a basis for designing distributed protocols for predictable interference model.

## Slide 10: Physical-Ratio-K (PRK) Interference Model
Suitable for designing distributed protocols:
  Both signal strength and link reliability are locally measurable
  K is locally controllable
Generally applicable
  Only assumption: non-increasing “BER vs. SINR” function
  Given a transmission from S to R, a concurrent transmitter C is regarded as not interfering with the reception at R iff.
S
R
C
signal strength from S to R
function of required PDR TS,R
Interference power from C to R
H. Zhang, X. Che, X. Liu, X. Ju, “Adaptive Instantiation of the Protocol Interference Model in Wireless Networked Sensing and Control”, ACM Transactions on Sensor Networks, 10(2), 2014
Notes: Signal-strength-based definition can deal with wireless channel irregularity
  ===
  K can be searched via local, control-theoretic approach
  Based on the result above, we propose the Physical-Raio-K model.
  Given a transmission from the sender to the receiver, the PRK model define a (signal-strength-based exclusive) region; the boundary of this exclusive region is such that an interferer will only one of k-th of received signal strength between the sender and the receiver. For any nodes outside this region, PRK model ignores its interference. For example, the interference from Node C’s transmission will be ingored in PRK model.
  In the presence of dynamic interference, The value of K can change promptly so that the link quality is always above the threshold T_pdr.
  Therefore, PRK model can facilitate the distributed protocol design while ensure the relibility.
  As may notice that there is no closed-form formular for K. But if you look at the model carefully, all parameters, received signal strength and the reliability, are locally measurable. The K can be searched via local, control-theoretic approach.
  We define the PRK model based on signal strength instead of geographic distance based on two reason: 1). The signal strength is locally measurable; 2). It can deal with wireless channel irregularity, (such as different transmission power or non-uniform signal attenuation, as we shown here).
  As link quality is online, locally meaured metric. It can be obtained through real-time, data-driven, passive measurement.
  It is desirable to use the minimum k that ensure a certain link quality, since it tends to avoid throughput loss cased by using any unnecessarily large K.
  where P(ni, nr) and P(ns, nr) is the strength of signals reaching nr from ni and ns respectively, and
  Benefits of PRK model:
  1. K(ns, nr, Tpdr) is chosen such that the probability of nr successfully receiving packets from ns is at least Tpdr in the presence of interference from all concurrent transmitters

## Slide 11: Predictable Link Reliability in Distributed PRK-based Scheduling (PRKS)
Predictable link PDR through localized PRKS model adaptation
Concurrency and spatial reuse statistically equal or close to that in state-of-the-art centralized scheduling

## Slide 12: Convergence of distributed controllers
Median: 26 control steps
90-percentile: 43 control steps
Settling time
PDR time series of a typical link:
PDR req. = 90%
Network-wide convergence
Notes: From mean PDR guarantee to instantaneous PDR guarantee:
Extra SINR margin as a protection
Integrate with other techniques …

## Slide 13: Heterogeneous Settings
Heterogeneous link transmission power
in a network
Heterogeneous PDR requirements in a network
Predictable link PDR in the presence heterogeneous application requirements and network configurations

## Slide 14: Temporally-Varying PDR Requirements: 70%80%90%95%90%80%70%
PDR of a typical link
Settling time
Notes: Converges fast (or faster than bootup), with a median settling time around 18 control steps.

## Slide 15: Comparison with Existing Protocols: PDR
PDR requirement = 90%
Notes: Larger networks: even lower PDR in other protocols (except SCREAM), but predictably high pdr in PRKS

## Slide 16: Current Practice (1): Improve Reliability by Retransmission
Significantly longer delay in existing protocols due to retransmission

## Slide 17: Current Practice (2): Improve Reliability by Reducing Traffic Load
Significantly lower throughput in existing protocols due to low utilization of channel capacity

## Slide 18
PRK-based scheduling in vehicular networking?

## Slide 19: Vehicular Networks: Challenges of Vehicle Mobility & Broadcast
Fast-varying interference relations between vehicles
  Highly-dynamic network topology
  Highly-dynamic wireless channels
Challenges
  Identification of interference relations
  Signaling of interference relations
Single-hop broadcast as a fundamental vehicular networking primitive
  Lack of simultaneous receiver feedback
  Correlated receiver exclusion regions
In collaboration with Ford Research

## Slide 20: Challenge of Interference Relation Signaling
PRKS: maintain signal maps on channel gains among potentially- interfering vehicles
Signaling overhead
            N: # of interfering vehicles
            t0: information update interval
Costly or even infeasible to maintain accurate signal maps
Notes: V2V communication standard IEEE 802.11p can only support a transmission rate of 6Mbps - 27Mbps

## Slide 21: gPRK Model:Geometric Approximation of PRK Model
Vehicle location information readily available through GPS, SLAM etc
gPRK interference model
gPRK vs. PRK model: distance vs. signal power attenuation
  Stronger interference from closer-by vehicles
  Additive interference
  Given a transmission from S to R, a concurrent transmitter C is regarded as not interfering with the reception at R iff.
S
R
C
distance from S to R
function of required PDR TS,R
distance from
C to R

## Slide 22: Signaling overhead in gPRK-based Scheduling
Factor of overhead reduction as compared with PRK-based scheduling:
  Orders of magnitude reduction

## Slide 23: gPRK Model: Efficiency & PRK Similarity
Signaling overhead:
  Orders of magnitude reduction as compared with PRK-based scheduling (i.e., )
(Broadcast) exclusion region similar to PRK-based scheduling

## Slide 24: gPRK Model Instantiation
Distributed regulation control
gPRK model controller:
required PDR
actual PDR
desired receiver-side interference change
interference beyond
exclusion region

## Slide 25
Use of gPRK model in highly-dynamic vehicular networks?
Effectiveness of gPRK-based scheduling?

## Slide 26: Cyber-Physical Structures of Vehicle Traffic Flow
Physical structures
  Macroscopic vehicle clustering effect
  Microscopic vehicle dynamics
Cyber structures
  Spatial interference correlation
  Temporal interference correlation
In collaboration with Ford Research
Notes: Spatial correlation: links of distance no more than 30 meters
Temporal correlation: time lag of two seconds

## Slide 27: Addressing Vehicle Mobility (1): gPRK Model Instantiation & transient links
Relatively-stable vehicle clustering effect in a traffic flow
  Facilitate control-theoretic gPRK model instantiation
gPRK model instantiation for transient links
  Spatial interference correlation
  Temporal interference correlation
Notes: gPRK model initialization leveraging spatial interference correlation

## Slide 28: Addressing Vehicle Mobility (2): Effective Use of gPRK Model
Vehicle location prediction in between location updates
  E.g., up to 22.22 meters inter-vehicle distance change at speed of 80km/h and update interval of 0.5 second
Well-understood microscopic vehicle dynamics
  E.g., Intelligent Driver Model (IDM) for acceleration/ deceleration
Unscented Kalman Filter (UKF) for nonlinear systems

## Slide 29: Ensuring Reliable Inter-Vehicle Broadcast
Broadcast exclusion region (ER) as union of receiver ERs
Correlation in ER adaptation across receivers

## Slide 30: Cyber-Physical Scheduling (CPS) for Inter-Vehicle Communication
Multi-scale structure in adaptation
Leveraging cyber-physical structures of vehicular networks in identification and signaling of interference relations

## Slide 31: Multi-Dimensional Simulation of Vehicular Networks

## Slide 32: Experimental Study of CPS Behavior
Midtown Detroit
I-75 in
Southeast Michigan

## Slide 33: CPS for Predictable Inter-Vehicle Communication
Predictable reliability
Significantly lower delay, higher throughput

## Slide 34: Cyber-Physical Scheduling (CPS)
Leverage cyber-physical structures of vehicle traffic flows
  Physical structures
    gPRK interference model: distance vs. signal power attenuation
    Microscopic vehicle dynamics
    Macroscopic vehicle clustering effect
  Cyber structures: spatiotemporal interference correlation
PRK-based scheduling (and variants) as a general framework for interference-oriented scheduling
  Static & mobile networks
In collaboration with Ford Research
Hongwei Zhang
hongwei@iastate.edu
http://www.ece.iastate.edu/~hongwei