## Slide 1: When In-Network Processing Meets Time: Complexity and Effects of Joint Optimization in Wireless Sensor Networks
Department of Computer Science, Wayne State University
Department of Computer Science, Indiana University
Applied Research and Technology Center, Motorola

## Slide 2: Introduction
Wireless Sensor Networks
  Highly resource-constrained
In-Network Processing
  Reduce traffic flow → resource efficient
  End-to-end QoS are usually not considered
Mission-Critical Real-Time CPS:
  Close-loop control
  More emphasis on end-to-end QoS, especially latency and reliability

## Slide 3: Introduction
Packet packing
  Application independent INP
  Simple yet useful INP in practice
    UWB intra-vehicle control
    IETF 6LowPAN: high header overhead
Our focus:
  Understanding problem complexity
  Designing simple distributed online algorithm
  Understanding systems benefits

## Slide 4: Outline
System Model and Problem Formulation
Complexity Analysis
A Utility Based Online Algorithm
Performance Evaluation
Conclusion

## Slide 5: System Model and Problem Formulation
System Model
  A directed collection tree T = (V,E)
  Edge (vi, vj) ∈ E with weight ETXvi, vj (l)
  A set of information elements X = {x}
  Each element x: (vx, lx, rx, dx)
Problem (P):
  Schedule the transmission of X to R
  Minimize the total number of transmissions
  Satisfy the latency constraints of each x ∈ X

## Slide 6: Outline
System Model and Problem Formulation
Complexity Analysis
A Utility Based Online Algorithm
Performance Evaluation
Conclusion

## Slide 7: Complexity Analysis
Problem P0
  Elements are of equal length
  Each node has at most one element
Problem P1
  Elements are of equal length
  Each node generates elements periodically
Problem P2
  Elements are of equal length
  Arbitrary data generating pattern

## Slide 8: Complexity Analysis
P0, P1, P2, P | K ≥ 3 | K = 2 | 
 |  | re-aggregation is not prohibited | re-aggregation is prohibited
Complexity | strong NP-hard | strong NP-hard | O(N3)
NP-hard to achieve approximation ratio |  |  | 
  K = Maximal packet length N = |X|
  Re-aggregation: a packed packet can be dispatched for further packing.

## Slide 9: Complexity Analysis
K ≥ 3, P0 is NP-hard in tree structures -- Reduction from SAT
Given a SAT instance with n clauses and m variables
For each clause j
For m variables

## Slide 10
For each variable occurred in clause j
Auxiliary elements related to the red ones

## Slide 11: Complexity Analysis
When K ≥ 3 and T is a tree, regardless of re-aggregation
  P0 is NP-hard →P1 is NP-hard → P2 is NP-hard → P is NP-hard
When K ≥ 3, and T is a chain, regardless of re-aggregation
  The reduction from SAT still holds*
When K = 2 and re-aggregation is not prohibited
  The reduction from SAT still holds in both tree and chain structures
When K = 2 and re-aggregation is prohibited
  Problem P is equivalent to the maximum weighted matching problem in an interval graph.
  Solvable in O(N3) by Edmonds’ Algorithm
  * This solves an open problem in batch processing

## Slide 12: Outline
System Model and Problem Formulation
Complexity Analysis
A Utility Based Online Algorithm
Performance Evaluation
Conclusion

## Slide 13: A Utility Based Online Algorithm
When a node receives a packet pkt with length sf
  Decisions: to hold or to transmit immediately
  Utility of action: Reduced Amortized Cost
  One-hop locality

## Slide 14: A Utility Based Online Algorithm
Utility of holding a packet:
Utility of transmitting a packet:
Cost without packing
Cost with packing
Every packet received by parent can get fully packed via pkt

## Slide 15: A Utility Based Online Algorithm
Decision Rule
  The packet should be immediately transmitted if Up > Ul
  The packet should be held if Up ≤ Ul
Competitive Ratio
  Problem P’
    T is a complete tree
    Leaf nodes generate elements at a common rate
  Theorem: For problem P′, tPack is
-competitive, where K is the maximum number of information elements that can be packed into a single packet, V>1 is the set of nodes that are at least two hops away from the sink R.
  Example: When ETX is the same for each link, tPack is 2-comptetive

## Slide 16: Outline
System Model and Problem Formulation
Complexity Analysis
A Utility Based Online Algorithm
Performance Evaluation
Conclusion

## Slide 17: Performance Evaluation
Experiment Setting Up
  Testbed: NetEye, a 130-sensor testbed
  Topology: 120 nodes, half are source nodes
  Protocols compared: noPacking, simplePacking, tPack
  Traffic patterns: 6 second periodic traffic and event traffic
  Metrics:
    packing ratio
    delivery reliability
    delivery cost
    latency jitter

## Slide 18: Packing Ratio

## Slide 19: Delivery Reliability

## Slide 20: Delivery Cost

## Slide 21: Latency Jitter

## Slide 22: Outline
System Model and Problem Formulation
Complexity Analysis
A Utility Based Online Algorithm
Performance Evaluation
Conclusion

## Slide 23: Conclusion and Future Work
Conclusion
  Impact of INP constraints on problem complexity
  Feasibility of a simple, distributed online algorithm
  Systems benefits in terms of efficiency and predictable latency
Future Work
  Complete competitive analysis on the utility based algorithm
  Joint optimization of other INP and QoS constraints in WCPS